## Slide 1: Way forward on the SSB time index acquisition time
Huawei, HiSilicon, Ericsson, Intel, MediaTek, [Samsung], [Qualcomm], …
3GPP TSG-RAN WG4 Meeting #85 Reno, USA, 27th November – 1st December 2017
R4-1714251

## Slide 2: Background (1/2)
After RAN1 #90bis, redesign of SS/PBCH has been agreed and no further redesign is allowed. RAN1 #91 also sees update for SS/PBCH design.
Updated design of SS/PBCH can be illustrated as follows:

## Slide 3: Background (2/2)
It is considered that, in each SMTC configured for a certain UE operations of SS/PBCH acquisition, only 1 SSB can be seen by the UE for the worst case due to beam switching.
The SS/PBCH index acquisition time will be derived based on the following assumption:
    PBCH-DMRS sequence acquisition time for FR1
    PBCH decoding (NR-MIB acquisition) time for FR2
    Side condition: SNR = [-6]dB and [99]% decoding success rate

## Slide 4: Observation
RAN4 observed the need of further study on NR SS/PBCH time index acquisition time TSSB_time_index based on the link level simulations because of the further update of SSB design after RAN1#91
  For FR1, only DMRS acquisition is needed for SSB time index acquisition. Simulation results show that [TBD] attempt are needed at -6dB.
  For FR2, both PBCH-DMRS acquisition and PBCH NR-MIB decoding are needed for SSB time index acquisition. Simulation results show that [TBD] attempts are needed at -6dB.
  PBCH Soft-combining is not mandatory and shall be up to implementation.

## Slide 5: Simulation result summary (For information)
SSBs needed for successful reception | PBCH decoding (attempts) | PBCH-DMRS acquisition (attempts)
 | for FR2 | for FR1
Huawei | 2 | 1~2
Ericsson | 3~4 | 2~3
Qualcomm | 2 | 1
Intel | 2 | 2
Mediatek | 2~25 | 2~3
Nokia | 6~9 | 
Number of attempts

## Slide 6: Way forward
Companies are encouraged to provide further link simulation results based on the simulation assumption R4-1713437 in order to derive the required attempts to acquire SSB index.