## Slide 1: WF on Clarification of UE Measurement Mode
MediaTek
R4-1801506
Document for: Approval
3GPP TSG-RAN WG4 meeting #86
Athens, Greece, February 26th – March 2nd, 2018
Agenda item: 7.9.3.1

## Slide 2: Background
In RAN4 AH1801 meeting, WF R4-1801087 was approved to further study the remaining issues in the following scenarios for UE capable to per-FR-gap:
  Scenario 1: In NSA, for UE capable to per-FR gap without FR2 serving cells but with both FR1/LTE and FR2 measurement objects, there is an ambiguity on which mode to follow if network configures only one measurement gap pattern ID within #0 to #11.
    FFS the effective MGRP X ms to be adopted for UE to meet the corresponding toward FR2 measurement objects
  Scenario 2: For UE capable to per-FR gap with both FR1 and FR2 serving cells and with both FR1/LTE and FR2 measurement objects, there is an ambiguity on which mode to follow if network configures only one measurement gap.
    FFS the UE behavior

## Slide 3: Scenario 1
X = 20, which is shared with the requirement for UE capable for gap-less measurement.

## Slide 4: Scenario 2
If UE claimed gap-less measurement capability through needforGaps on all serving cells in a frequency range without measurement gap configured, then UE meets the inter-frequency measurement requirements toward those measurement objects in that frequency range according to the effective MGRP 20ms.
If UE did not claimed gap-less measurement capability through needforGaps on all serving cells in a frequency range, UE expects measurement gap for that frequency range will always be configured by network.