## Slide 1: Way forward on eV2X RRM requirements
Huawei, HiSilicon,
3GPP TSG-RAN WG4 Meeting #86 R4-1802628
Athens, Greece, Feb 26th– Mar 2nd, 2018
Agenda Item: 6.17.3

## Slide 2: Agreements on V2X Carrier Aggregation
Maximum Receive Timing Difference (MRTD) and Maximum Transmission Timing Difference (MTTD)
  No need to introduce MRTD or MTTD requirements for both V2X intra-band contiguous CA and V2X non-contiguous CA
V2X Synchronization Reference Source selection/reselection requirements for V2X sidelink CA will be introduced in new section
  The legacy measurement requirements on a detectable intra-frequency SyncRef UE are applied only for the component carrier(s) configured as the synchronization carrier.
  The dropping related requirements are applied for all the component carriers used for V2X CA.

## Slide 3: Agreements on V2X Carrier Aggregation
Delay requirements for CC addition/release based on dedicated RRC signaling.
  20ms RRC processing time is enough
  1ms interruption is allowed for UE performing RF tuning/retuning and AGC settling
  The allowed maximum CC addition time is 20ms
  The allowed maximum CC release time is 20ms
Interruption at CC addition/release for V2X CA.
  Interruptions to WAN
    No interruption is allowed for V2X intra-band contiguous CA
    An interruption of up to 2 subframes is allowed for V2X non-contiguous CA
  Interruptions to V2X Sidelink Communication
    An interruption of up to 1 subframe is allowed for V2X intra-band contiguous CA
    An interruption of up to 1 subframe is allowed for V2X non-contiguous CA