## Slide 1: WF on n5 usage in Japan
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 Meeting #86
Athens, Greece, 26 February – 2 March 2018
R4-1803248

## Slide 2: Background
To utilize n5 in Japan (for harmonization purpose), additional spurious requirements of -40 dBm/MHz at 870-890 MHz which is one of Japanese regulatory requirements has been proposed by introducing A-MPR up to 15 MHz CBW [1].
For the proposal, several concerns for n5 operations in US were raised.
  Unnecessary constraints such as power reduction, RB restriction in US operation
  US regulatory impacts i.e. FCC limits
  UE design impact
[1] R4-1802138 Further discussion on band n5 usage in Japan Source: NTT DOCOMO, INC.

## Slide 3: Observations
The intension to introduce A-MPR with NS is NOT to impact n5 operations in US and those concerns cannot be issues with reasons below
  Constraints in US operation such as power reduction, RB restriction
    The A-MPR applies only when the gNB signals the NS i.e., unless US operators indicate the NS, the A-MPR will never be used. Furthermore, number of RB is also not reduced unless their gNB intentionally restricts it.
  US regulatory impacts i.e. FCC limits
    With the same reason as the above, emission limits for n5 UEs operated in US will never change as long as US operators signal NS_01.
  UE design impact
    As explained in [1], the motivation of A-MPR introduced in LTE B5 was not to impact legacy B5 duplexer design. Therefore, the same approach for n5 will also not affect the UE design.

## Slide 4: Way forward
It is proposed to confirm that n5 operations in US are not affected by introducing the A-MPR with the observations shown in previous slide for the next meeting.
If no issue is identified for n5 operations in US, the additional emission requirement with NS will be specified for n5 up to 15 MHz CBW.