## Slide 1: Proposal on NR HPUE definition for PC2
CMCC, Huawei, HiSilicon, OPPO, vivo, Xiaomi, ZTE, CATT, Intel, Qorvo, Skyworks, broadcom
3GPP TSG-RAN WG4 Meeting #86 R4-1803259
Athens, Greece, 26 Feb – 2 March 2018

## Slide 2: Background
The following NR bands were approved to support PC2 HPUE for 5G NR[1][2][3]:
Band n41 (2496 – 2690 MHz)
UL-MIMO (2Tx 23+23dBm) and 1Tx 26dBm are supported for NR Band n41
Band n77 (3.3 - 4.2 GHz)
Band n78 (3.3 - 3.8 GHz)
Band n79 (4.4 - 5 GHz)
References
  [1] R4-1706068 WF on high power UE for 3.5GHz CMCC
  [2] R4-1709974 WF on HPUE requirements in Rel15 Huawei, HiSilicon
  [3] R4-1801190 WF on HPUE definition for NR PC2 UE CMCC

## Slide 3: Proposals
5G NR PC2 HPUE definition for SA scenario:
  UL MIMO (2Tx 23+23dBm) with total output power of 26dBm is supported by specification for NR Bands n77,n78,n79
  1Tx +26dBm HPUE is also supported by specification for NR Bands n77,n78,n79
  Only PA configurations of 23+23dBm for UL MIMO and 26dBm for 1Tx are supported by specification for NR TDD bands for PC2 UE in Rel-15