## Slide 1: WF on DL CA Tx requirements for FR2
Qualcomm, Intel, [ ]
R4-1803274
3GPP TSG-RAN WG4 Meeting #86
Athens, Greece, 26th Febuary – 2nd March
Agenda item: 7.

## Slide 2: Background
R4-1801740, “Tx Requirements for CA combinations with asymmetric number of CCs in UL and DL”, 3GPP TSG RAN WG4 Meeting #86, Athens, Greece, February 26 – March 2, 2018
New problem in CA operation in FR2 was presented
Some companies needed more input for discussions
Carrier leakage and IQ Image are specified relative to power of allocated RBs
Details on excerptions depend on peak EIRP discussion

## Slide 3: Way Forward
Carrier leakage and IQ Image excerptions will be specified for DL CA
Aggregated BW of DL will be used as basis for carrier leakage regardless of UL aggregated BW
Details, levels and how to specify are FFS
RAN4 will not introduce requirements for FR2 non-contiguous UL CA in during Rel-15 work item
No CA requirements for FR2 will be specified until agreement on carrier leakage and IQ image requirements is reached