## Slide 1: Way forward on eFeMTC RRM requirements for CRS muting
Ericsson, Nokia, Nokia Shanghai Bell, Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #86 R4-1803491
Athens, Greece, 26 February – 2 Mars, 2018
Agenda Item: 6.19.4.2

## Slide 2: Proposals for CRS muting
Initial cell acquisition
  when UE has EARFCN pre-provisioning
    UE may assume that there is no full BW CRS transmission
  when UE does not have EARFCN pre-provisioning
    full BW CRS is transmitted in 1 DL subframe every TBD ms.

## Slide 3: Proposal for CRS muting
Muted CRS BW for category M2
  In a cell where CRS muting is applied, RAN4 agreed that CRS are always transmitted in the following number of PRBs in the centre of the cell BW:
    6 PRBs, or
      Category M1 transmit timing error requirements of 24*Ts applies for category M2
    24 PRB
      If this indication is received, category M2 transmit timing error is defined as 12*Ts
  Therefore, there is a need for the network to inform UE about the number of PRBs in the central frequency of the cell bandwidth when muting is enabled.