## Slide 1: Way forward on SSB-based inter-frequency measurement requirements
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #86bis Melbourne, Australia, 16th – 20th April, 2018
Agenda item: 7.9.4.2
R4-1805565

## Slide 2: Background
Measurement objects with same SMTC periodicity and offset within the same FR range should share the same delay requirement.
Strive to address the SMTC overlapping issue should be based on SMTC periodicity and offset grouping and each group has its own scaling factor
  The definition of SMTC periodicity and offset grouping is FFS
  When all SMTC occasions are non colliding (no measurement gap contains SMTC from more than one frequency layer) there is no need for an additional scaling factor
Strive to keep UE measurement flexibility the same as LTE
Companies are encouraged to suggest the principle to define the requirement methodologies within the below options:
  Option 1: unified delay requirement among different carriers
  Option 2: requirements are defined per carrier
Companies are encouraged to provide views on the impact of AGC issue
FFS the delay caused by gap sharing with intra-frequency measurement and DRX mode.

## Slide 3: Way forward
Conclusion on the methodology of defining inter-frequency measurement requirements will be expected in RAN4#87 meeting.
Companies are encouraged to provide analysis and investigation on four alternatives of defining the inter-frequency measurement requirements in considering of the following aspects
  Factor 1: Margin for UE implementation
  Factor 2: Gap utilization
  Factor 3: Trade-off between Factor 1 and Factor 2.

## Slide 4: Way forward
Atl1: The delay requirement is unified among different carriers, and the requirement of inter-frequency carrier #i can be expressed as:
Atl2: The delay requirement is per-carrier defined for each carrier, and the requirement of inter-frequency carrier #i can be expressed as:
  The value of scaling factor in each carrier Nscaling1,carrier_i = Nfreq,fully + Nfreq,partially + 1 ≤ Nfreq
    Where Nfreq,fully is the number of carriers whose SMTC occasions are fully colliding with the SMTC occasions of carrier #i.
    Where Nfreq,fully is the number of carriers whose SMTC occasions are partially colliding with the SMTC occasions of carrier #i.

## Slide 5: Way forward
Atl3: The delay requirement is per-carrier defined for each carrier, and the requirement of inter-frequency carrier #i can be expressed as:
  The value of scaling factor in each carrier Nscaling2,carrier_i ≤ Nfreq
    The scaling factor is based on the assumption
    The detailed principles to decide the value of Nscaling,carrier_i refer to the Proposal 1 in [R4-1803787, Ericsson]
Atl4: The delay requirement is per-carrier defined for each carrier, and the requirement of inter-frequency carrier #i can be expressed as:
  The value of scaling factor in each carrier Nscaling3,carrier_i ≤ Nfreq
    The detailed principles to decide the value of Nscaling,carrier_i refer to Page 4 in [R4-1804608, NTT DOCOMO]

## Slide 6: Way forward
For Alt 1-4, it is assumed that there are totally Nfreq inter-frequency layers to be monitored via this gap pattern.
Companies are encouraged to provide views on how to resolve the AGC issue, e.g.,
  Increasing UE’s dynamic range
  Extending the M value which is the required sample number for inter-frequency measurement.
  Duplicating same beam direction to 2 SSBs
The requirements derived for Alt 1-4 do not yet consider the delay caused by gap sharing with intra-frequency measurement and DRX mode.
  Note: FFS on how to capture the scaling factor K for gap sharing and DRX.
The requirements derived for Alt 1-4 are suggested to consider the number of inter-RAT carriers configured in the UE