## Slide 1: WF for FR2 Power Control Requirements
MediaTek Inc.
3GPP TSG-RAN WG4 #86bis Meeting R4-1805701
Melbourne, Australia, April 16th – 20th, 2018

## Slide 2: Background
FR2 UE power control has been further discussed in this meeting [1-4] following the way forward in RAN4 #86 meeting [5].
Open-loop power control (absolute power) test method and requirements has been proposed in [1-3].
Relative power control tolerance requirements were proposed in [1].

## Slide 3: Agreements
Both open-loop power control and relative power control tolerance requirements are verified under beam-locked condition.
Relative power control tolerance is verified in peak EIRP direction.

## Slide 4: Way Forward (1)
To define open-loop power control requirements
  The output power to be set such that the received power at the test system is within a range defined by the target received power and the absolute tolerance.
  Tolerance requirement to be considered as a starting point
    [+/- 12 dB] under normal condition

## Slide 5: Way Forward (2)
Consider relative power control requirement using the following numbers as a starting point.
Power step DP (Up or down) [dB] | All combinations of PUSCH and PUCCH, PUSCH/PUCCH and SRS transitions between sub-frames, PRACH [dB]
ΔP < 2 | [±3.0]
2 ≤ ΔP < 3 | [±4.0]
3 ≤ ΔP < 4 | [±5.0]
4 ≤ ΔP < 10 | [±6.0]
10 ≤ ΔP < 15 | [±8.0]
15 ≤ ΔP | [±9.0]
TPC command | UL channel | Aggregate power tolerance within [21] ms
0 dB | PUCCH/PUSCH | [±3.5 dB]
Relative power tolerance for transmission (normal conditions)
Aggregate power control tolerance (normal conditions)

## Slide 6: References
[1] R4-1804159, “Open loop TPC for FR2”, Intel Corporation
[2] R4-1804213, “Pcmax in FR2 UL power control”, Intel Corporation
[3] R4-1804264, “Absolute power control accuracy and relation to beam correspondence for FR2”, Ericsson
[4] R4-1804333, “FR2 UE power control requirements”, MediaTek Inc.
[5] R4-1803371, “Way Forward on FR2 Power Control”, MediaTek Inc., Intel, Ericsson, LGE