## Slide 1: Consideration on evaluation system performance of 2RX vehicle mounted NR UE at FR1
LG Electronics, Volkswagen AG, Samsung
3GPP TSG-RAN WG4 #88 Meeting Gothenburg, Sweden, 20 - 24 August 2018 Agenda Item: 10.3.2
R4-1810454

## Slide 2: Background (1)
In LS from 5GAA, Car OEM requested to allow 2Rx antenna as exceptional case for vehicle mounted NR UE at frequency bands where 4Rx is mandated.
  Use cases are broadband use cases like infotainment or data exchange using Uu interface
  4Rx mandating for some NR operating bands (n7, n38, n41, n77, n78, n79) at FR1 will restrict the design freedom of Car OEM.  need for 2Rx vehicle UE at above listed bands
  If exceptional 2Rx antenna is not agreed, slower deployment of vehicle mounted NR UE is expected which can result in less positive market perception of 5G.
  This exception request is not for the NR V2X service specified in SA1 in Rel-15.
    No NR V2X WI in RAN as of now.
    This issue is irrelevant with NR V2X.
  RAN4 agreed WF with three candidate options

## Slide 3: Background (2)
In last RAN Plenary meeting, interested companies joined further discussion how to treat the automotive industry and 5GAA request for 2Rx exceptions
RAN plenary agreed to study on evaluation for 2Rx exception in rel-15 vehicle NR mounted UE in RP-181467 with these objectives
  Aspects to study in allowing 2 RX exception for vehicle mounted UEs in frequency bands where 4 Rx is mandated:
    Investigate the impact of 2Rx vehicle mounted UE on coverage and throughput and the possible ways to avoid or at least minimize such impact.
      Link budget with 2 RX vehicular UE
      TCU receiver RF chain and architecture
      Coverage and throughput impacts at system level
    Methods to distinguish vehicular UE from handheld UE
      Methods to define vehicle mounted UEs
      Methods to verify conformance and GCF certification (excluding OTA scope)

## Slide 4: Issues
RAN4 list up technical aspect for 2Rx vehicle UE
  1 : System throughput issues with 4Rx Handheld device and 2Rx Vehicle UE
    Whether or not need to decide basic system parameters to evaluate system throughput
  2 : System Coverage issues with 4Rx Handheld device and 2Rx Vehicle UE
    Need to agree the link budget for vehicle mounted NR UE
    Antenna gain including losses (caused by bodies or cables) for both HH UE and vehicle UE
  3 : How to distinguish Handheld UE and Vehicle UE in FR1
    Need to declare its type to TE vender?
    Whether or not need to MIMO layer indications(optional feature) for some 4Rx mandatory bands at FR1

## Slide 5: 1. System throughput issue
Whether or not need to evaluate the system performance?
  System capacity study is not responsibility of RAN4
    Most WI treat in RAN1 for system capacity
  Rel-15 NR specifications allow 2Rx fallback as UE implementation
    In real field, some 4Rx UE can be fallback to 2Rx (e.g., to save the UE power) as far as they can remain in the network coverage.
    Effectively, 2Rx and 4Rx HH UE will exist in real field operation at specific band regardless of being vehicle UE.
    Therefore, RAN4 can conclude that allowing 2 RX for vehicle UEs does not cause additional negative impact on the system capacity.
In an event of impact on the system capacity, then the performance comparison should be between
    When 2Rx vehicle exception is allowed (i.e., vehicle UEs with 2 RX), and
    When 2Rx vehicle exception is NOT allowed (i.e., vehicle UEs with 4 RX)
    NOTE: Rx antenna implemations in vehicles differ from HH implementations in terms of gains and radiation pattern
  Also consider aspects including the portion of HH UEs and the impact of fallback operation.

## Slide 6
  Shall consider reasonable link budget for vehicle UE
    Vehicle reference architecture -> one implementation given in RP‑181117
    Comparison antenna gain (including cable or body loss)
      Handheld NR UE
      Vehicle mounted NR UE
  Vehicle UE antenna gain needs to be determined based on automotive industry input.
    Antenna gain in vehicle is much higher (at least 4dB) than handheld UE
    DL: Taking antenna gain into account, expected similar receiver SNR compare to 2Rx of vehicle UE and 4Rx handheld UE
    UL: Taking antenna gain into account, vehicle UE has superior performance than handheld device.
    NOTE: In contrast to HH vehicular UE usage doesn‘t suffer from body and building losses.
2. System Coverage issue

## Slide 7: 3. Method to distinguish vehicle NR UE from Handheld UE
  Option1: UE declaration for testing (in RAN4 previous discussion)
    For conformance test, both 2Rx and 4Rx can be declared for all chipset
    For device conformance test, vehicle UE can only declare 2Rx for some specific 4Rx mandating NR Bands
  Option2: use MIMO layer signalling (defined the UE capability signalling as optional feature in NR)
    RAN agreed 4 layer was mandatory for 4Rx mandatory operating NR Bands.
      It means HH UE signal the MIMO layer with 4 layer
    Vehicle UE can signal the number of layer with 2 layer to gNB to distinguish between V UE and HH UE  Then gNB optimize the NR UE scheduling resource.
    Also, in conformance test, V UE signalled the number of layer with 2 layer.
  Option 2 is more clear in both real field and conformance test

## Slide 8: References
[1] R4-1806681 Consideration on 2Rx REFSNES for NR vehicular UE at FR1 [2] ECCREP228 (Refer Antenna gain in 2.4)
[3] http://5gaa.org/membership/our-members/
[4] RP-181117 Minimum requirement of 2Rx antennas for permanently mounted UE in vehicles for NR