## Slide 1: Way forward on demodulation and CSI requirements for high capacity stationary wireless link and 1024QAM
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #88 R4-1811378
Gothenburg, Sweden, August 20 – 24, 2018
Agenda Item: 6.6.4

## Slide 2: Demodulation requirements under fading conditions
Parameters | Value
Bandwidth | 10MHz
Channel model | EPA5
CFI (OFDM symbol for control channel) | 1
Duplex mode | FDD, TDD
Table 1: common parameters
For 1024QAM demodulation requirements, the test cases given in Table 2 with the common parameters given in Table 1 are identified

## Slide 3: Demodulation requirements under fading conditions
Table 2: Test cases for demodulation tests under fading conditions
No. | TM | PMI feedback (pre-coding) | MIMO layer | MCS | Antenna config.
1 | TM4 | Wideband PMI Feedback (PUSCH 3-1, Reporting interval =1) | 1-layer | MCS#23 (with 52752 bits) | 4x2 Low
2 | TM4 | Wideband PMI feedback (PUSCH 3-1, Reporting interval =1) | 2-layer | MCS#23 (with 52752 bits) | 4x4 Low
3 | TM9 (Note 1) | Per-PRG Random Precoder | 1-layer | MCS#23 (with 52752 bits) | 4x2 Low
4 | TM9 | Wideband PMI feedback | 2-layer | MCS#23 (with 52752 bits) | 4x4 Low
For 1024QAM demodulation requirements, the candidate test cases given in Table 2 with the common parameters given in Table 1 are identified
Companies are encouraged to provide the simulation results with impairments for 1024QAM DL FDD and TDD demodulation fading tests
Note 1: For TM9, configure 4Tx with 2 CRS ports

## Slide 4: SDR test
Test parameters:
Transmission mode: TM3
Bandwidth: 10MHz
Antenna configuration: 2 x 2 for 2-layer transmission per CC, and 4 x 4 for 4-layer transmission per CC
MCS 24 for 2 x 2 2-layer transmission per CC, and MCS 24 for 4 x 4 4-layer transmission per CC
CFI = 1
Tx EVM: 2%

## Slide 5: CQI reporting test (For information)
Definition test:
Minimum requirement PUCCH 1-0 (Cell-Specific Reference Symbols): CRS based TM single codeword with TM1 under static channel in Annex B.1
  Bandwidth:
    FDD: 10MHz
    TDD: 20MHz
CQI Index |  |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | Notes
Target Spectral Efficiency |  |  | OOR | 0.1523 | 0.3770 | 0.8770 | 1.4766 | 2.4063 | 3.3223 | 3.9023 | 4.5234 | 5.1152 | 5.5547 | 6.2266 | 6.9141 | 7.4063 | 8.3321 | 9.2578 | 
MCS Scheme | PRB | Available RE-s | Imcs |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MCS.x1A | 50 | 6300 | DTX | 0 | 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 | 21 | 22 | 23 | 25 | 
MCS.x2A | 100 | 12600 | DTX | 0 | 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 | 21 | 22 | 23 | 25 | 
Note 1: Mapping between Imcs and CQI Index according to Tables 7.1.7.1-1A, 7.1.7.2.1-1 and 7.2.3-2 in TS 36.213 [6]. Note 2: 3 symbols allocated to PDCCH. Note 3: Sub-frame#0 and #5 are not used for the corresponding requirement. The next subframe (i.e. sub-frame#1 or #6) shall be used for potential retransmissions. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Table 3: CQI2MCS table

## Slide 6: DMRS overhead reduction
DMRS ports 7,8,11,13 with OCC=4
16QAM, EPA5, 4-layer
1dB difference i.e. improvement with reduced DMRS