## Slide 1: Way forward on NR UE CSI requirements
Samsung
3GPP TSG-RAN WG4 Meeting RAN4#88 R4-1811693
Gothenburg ,Sweden, 20 -24 Aug, 2018

## Slide 2: Background (agreed test cases list in previous meeting)
Static CQI test cases
  Test 1: FR1 FDD 10MHz &15kHz , 2*2, 2*4
  Test 2: FR1 TDD 40MHz&30kHz, 2*2, 2*4
  Test 3: FR2 100MHz& 120kHz, 2*2
Wideband fading CQI test cases
  Test 1: FR1 FDD 10MHz &15kHz , 2*2, 2*4
  Test 2: FR1 TDD 40MHz&30kHz, 2*2, 2*4
  Test 3: FR2 100MHz& 120kHz, 2*2
Wideband PMI test cases
  Test 1: FR1 FDD 10MHz &15kHz , 8*2, 8*4
  Test 2: FR1 TDD 40MHz&30kHz, 8*2, 8*4
  Test 3: FR2 100MHz& 120kHz, 2*2
4Tx PMI test cases (FFS for wideband or sub-band)
  Test 1: FR1 FDD 10MHz &15kHz , 4*2, 4*4
  Test 2: FR1 TDD 40MHz&30kHz, 4*2, 4*4
RI test
  Test 1: FR1 FDD 10MHz&15kHz, 2*2,4*4
  Test 2: FR1 TDD 40MHz&30kHz, 2*2, 4*4
  Test 3: FR2 100MHz&120kHz, 2*2

## Slide 3: Test Scope
Prioritize CQI, PMI, RI test cases in Rel-15
CSI reporting Type
  No test cases for semi-persistent CSI reporting in Rel-15
CSI-RS resources Type
  Introducing Test cases for semi-persistent CSI-RS resources
    Replace CSI-RS configuration in one of periodic CSI test cases with semi-persistent CSI-RS resources
  CRI/CSI test cases
  Deprioritize CRI/CSI test cases in Rel-15
L1-RSRP measurement handling
  L1-RSRP corresponding requirements will be covered in RRM specification
FFS whether introducing joint CQI,PMI reporting test case(s)
Sub-band CQI test cases
  Introducing sub-band CQI test cases in Rel-15 as second priority
    Using largest sub-band size according to BWP bandwidth
    FFS for applicable channel model
Measurement restriction configuration: off (baseline assumption)
  specific test cases will be introduced with Measurement restriction configuration: on

## Slide 4: Generic test set-up (1/2)
CHBW and SCS
  Case 1: FR1 FDD 10MHz CBW + 15kHz SCS
  Case 2: FR1 TDD 40MHz CBW + 30kHz SCS
  Case 3: FR2 TDD 100MHz CBW + 120kHz SCS
  CQI table
      For FR1 CQI table 2
      For FR2 CQI table 1
TDD DL-UL configuration
  FR1 30kHz: 7D1S2U, S = 6D:4G:4U
  FR2 120kHz:DDSU, S=11D+3G
PDSCH scheduling Type:
  Type A, Bundle size 2
  skip scheduling PDSCH in special sub-frames
DMRS configurations:
  Type 1, 1 front loaded symbol + 1 additional DMRS symbol
  TDM for DMRS and PDSCH
Control symbols assumption:
  FR1: Symbols #0 and 1 in each slot
  FR2: Symbol #0 and 1 in each slot
  Do not schedule PDSCH in in control symbols time duration
HARQ:
  For PMI, RV sequence ={0,2,3,1}
  For RI and CQI test cases ,no retransmission
PTRS, TRS configuration:
  TRS: 20ms periodicity, 2 slots pattern, with offset 10ms, Bandwidth: full BWP,0 dB boosting
  PTRS: [only configured for FR2 with port 1, per 2PRB in frequency domain, per symbol in time domain]
PBCH configuration:
  [PBCH overhead: Skip scheduling PDSCH for PBCH slot i.e. slot 0 per radio frame (20ms periodicity)]

## Slide 5: Generic test set-up (2/2)
NZP CSI-RS port configurations:
NZP CSI-RS periodicity and slot offset: TBD
  For simulation purpose, configured with periodicity of 5 slots with slot offset as 1
CQI to MCS mapping table follows the 1-to-1 CQI to MCS mapping according to the (spectral) efficiency column in corresponding CQI and MCS tables.
CSI computation delay and gNB emulator scheduling delay assumption
  Periodic CSI feedback delay can be assumed as below:
    Minimum CSI computation delay 4ms
    Minimum gNB emulator scheduling delay 4ms
  Aperiodic CSI feedback delay followed the definition in TS38.214 5.4, assuming same processing delay for UE computation and gNB emulator processing delay.
    For simulation purpose, the detailed aperiodic CSI feedback delay for aperiodic CSI reporting tests is FFS.
Parameters | 2 Ports | 4 ports | 8 ports
nrofPorts | 2 | 4 | 8
firstOFDMSymbolInTimeDomain | 5 | 5 | 5
firstOFDMSymbolInTimeDomain2 | N.A | N.A | N.A
cdm-Type | fd-CDM2 | fd-CDM2 | cdm4-FD2-TD2
density | 1 | 1 | 1

## Slide 6: CQI Test cases
Test metric
  Static CQI:
    The reported CQI value shall be in the range of ±1 of the reported median more than 90% of the time.
    If the PDSCH BLER using the transport format indicated by median CQI is less than or equal to 0.1, the BLER using the transport format indicated by the (median CQI + 1) shall be greater than 0.1. If the PDSCH BLER using the transport format indicated by the median CQI is greater than 0.1, the BLER using transport format indicated by (median CQI – 1) shall be less than or equal to 0.1.
  Fading CQI:
    a) a CQI index not in the set {median CQI -1, median CQI, median CQI +1} shall be reported at least a % of the time;
    b) the ratio of the throughput obtained when transmitting the transport format indicated by each reported wideband CQI index and that obtained when transmitting a fixed transport format configured according to the wideband CQI median shall be ≥ g ;
    c) when transmitting the transport format indicated by each reported wideband CQI index, the average BLER for the indicated transport formats shall be greater or equal to TBD.
Test SNR points:
  FFS between [0~20] dB
  Companies are encouraged to bring results within [0~20]dB with 2dB step size
Channel model and MIMO correlation:
  Static CQI: static channel as TS 36.101 annex B
  Wideband fading CQI: FR1 (ULA High for 2Rx, [XP High for 4Rx]), FR2 [(ULA XP High)]
    TDL-A 30ns, 5Hz for FR1 FDD
    TDL-A 30ns, 10Hz for FR1 TDD
    TDL-A 30 ns, 75 Hz for FR2 TDD
CSI-RS resources and CSI reporting Type: Periodic
Companies are encouraged to bring results
  Static CQI: percentile of within median CQI +/-1 and BLER for median CQI +/-1
  Fading CQI: Relative throughput ratio between following CQI and median CQI , BLER with following CQI, reporting CQI percentile out side of {median CQI-1 ~median CQI +1}

## Slide 7: PMI test cases
4Tx PMI test cases for FR1:
  wideband PMI
FFS for 16,32 Tx ports test cases in FR1
Test metric: Reusing LTE test metric
  Relative Throughput ratio between following PMI and random PMI at SNR point corresponding to [70% ] TP with follow PMI.
Codebook construction parameters for 8Tx ports: (N1,N2), (O1,O2)
  (N1,N2) = (4,1), (O1, O2) = (4,1)
CSI-RS resources and CSI reporting Type: aperiodic
FRC (baseline)
  4Tx PMI test case: MCS 13 with Rank1
  8Tx PMI test case: MCS 13 with Rank2
  2Tx PMI test case: MCS 13 with Rank1
Channel model & MIMO correlation:
  2Tx: [ULA Low], TDL-A 30 ns, 75 Hz for FR2 TDD
  4Tx: XP High , TDL-A, 30ns, 5Hz for FR1 FDD, 10 Hz for FR1 TDD
  8Tx: XP High, TDL-A,30 ns, 5Hz for FR1 FDD, 10 Hz for FR1 TDD
FFS for beam steering model
  For simulation, beam steering mode in TS 36.101 B.2.3A.4 used for 4Tx ad 8Tx PMI test cases
For simulation purpose, companies are encouraged to provide absolute TPs with following PMI and random PMI results with SNR [-6dB ~ 20dB] with 2dB step size

## Slide 8: RI test cases
Previous agreements
  Number of Rank layers
    FR1 : 1,2,3,4
    FR2: 1,2
  In Rel-15 at least introduce below test cases
    FR1:
      2*2 for upper to Rank 2 test
      4*4 for upper to Rank4 test
    FR2:
      2*2 for upper to Rank2 test
  Test metric: using LTE as starting point, FFS for test point(s)
    a) The ratio of the throughput obtained when transmitting based on UE reported RI and that obtained when transmitting with fixed rank 1 shall be ≥ g1;
    b) The ratio of the throughput obtained when transmitting based on UE reported RI and that obtained when transmitting with fixed rank 2 shall be ≥ g2;
Proposal:
  CSI-RS resources and CSI reporting Type: periodic
  MIMO correlation:
    FR1 TDD: TDL_A 30ns, 10Hz, [ULA Low and ULA High]
    FR1 FDD: TDL_A 30ns, 5Hz,[ ULA Low and ULA High]
    FR2 TDD: TDL-A 30 ns, 75 Hz for FR2 TDD,[ (ULA Low, ULA High)]
  For simulation purpose, companies are encouraged to provide following Rank, fixed rank1 and fixed rank2 results
    For RI test cases with 4Tx 4Rx, interested companies can bring the simulation results for fixed rank 3 and rank 4 should also be collected, in order to help decide the final test metric.
Notes: Qualcomm: for fixed rank-3 and rank-4, what is the motivation? Are you going to check low SNR to see the gain? It does not make sense.
China Telecom: we are not proposing to define the requirements based on rank-3/4. We just want company to provide simulation results for comparison to see the whole picture to decide the test metric.
Qualcomm: without intention to define the requirements, what is the purpose?
Intel: we agreed to provide the results with fixed rank-1 and rank-2.
Samsung: the baseline is to provide the requirements with fixed rank-1 and rank-2. the interested companies can provdie the requiremetns with rank-3/4.

## Slide 9: Summary of agreed test cases list
Static CQI test cases
  Test 1: FR1 FDD 10MHz &15kHz , 2*2, 2*4
  Test 2: FR1 TDD 40MHz&30kHz, 2*2, 2*4
  Test 3: FR2 100MHz& 120kHz, 2*2
Wideband fading CQI test cases
  Test 1: FR1 FDD 10MHz &15kHz , 2*2, 2*4
  Test 2: FR1 TDD 40MHz&30kHz, 2*2, 2*4
  Test 3: FR2 100MHz& 120kHz, 2*2
Wideband PMI test cases
  Test 1: FR1 FDD 10MHz &15kHz , 8*2, 8*4
  Test 2: FR1 TDD 40MHz&30kHz, 8*2, 8*4
  Test 3: FR2 100MHz& 120kHz, 2*2
4Tx PMI test cases (Wideband)
  Test 1: FR1 FDD 10MHz &15kHz , 4*2, 4*4
  Test 2: FR1 TDD 40MHz&30kHz, 4*2, 4*4
RI test
  Test 1: FR1 FDD 10MHz&15kHz, 2*2,4*4
  Test 2: FR1 TDD 40MHz&30kHz, 2*2, 4*4
  Test 3: FR2 100MHz&120kHz, 2*2
Sub-band CQI test cases
  Test 1: FR1 FDD 10MHz &15kHz , 2*2, 2*4
  Test 2: FR1 TDD 40MHz&30kHz, 2*2, 2*4
  Test 3: FR2 100MHz& 120kHz, 2*2
FFS whether introducing 16Tx, 32 Tx ports PMI test cases in FR1

## Slide 10: Initial Simulation assumption for Static CQI (information)
Parameter | Unit | Static CQI test (FR1 FDD) | Static CQI test (FR1 TDD) | Static CQI test (FR2)
System parameter |  |  |  | 
Bandwidth/SCS | MHz/kHz | 10MHz /15kHz | 40MHz/30kHz | 100MHz/120kHz
Transmission Scheme |  | 1 | 1 | 1
Duplex Mode |  | FDD | TDD | TDD
DLUL configuration |  | N.A | 7D1S2U | DDDSU
Propagation channel |  | AWGN | AWGN | AWGN
Correlation and antenna configuration |  | 2*2, 2*4 with static channel in TS36.101 Annex B | 2*2, 2*4 with static channel in TS36.101 Annex B | 2Rx 2*2 with static channel in TS36.101 Annex B
CSI-RS resource setting (periodic) |  |  |  | 
resourceConfigType |  | Periodic | Periodic | Periodic
CSI-RS/CSI-IM periodicity and slot offset |  | 5slot 1 slot offset | 5slot, 1 slot offset | 5slot, 1 slot offset
NZP CSI-RS ports |  | 2 port {3000,3001} | 2 port {3000,3001} | 2 port {3000,3001}
NZP CSI-RS configuration CDM type/CSIRS resource mapping/CSI-RS-Density |  | [FD-CDM2/density 1] | [FD-CDM2/density 1] | [FD-CDM2/density 1]
CSI-IM configuration |  | FFS | FFS | FFS
CSI report setting (periodic) |  |  |  | 
reportConfigType |  | periodic | periodic | periodic
Reporting periodicity and slot offset |  | FFS | FFS | FFS
Codebook Restriction |  | 010000 (fixed rank2) | 010000 (fixed rank2) | 010000 (fixed rank2)
Reporting granularity |  | Wide-band | Wide-band | Wide-band
Physical channel for reporting |  | PUSCH | PUSCH | PUSCH
PUCCH reporting format |  | FFS | FFS | FFS
CQI table |  | Table 2 with 256QAM | Table 2 with 256QAM | Table 1 without 256QAM

## Slide 11: Initial Simulation assumption for wideband fading CQI (information)
Parameter | Unit | Fading CQI test (FR1 FDD) | Fading CQI test (FR1 TDD) | Fading CQI test (FR2)
System parameter |  |  |  | 
Bandwidth/SCS | MHz/kHz | 10MHz /15kHz | 40MHz/30kHz | 100MHz/120kHz
Transmission Scheme |  | 1 | 1 | 1
Duplex Mode |  | FDD | TDD | TDD
DLUL configuration |  | N.A | 7D1S2U | DDDSU
Propagation channel |  | TDL_A 30ns, 5Hz | TDL_A 30ns, 10Hz | TDL_A 30ns, 75Hz
Correlation and antenna configuration |  | 2Rx 2*2 4Rx: 2*4 [ULA High] for 2Rx [XP High] for 4Rx | 2Rx 2*2 4Rx: 2*4 [ULA High] for 2Rx [XP High ]for 4Rx | 2Rx 2*2 [ULA High]
CSI-RS resource setting (periodic) |  |  |  | 
resourceConfigType |  | Periodic | Periodic | Periodic
CSI-RS/CSI-IM periodicity and slot offset |  | 5slot 1 slot offset | 5slot, 1 slot offset | 5slot, 1 slot offset
NZP CSI-RS ports |  | 2 port {3000,3001} | 2 port {3000,3001} | 2 port {3000,3001}
NZP CSI-RS configuration CDM type/CSIRS resource mapping/CSI-RS-Density |  | [FD-CDM2/density 1] | [FD-CDM2/density 1] | [FD-CDM2/density 1]
CSI-IM configuration |  | FFS | FFS | FFS
CSI report setting (periodic) |  |  |  | 
reportConfigType |  | periodic | periodic | periodic
Reporting periodicity and slot offset |  | FFS | FFS | FFS
Codebook Restriction |  | 000001 | 000001 | 000001
Reporting granularity |  | Wide-band | Wide-band | Wide-band
Physical channel for reporting |  | PUSCH | PUSCH | PUSCH
PUCCH reporting format |  | FFS | FFS | FFS
CQI table |  | Table 2 with 256QAM | Table 2 with 256QAM | Table 1 without 256QAM

## Slide 12: Initial Simulation assumption for Wideband PMI (information)
Parameter | Unit | Test 1 (FR1 FDD) | Test 2 (FR1 TDD) | Test 3 (FR2)
System parameter |  |  |  | 
Bandwidth/SCS | MHz/kHz | 10MHz /15kHz | 40MHz/30kHz | 100MHz/120kHz
Transmission Scheme |  | 1 | 1 | 1
Duplex Mode |  | FDD | TDD | TDD
DLUL configuration |  | N.A | 7D1S2U | DDDSU
Propagation channel |  | TDL_A 30ns, 5Hz | TDL_A 30ns, 10Hz | TDL_A 30ns, 75Hz
Correlation and antenna configuration |  | 8*2 8*4 [XP spatially High] | 8*2 8*4 [XP spatially High] | 2*2 [ULA Low]
CSI-RS resource setting (aperiodic) |  |  |  | 
resourceConfigType |  | aperiodic | aperiodic | aperiodic
CSI-RS/CSI-IM periodicity and slot offset |  | 5slot 1 slot offset | 5slot 1 slot offset | 5slot 1 slot offset
NZP CSI-RS ports |  | 8 port {3000…3007} | 8 port {3000…30007} | 2 port {3000,3001}
NZP CSI-RS configuration CDM type/CSIRS resource mapping/CSI-RS-Density |  | [CDM4,density 1 (row 9)] | [CDM4,density 1 (row 9)] | [FD-CDM2/density 1]
CSI-IM configuration |  | FFS | FFS | FFS
CSI report setting (aperiodic) |  |  |  | 
reportConfigType |  | aperiodic | aperiodic | aperiodic
Reporting periodicity and slot offset |  | FFS | FFS | FFS
(N1,N2) |  | (2,2) | (2,2) | N.A
(O1,O2) |  | (4,4) | (4,4) | N.A
CodebookMode |  | 1 | 1 | N.A
Codebook Restriction |  | FFS | FFS | FFS
Reporting granularity |  | Wide-band | Wide-band | Wide-band
Rank |  | 2 | 2 | 1
FRC |  | MCS13 | MCS13 | MCS13
Physical channel for reporting |  | PUSCH | PUSCH | PUSCH
PUCCH reporting format |  | FFS | FFS | FFS
CQI table |  | Table 2 with 256QAM | Table 2 with 256QAM | Table 1 without 256QAM

## Slide 13: Initial Simulation assumption for Sub-band PMI (information)
Parameter | Unit | Test 1 (FR1 FDD) | Test 2 (FR1 TDD) | 
System parameter |  |  |  | 
Bandwidth/SCS | MHz/kHz | 10MHz /15kHz |  | 40MHz/30kHz
Transmission Scheme |  | 1 |  | 1
Duplex Mode |  | FDD |  | TDD
DLUL configuration |  | N.A |  | 7D1S2U
Propagation channel |  | TDL_C 100ns, 5Hz |  | TDL_C 100ns, 10Hz
Correlation and antenna configuration |  | 4*2 4*4 [XP spatially High] |  | 4*2 4*4 [XP spatially High]
CSI-RS resource setting (aperiodic) |  |  |  | 
resourceConfigType |  | aperiodic |  | aperiodic
CSI-RS/CSI-IM periodicity and slot offset |  | 5slots, 1 slot offset |  | 5slotss, 1 slot offset
NZP CSI-RS ports |  | 4 port {3000…3003} |  | 4 port {3000…30003}
NZP CSI-RS configuration CDM type/CSIRS resource mapping/CSI-RS-Density |  | [FD-CDM2 density 1 (row 4)] |  | [FD-CDM2 density 1 (row 4)]
CSI-IM configuration |  | FFS |  | FFS
CSI report setting (aperiodic) |  |  |  | 
reportConfigType |  | aperiodic |  | aperiodic
Reporting periodicity and slot offset |  | FFS |  | FFS
(N1,N2) |  | (2,1) |  | (2,1)
(O1,O2) |  | (4,-) |  | (4,-)
CodebookMode |  | 1 |  | 1
Codebook Restriction |  | FFS |  | FFS
Reporting granularity |  | Sub-band |  | Sub-band
Rank |  | 1 |  | 1
FRC |  | MCS13 |  | MCS13
Physical channel for reporting |  | PUSCH |  | PUSCH
PUCCH reporting format |  | FFS |  | FFS
CQI table |  | Table 2 with 256QAM |  | Table 2 with 256QAM

## Slide 14: Initial Simulation assumption for RI (information)
Parameter | Unit | Test 1 (FR1 FDD) | Test 2 (FR1 FDD) | Test 3 FR2
System parameter |  |  |  | 
Bandwidth/SCS | MHz/kHz | 10MHz /15kHz | 40MHz/30kHz | 100MHz/120kHz
Transmission Scheme |  | 1 | 1 | 1
Duplex Mode |  | FDD | TDD | TDD
DLUL configuration |  | N.A | 7D1S2U | DDDSU
Propagation channel |  | TDL_A 30ns, 5Hz | TDL_A 30ns, 10Hz | TDL_A 30ns, 75Hz
Correlation and antenna configuration |  | 2Rx 2*2 4Rx: 4*4 [ULA Low ULA High] | 2Rx 2*2 4Rx: 4*4 [ULA Low ULA High] | 2Rx 2*2 [ULA Low, ULA High]
CSI-RS resource setting (periodic) |  |  |  | 
resourceConfigType |  | Periodic | Periodic | Periodic
CSI-RS/CSI-IM periodicity and slot offset |  | 5 slots, 1 slot offset | 5slots, 1 slot offset | 5slots, 1 slot offset
NZP CSI-RS ports |  | 2/4 | 2/4 | 2
NZP CSI-RS configuration CDM type/CSIRS resource mapping/CSI-RS-Density |  | 2 ports: [FD-CDM2/density 1] 4 ports: [FD-CDM2 density 1 (row 4)] | 2 ports: [FD-CDM2/density 1] 4 ports: [FD-CDM2 density 1 (row 4)] | [FD-CDM2/density 1]
CSI-IM configuration |  | FFS | FFS | FFS
CSI report setting (periodic) |  |  |  | 
reportConfigType |  | periodic | periodic | periodic
Reporting periodicity and slot offset |  | FFS | FFS | FFS
Codebook Restriction |  | FFS | FFS | FFS
Reporting granularity |  | Wide-band | Wide-band | Wide-band
Physical channel for reporting |  | PUSCH | PUSCH | PUSCH
PUCCH reporting format |  | FFS | FFS | FFS
CQI table |  | Table 2 with 256QAM | Table 2 with 256QAM | Table 1 without 256QAM