## Slide 1: WF on demodulation performance for eV2X UE
3GPP TSG-RAN WG4 Meeting #88 Gothenburg, Sweden, Aug 20 – 24th, 2018
Agenda Item: 6.3.5
R4-1811696
CATT

## Slide 2: Agreements
The following agreements were reached on Tuesday Main session in RAN4#88 meeting:
  Define the following requirements for Rel-15 eV2X CA
    Define PSSCH soft buffer test
    PSCCH decoding capability test
      FFS how to define the tests
    Sustained downlink data rate test
  Do not define UE performance requirements to verify transparent transmit diversity
  scheme feature.
  Do not define any UE performance requirements for Mode-3/Mode-4 pool sharing and Resource selection latency reduction features.

## Slide 3: PSSCH enhancement
  Background
  64QAM is new modulation scheme supported by Rel-15 eV2X UE
  Rate matching and TBS scaling are introduced for Rel-15 eV2X PSCCH
Test purpose
  Verify 64QAM, rate matching and TBS scaling supported by Rel-15 eV2X
  eV2X PSSCH enhancement performance requirement
  Define two additional PSSCH test cases with GNSS based synchronization:
    PSSCH, 20MHz, MCS[22], EVA[180], [8]RB, retransmission: 0 time
    PSSCH, 10MHz, MCS4, EVA2700, 3RB, retransmission: 1 time

## Slide 4: Soft buffer test
Background
  SL-C-Rx Category 3 and 4 have been introduced for Rel-15 eV2X UE
Test purpose
  Verify SL soft buffer management and the maximum number of bits per TTI supported by the UE
    single carrier with 20 MHz CBW to verify SL-C-RX Category 3
    3 CCs with 10MHz CBW to verify SL-C-RX Category 4
UE SL-C-RX Category | Maximum number of SL-SCH transport block bits received within a TTI | Maximum number of bits of a SL-SCH transport block received within a TTI | Total number of soft channel bits | Comments
SL-C-RX Category 1 | 25456 | 25456 |  | 
SL-C-RX Category 2 | 31704 | 31704 | 737280 | 20MHz aggregated BW 16QAM
SL-C-RX Category 3 | 48936 | 48936 | 995328 | 20MHz aggregated BW 64QAM (Applicable for 10MHz+10MHz and 20MHz)
SL-C-RX Category 4 | 24496 + 24496 + 24496 = 73488 | 48936 | 1492992 | 30MHz aggregated BW 64QAM (Applicable for 10MHz+10MHz+10MHz and 10MHz+20MHz)

## Slide 5: PSCCH decoding processing test
Background
  New PSCCH decoding capability has been introduced for Rel-15 eV2X UE
Test configuration
  Verify PSCCH decoding capability both X=15 and X=30 according to UE capability
    For Type 3: X=15, Y=150
    For Type 4: X=30, Y=204
      Do not consider PSSCH overlapping test configuration
      Focus on verifying X as baseline
Aggregated RX BW by UE, MHz | V2X High Reception Capability | V2X Default Reception Capability
10, 20 (Rel.14, Rel.15) | 20 PSCCHs and 136 RBs | 10 PSCCHs and 100 RBs
30 (Rel.15) | 30 PSCCHs and 204 RBs | 15 PSCCHs and 150 RBs

## Slide 6: SDR test
Definition for performance requirement
  Combining legacy WAN SDR test and eV2X soft buffer test (PSSCH decoding processing test) to verify the concurrent WAN and eV2X communication operation, the test purpose is:
    The WAN reception in not impacted when PC5-based eV2X is concurrent with WAN operation and the PC5-based eV2X reception is not impacted by WAN reception either.

## Slide 7: Simulation assumptions
Single-link PSSCH test
  Evaluation cases
    PSSCH, 20MHz, MCS[22], EVA[180], [8]RB, retransmission: 0 time
    PSSCH, 10MHz, MCS4, EVA2700, 3RB, retransmission: 1 time
      Time interval between initial transmission and retransmission equals to 8ms
  CFO and Doppler shift algorithms: “single-DMRS” estimation
  Channel estimation
    linear interpolation in time domain
    frequency domain MMSE equalization
  PSSCH frequency offset estimation
    PSSCH DMRS
  Adjacent RBs are allocated for SA and its associated PSSCH transmission in the
  same subframe
  Note: The above assumptions have been used in Rel-14 V2X.

## Slide 8: Simulation assumptions
Single-link PSSCH test
Parameters | Unit | Values
Bandwidth | MHz | 10/20
RB |  | 3, 8
MCS |  | MCS4, MCS[22]
Time offset |  | +24Ts
Frequency offset | Hz | +1200
Propagation condition |  | EVA[180]/2700
Antenna configuration |  | 1x2 Low
Soft combining |  | Yes
Synchronization |  | GNSS or GNSS-equivalent
Table 1 Proposed simulation assumptions for PSSCH

## Slide 9: Simulation assumptions
Soft buffer test
  Test #1: single carrier with 20 MHz CBW
Table 2 Proposed simulation assumptions for Test #1
Test/Simulation parameter |  | Unit | Proposals
Channel bandwidth |  | MHz | 20
Propagation Condition |  |  | AWGN
Sidelink UE #i, 0 < i < 14 | Sidelink transmission |  | PSCCH+PSSCH
 | Timing offset | Ts | 0
 | Frequency offset | Hz | 0
 | Number of PSSCH transmissions |  | 2
 | # of subframe regarding two retransmission | subframe | 15
 | Allocated RB for PSCCH | ith subframe | 2
 | PSSCH RMC | ith subframe | 96 PRBs with MCS[27](64QAM)
 | Antenna configuration |  | 1x2
Performance metric |  |  | SNRPSSCH @5% BLER

## Slide 10: Simulation assumptions
Soft buffer test
  Test #2: 3 CCs with 10MHz CBW
Table 3 Proposed simulation assumptions for Test #2
Test/Simulation parameter |  | Unit | Proposals
Aggregated RX bandwidth |  | MHz | 30
Propagation Condition |  |  | AWGN
Sidelink UE #i, 0 < i < 14 | Sidelink transmission |  | PSCCH+PSSCH
 | Timing offset | Ts | 0
 | Frequency offset | Hz | 0
 | Number of PSSCH transmissions |  | 2
 | # of subframe regarding two retransmission | subframe | 15
 | Allocated RB for PSCCH | ith subframe | 2
 | PSSCH RMC | ith subframe | 144PRBs with MCS[27](64QAM)
 | Antenna configuration |  | 1x2
Performance metric |  |  | SNRPSSCH @ 5% BLER

## Slide 11: Simulation assumptions
PSCCH decoding capability test
  Test #1: For type 3 UE (X=15, Y=150)
Table 4 Proposed simulation assumptions for Test #1
Test/Simulation parameter |  |  | Unit | Proposals
Aggregated RX bandwidth |  |  | MHz | 30
Propagation Condition |  |  |  | Static propagation condition
Sidelink UE #j, 0 < j < 14 | Sidelink transmission |  |  | PSCCH+PSSCH
 | Timing offset |  | Ts | 0
 | Frequency offset |  | Hz | 0
 | Resource pool | Adjacenct PSCCH-PSSCH |  | True
 |  | startRB-Subchannel |  | 0
 |  | sizeSubchannel | RB | 10
 |  | numSubchannel |  | 15
 | Allocated RB for PSCCH |  |  | 2
 | Antenna configuration |  |  | 1x2
Performance metric |  |  |  | SNRPSCCH @ 1% BLER

## Slide 12: Simulation assumptions
PSCCH decoding capability test
  Test #2: For type 4 UE (X=30, Y=204)
Table 5 Proposed simulation assumptions for Test #2
Test/Simulation parameter |  |  | Unit | Proposals
Aggregated RX bandwidth |  |  | MHz | 30
Propagation Condition |  |  |  | Static propagation condition
Sidelink UE #j, 0 < j < 29 | Sidelink transmission |  |  | PSCCH+PSSCH
 | Timing offset |  | Ts | 0
 | Frequency offset |  | Hz | 0
 | Resource pool | Adjacenct PSCCH-PSSCH |  | True
 |  | startRB-Subchannel |  | 0
 |  | sizeSubchannel | RB | 5
 |  | numSubchannel |  | 30
 | Allocated RB for PSCCH |  |  | 2
 | Antenna configuration |  |  | 1x2
Performance metric |  |  |  | SNRPSCCH @ 1% BLER