## Slide 1: Way forward on possible solutions of SS-SINR measurement underestimation issue
CMCC
3GPP TSG-RAN WG4 Meeting RAN4#88 R4-1811738
Gotherburg ,Sweden, 20 -24 Aug, 2018

## Slide 2: Background
Problem:
  SS-SINR is introduced for the purpose of allow network to better predict the achievable user throughput.
  In the case of colliding SSBs, SS-SINR cannot reflect real cell load and is underestimated with low interferer load.
Deployment scenario:
  For one frequency layer, SSBs are transmitted at the same frequency location in order to avoid gap needed measurement.
Configuration restriction:
  For intra-frequency measurement, up to two SMTC periodicities can be configured with only single SMTC offset and duration.
  For inter-frequency measurement, only on SMTC configuration can be configured

## Slide 3: Way forward
RAN4 is to discuss the solutions to solve SS-SINR underestimation issue for FR1 in REL-15 TEI.
Companies are encouraged to provide analysis on the alternatives in Annex
  Other alternatives are not precluded.

## Slide 4: Annex: Possible solutions to solve the SS-SINR underestimation issue
Alternative 1: For each frequency layer, different cells transmit SSBs with same periodicity but different offsets in time domain.
  The potential impacts of Alt. 1 are discussed in R4-1810290.
Alternative 2: Introduce CSI-RS based RRM measurementss