## Slide 1: WF on FR2 EIS spherical coverage requirement
Qualcomm, Verizon, AT&T, CMCC, NTT DOCOMO, Vodafone, Telecom Italia, Orange, Dish
3GPP TSG-RAN WG4 Meeting #88 R4-1811809
Gothenburg, Sweden, 20th – 24th Aug, 2018

## Slide 2: Background
The following contributions were discussed in RAN4 #88
  R4-1810065, On EIS Spherical Coverage for FR2 Ues, Apple Inc.
  R4-1810066, Draft CR to TS 38.101-2: Introducing EIS spherical coverage requirements for PC3, Apple Inc.
  R4-1811023, On FR2 Spherical Coverage EIS Requirement, Qualcomm Incorporated
  R4-1811024, Draft CR to 38.101-2: FR2 EIS Spherical Coverage Requirement Qualcomm Incorporated
  R4-1810427, Relationship for the beam correspondence and spherical EIS requirements at FR2, LG Electronics France
In ad hoc meeting on spherical coverage (R4-1811522) for EIS the following proposal was agreed:
  Proposal 1 from R4-1811023: EIS requirements for each power class shall be specified at the same statistically specified direction as EIRP, in addition to peak direction.

## Slide 3: Way Forward
For single band, the spherical coverage requirements for EIS is defined based on the spherical coverage requirement for EIRP
  The %-ile for which spherical EIS is defined will be the same as that for EIRP for each power class
    E.g., 50%-ile will be defined for PC3
  The difference between peak EIS and spherical coverage EIS will be the same as the one specified for EIRP
    E.g., for n257, the 50%-ile EIS will be 10.9dB higher than peak EIS