## Slide 1: EN-DC RX Requirements
Qualcomm, Inc.
3GPP TSG-RAN WG4#88Bis Meeting R4-1813355
Chengdu, China, 8 – 12 October 2018
Agenda 7.6.12

## Slide 2: Outline
General
EN-DC Inter-band
EN-DC Intra-band Contiguous
EN-DC Inter-band Non-contiguous

## Slide 3: General
Test Waveform:
  Use DFT-s-OFDM QPSK waveform since REFSENS tests are based on this waveform.
  Blocking tests all relative to some value above REFSENS which uses DFT-s-OFDM QPSK
  Common to both LTE and NR
Sub-Carrier Spacing:
  Use SCS=15KHz and 30KHz
  Minimum guard band for available BW’s.
AMPR:
  AMPR=0dB for worst case since reduction of TX power of Pc_max – 7dB for 2UL

## Slide 4: EN_DC Inter-band (2UL)
Pc-max -7dB for 2 TX
Wanted signal adjusted in RX tests due to MSD
  MSD due to IMD product falls in self RX band
  MSD due to harmonic mixing with mandatory simultaneous RX/TX.
  MSD due to cross band noise
  How are RX Blocker tests affected and are the stand alone specs sufficient?
Sub-block in NR band
  ACS/IBB spec for 1 sub-block in NR band(s) –> Use Jammer BW = CCBW
  ACS/IBB spec for 1 contiguous CA sub-block in NR band(s) -> Use Jammer BW = [min(CCBW’s)]
  OBB spec for NR and/or NR_CA band applies
Sub-block in Re-farmed bands
  ACS/IBB/OBB specs apply for re-farmed bands with 5M jammer
  Sub-block in LTE bands
  ACS/IBB/OBB specs apply for LTE with 5M jammer
Sub-block in FR2 band
  FR2 ACS/IBB/OBB specs apply

## Slide 5: EN_DC Intra-band Contiguous (2UL)
EN_DC class AA, CA, DA, B
ACS is ratio of [jammer level] to [ aggregated power of LTE CC and NR CC ]
  Simplification table shown below
Specify ACS1 Jammer and ACS2/IBB/OBB wanted levels for each EN_DC contiguous class AA, CA, DA, B.
Jammer BW set to 5M for both LTE and NR for all BW class since LTE and NR in the same band or re-farmed band.
Pc_max – 7dB for TX power (RXBN effect)
UL configuration
  Need configuration for larger NR bandwidths to avoid RXBN for FDD cases.
  Any non-contiguous allocation for self RX protection will adjust the wanted signal for blocking tests via MSD or ΔR
Specify OBB range similar to LTE frequency range offsets
EN-DC Class | AggBW | Jammer BW | ACS1 dB | ACS2 sig, dBm | ACS2 dBm | ∆IBB sig | IBB1 dBm | IBB2 dbm | ∆OBB sig
AA | 60M-120M | 5M | 19.2 | -42.7 +10log(Nc/Nagg) | -25 | 16.8 | -56 | -44 | 9
CA | 80M-140M | 5M | 18.5 | -42.0 +10log(Nc/Nagg) | -25 | 17.5 | -56 | -44 | 9
DA | 100M-160M | 5M | 17.9 | -41.4 +10log(Nc/Nagg) | -25 | 18.0 | -56 | -44 | 9
B | 10M-20M | 5M | 27 | -50.5+10log(Nc/Nagg) | -25 | 9.0 | -56 | -44 | 9
NOTE 1: ACS1 tested with REFSENS+14dB per CC NOTE 2: ∆IBB and ∆OBB are added to REFSENS per CC NOTE 3: Jammer BW is the minimum CCBW in the Bandwidth Class NOTE 4: Jammer BW’s apply to ACS BW and IBB BW |  |  |  |  |  |  |  |  | 

## Slide 6: EN_DC Intra-band non-Contiguous (2 UL)
EN_DC Intra-band non-Contiguous
EN_DC Class A_A, C_A, D_A
Pc_max – 7dB for TX power (RXBN effect)
ΔRLTE , ΔR NRVs Wgap needs to be specified for FDD cases due to RXBN and TX IM2 and TX IMD effect for
  Values will vary with duplex spacing and NR bandwidth
  Table is example only
  Or do we use MSD based on UL configuration??
Specify ACS1 and ACS2/IBB/OBB wanted levels for each LTE non-CA/CA sub-block and NR sub-block
  Jammer BW = 5M for both LTE sub-block with 1 or more CC’s and NR sub-block
  Re-farmed ACS/IBB specs apply for NR sub-block
  LTE non-CA, LTE-CA ACS/IBB specs apply for LTE sub-block
Specify OBB range similar to LTE since only re-farmed bands are used for EN-DC non-contiguous
For ACS/IBB blocker in gap, no ACS/IBB test when Wgap < 2(Fint)-BWch = 15MHz
No Wide band intermodulation in Gap
DC configuration | Aggregated channel bandwidth (LTE+NR) | Wgap / (MHz) | UL LTE allocation | UL NR allocation | ΔRIBNC_LTE (dB) | ΔRIBNC_NR (dB) | Duplex mode
DC_3A_n3A | 5MHz+5MHz | 45.0 < Wgap ≤ 65.0 | 121 | 121 | 4.7 | 4.7 | FDD
 |  | 0.0 < Wgap ≤ 45.0 | 251 | 251 | 0 | 0 | 
 | 5MHz+10MHz | 40.0 < Wgap ≤ 60.0 | 121 | 121 | 3.8 | 3.8 | 
 |  | 0.0 < Wgap ≤ 40.0 | 251 | 251 | 0 | 0 | 
 | 20MHz+20MHz | 0.0 < Wgap ≤ 35.0 | 167 | 167 | 4.1 | 4.1 | 
 | 20MHz+25MHz | 0.0 < Wgap ≤ 30.0 | 167 | 167 | 3.8 | 3.8 | 
 | 20MHz+30MHz | 0.0 < Wgap ≤ 25.0 | 167 | 167 | 3.6 | 3.6 | 
NOTE 1: 1 refers to the UL resource blocks shall be located as close as possible to the downlink operating band but confined within the transmission. NOTE 2: Wgap is the sub-block gap between the two sub-blocks. NOTE 4: All combinations of channel bandwidths defined in Table 5.3B.1.3-1. NOTE 5: 5 refers to the UL resource blocks shall be located at RBstart=25. NOTE 6: 6 refers to the UL resource blocks shall be located at RBstart=35. NOTE 7: 7 refers to the UL resource blocks shall be located at RBstart=50. |  |  |  |  |  |  |