## Slide 1: Further agreements on NR PRACH demodulation – Remaining issues agreed via email
Ericsson, […]
R4-1815366
Document for: Approval
3GPP TSG-RAN WG4 RAN#89
Spokane, USA, 12 – 16 November, 2018
Agenda: 7.13.2.4

## Slide 2: Background
The following WFs were approved:
  R4-1811728, WF on NR PRACH demodulation requirements, RAN4#88
  R4-1813757, WF on NR PRACH demodulation, RAN4#88b

## Slide 3: Background: from R4-1813757 - Timing Offset
Reuse LTE timing offset sequence for format 0
  Timing offset start value:
    50% of Ncs
  Increased within the loop, adding 0.1us in each step (up to 0.9us)
  Then loop is reset and restart again.
Timing offset shall be scaled according to SCS and format
  To be further investigated, Email discussion. Deadline: Oct 26th
Tolerance on timing offset error should be further investigated for next meeting.
  Option1: Scaling according to SCS
  Other option is not precluded
  Email discussion. Deadline: Oct 26th

## Slide 4: Timing offset
For preambles with short sequence:
  Set the timing offset base value as 0
  This offset is increased within the loop, by adding in each step a value of 0.1us, until the end of the tested range, which is 0.8us.
  Then the loop is being reset and the timing offset is set again to 0us.

## Slide 5: Time estimation error tolerance
PRACH Preamble | PRACH SCS | PUSCH/PUCCH CP duration (normal CP) | PRACH signal time resolution | Proposed time error tolerance for AWGN | Proposed time error tolerance for TDL channel
Long sequence | 1.25kHz | 144/(15*10^3*2048) *10^6=4.69us | 0.95 us | 1.04 us | 1.04 us + 1.51 us = 2.55 us
Short sequence | 15kHz | 144/(15*10^3*2048) *10^6=4.69us for 15kHz SCS PUSCH 144/(30*10^3*2048) *10^6=2.34us for 30kHz SCS PUSCH | 0.48 us | 0.52 us | 0.52 us + 1.51 us = 2.03 us
 | 30kHz |  | 0.24 us | 0.26 us | 0.26 us + 1.51 us = 1.77 us
 | 60kHz | 144/(60*10^3*2048) *10^6=1.17us for 60kHz SCS PUSCH 144/(120*10^3*2048) *10^6=0.59us for 120kHz SCS PUSCH | 0.12 us | 0.13 us | 0.13 us + 0.15 us = 0.28 us
 | 120kHz |  | 0.06 us | 0.07 us | 0.07us + 0.15 us = 0.22us