## Slide 1: Updated simulation assumptions for Rel-15 NB-IoT WUS
Ericsson
3GPP TSG-RAN WG4 Meeting #89 R4-1816056
Spokane, US, 12 – 16 November 2018
Agenda Item: 6.4.4.1

## Slide 2: WUS simulation assumptions for Rel-15 NB-IoT (1/2)
Parameter | Value
BS TX antenna configuration | 1 Tx, 2 Tx with transmit diversity, Note: Tx diversity scheme will depend on RAN1 agreements
UE Rx antenna configuration | 1 Rx
WUS BW | 180 kHz
Channel model | EPA 1Hz, ETU 1 Hz
SNR | -6 dB, -12 dB
False alarm rate | 1%
Detection probability | 99%
Combining | Option 1: No coherent combining over multiple subframes; Option 2: Coherent combining of 2 consecutive WUS subframes
Precoders | precoders alternate every 2 WUS subframes for 2 Tx based WUS transmissions

## Slide 3: WUS simulation assumptions for Rel-15 NB-IoT (2/2)
DRX cycle (s) | Frequency drift [Hz] | Timing drift [us]
1.28 | 170.8 | 4.0960e-08
2.56 | 311.6 | 1.6348e-07
5.12 | 593.2 | 6.5536e-07
10.24 | 1156.4 | 2.6212e-06