## Slide 1: WF for NR PUSCH demodulation
R4-1900097
Document for: Approval
3GPP TSG-RAN WG4 RAN#90
Athens, Greece, 25th Feb – 1st Mar, 2019
Agenda: 6.14.2.2
Nokia, Nokia Shanghai Bell, […]

## Slide 2: Background
The following WFs were approved:
  R4-1808024, WF on NR PUSCH demodulation requirements in Rel-15, RAN4#87
  R4-1809366, WF on NR PUSCH demodulation requirements, RAN4#AH1807
  R4-1811694, WF on NR PUSCH demodulation requirements, RAN4#88
  R4-1813942, WF on NR PUSCH demodulation requirements, RAN4#88bis
  R4-1816347, WF on NR PUSCH demodulation requirements, RAN4#89

## Slide 3: UCI on PUSCH
UCI Test case settings
  Follow CP-OFDM PUSCH test case as far as possible.
  One UCI test case for FR1 and one UCI test case for FR2.
  CSI only payload of 7 bits (part1=5bits, part2=2bits) and UL-SCH.
  Testing metric to be 2% BLER of the UCI.
Simulation alignment
  SCS/BW combinations as in PUSCH.
  UL/CL allocation as in PUSCH.

## Slide 4: Applicability Rule - SCS/BW
Text for applicability rules concerning SCS and BW declarations.
  “All declared SCS’ shall be tested. For each SCS, the BS shall test at least the highest CBW, which has been declared in combination with the tested SCS. In the case that the largest CBW declared in combination with the test SCS is not in the subset of SCS/CBW combinations with specified performance requirements, the BS shall be tested on the nearest smaller CBW (i.e., reference BW) in the set of SCS/CBW, where tests are specified. The reference BW shall be placed in the middle of the original CBW during the test. The performance metrics (e.g., 70% max throughput) shall be calculated according to the specified test FRC”.

## Slide 5: Application Rule - General
Make text proposals that introduce testing flexibility.
  Option 1: Introduce manufacturer test case configuration declaration.
  Option 2: Declare specific requirements as optional.
  Other options not precluded

## Slide 6: Simulation Assumptions, UCI over PUSCH
Parameter |  | Value | 
 |  | FR1 | FR2
General System | Transform precoding | Disabled | Disabled
 | Number of Tx | 1 | 1
 | Number of Rx | 2 | 2
 | Number of layers | 1 | 1
 | [Uplink-downlink allocation for TDD] | 30 kHz SCS: 7D1S2U, S=6D:4G:4U | 120kHz SCS: 3D1S1U, S=10D:2G:2U
 | Code block group based PUSCH transmission | Disabled | Disabled
 | MCS index | [16] | [16]
 | Propagation Condition | [MCS 16: TDL-C 300ns, 100 Hz] | [MCS 16: TDL-A 30ns, 300Hz]
HARQ |  | Off | Off
DMRS | DMRS configuration type | 1 | 1
 | Maximum number of OFDM symbols for front loaded DMRS | 1 | 1
 | Number of additional DMRS symbols | 0 | 0
 | Number of DMRS CDM group(s) without data | 2 | 2
 | EPRE ratio of PUSCH to DMRS | -3 dB | -3 dB
 | DMRS port | 0 | 0
 | DMRS sequence generation | NID=0, nSCID =0 | NID=0, nSCID =0
Time domain resource | PUSCH mapping type | A | B
 | PUSCH starting symbol index | 0 | 2
 | PUSCH symbol length | 14 | 10
Frequency domain resource | Carrier frequency (GHz) | 4 | 30
 | SCS and BW | 30kHz: 40 MHz | 120kHz: 100 MHz
 | RB assignment | Full applicable test bandwidth | Full applicable test bandwidth
 | Frequency hopping | Disabled | Disabled
PTRS configuration | Frequency density (KPT-RS) | no PTRS | 2
 | Time density (LPT-RS) | no PTRS | 1
UCI | UL-SCH | yes | yes
 | Payload (bits) | 7 (CSI only, part1=5, part2=2) | 7 (CSI only, part1=5, part2=2)
 | uci-on-pusch-scaling | f0p5 | f0p5
 | I^CSI-1 and I^CSI-2 | 13 (default) | 13 (default)
Test metric |  | SNR@ 2% BLER | SNR@ 2% BLER

## Slide 7: Test Parameters, CP-OFDM
Parameter | value | 
 | FR1 | FR2
Transform precoding | Disabled | Disabled
Number of Tx | 1, 2 | 1, 2
Number of Rx | 2, 4, 8 | 2
Number of layers | 1, 2 | 1, 2
Transmission scheme | Identity matrix (TPMI index 0) | Identity matrix (TPMI index 0)
DMRS type | type 1 | type 1
Number of DMRS symbols | 1, 1+1 | 1
symbols length | 14 | 10
start symbol index | 0 | 0
Time domain resource allocation type | type A | type B
Frequency domain resource | Full applicable test bandwidth | Full applicable test bandwidth
MCS index | 2, 16, 20 (20 only for 1Tx) | 2, 16, 20 (20 only for 1Tx)
Carrier frequency (GHz) | 4 | 30
Propagation condition | MCS 2: TDL-B 100ns, 400 Hz MCS 16: TDL-C 300ns, 100 Hz MCS 20: TDL-A 30ns, 10Hz | MCS 2: TDL-A 30ns, 300Hz MCS 16: TDL-A 30ns, 300Hz MCS 20: TDL-A 30ns, 75Hz
SCS and BW | 15kHz: 5MHz, 10MHz, 20MHz; 30kHz: 10MHz, 20MHz, 40MHz, 100MHz 60kHz(FR2): 50MHz, 100MHz; 120kHz: 50MHz, 100MHz, 200MHz | 
PTRS | Not configured | Configured with KPTRS =2, LPTRS =1
Timing offset | 0 | 0
Frequency offset | 0 | 0
Code block group, Frequency hopping, Limited buffer rate matching | Disabled | Disabled
Number of HARQ transmissions | 4 | 4
Testing metric | SNR @70% of maximum throughput | SNR @70% of maximum throughput

## Slide 8: Test Parameters, DFT-s-OFDM
Parameter | value | 
 | FR1 | FR2
Transform precoding | enabled | enabled
Number of Tx | 1 | 1
Number of Rx | 2, 4, 8 | 2
Number of layers | 1 | 1
DMRS type | type 1 | type 1
Number of DMRS symbols | 1+1, 1 | 1
symbols length | 14 | 10
start symbol index | 0 | 0
Time domain resource allocation type | type A | type B
Frequency domain resource | 15kHz: 25 PRB; 30kHz: 24 PRB (middle of test BW) | 60kHz: 30 PRB; 120kHz: 30 PRB (middle of test BW)
MCS index | 2 | 2
Carrier frequency (GHz) | 4 | 30
Propagation condition | MCS 2: TDL-B 100ns, 400 Hz MCS 16: TDL-C 300ns, 100 Hz MCS 20: TDL-A 30ns, 10Hz | MCS 2: TDL-A 30ns, 300Hz MCS 16: TDL-A 30ns, 300Hz MCS 20: TDL-A 30ns, 75Hz
SCS and BW | 15kHz: 5 MHz; 30kHz: 10 MHz | 60kHz: 50; 120kHz: 50
PTRS | Not configured | NRB0=0, NRB1=8, NRB2=NRB3=32, and NRB4=108
Timing offset | 0 | 0
Frequency offset | 0 | 0
Code block group, Frequency hopping, Limited buffer rate matching | Disabled | Disabled
Number of HARQ transmissions | 4 | 4
Testing metric | SNR @70% of maximum throughput | SNR @70% of maximum throughput