## Slide 1: Way Forward on UE Timing Adjustment
Ericsson, Mediatek, Qualcomm
3GPP TSG-RAN WG4 Meeting # 90
Athens, Greece, February 25-March 01, 2019
Agenda: 6.12.6.1
R4-1902047

## Slide 2: Background
Receive beam change:
  The UE may adjust its receive beam autonomously or in response to change in the active TCI state:
Active TCI state change:
  The active TCI state can be changed by gNB via DCI or via MAC command:
    active TCI state for PDSCH via DCI (section 5.1.5, TS 38.214) and
    active TCI state for PDCCH via MAC (section 10.1, TS 38.213) .
  Each TCI state is associated with SSB i.e. QCL with SSB.

## Slide 3: Way Forward on Beam Switch
Specify rules for UE transmit timing adjustment when UE switches its RX beam autonomously or in response to the active TCI state change in gNodeB.
Discussion:
  Upon RX beam switch or active TCI state change the UE shall adjust its transmit timing as follows:
    Option 1: timing adjustment in one shot if the magnitude of the change in the downlink timing (T) at the UE between the old and new beam is greater than Te i.e. gradual timing adjustment shall NOT be applied.
    Option 2: gradual timing adjustment if T is less than or equal to threshold (H) but greater than Te; otherwise one shot timing adjustment (i.e. if  T> H).
    Requirement will be based on one of the above two options:
      RAN4 decision will be based on BS and UE impact, complexity and implementation.
  Other solutions are not precluded.
  It is FFS whether the beam switch will cause any interruption.
  FFS whether one shot timing adjustment is in the same or opposite direction of DL timing change.
Conditions/scenarios:
  The above requirements are specified under the following assumptions:
    The UL channel on which transmit timing is being adjusted is QCL’d to the same RS on which the DL channel timing is being tracked and
    The old and target beam’s SSB Es/Iot is FFS.