## Slide 1: WF on Rel-16 Improvement of A-MPR for B41/n41 EN-DC
Sprint
R4-1902494
3GPP TSG-RAN WG4 #90 Meeting
Athens, Greece, 25th Feb. – 01st March, 2019

## Slide 2: Background
Rel-15 A-MPR is structured around these principles
Two curves, for IM3s falling into -13 and -25 dBm/MHz regions of SEM
  Relate aggregate allocation size to backoff
  Derived from measurements made with certain assumptions, including 2PAs
  Specify backoff, equally applied to each RAT
Frequency Domain formulas, based on channel locations, to determine which curve applies.
PCMAX definition allows “trading” between LTE and NR power so long as total power limit is met

## Slide 3: Potential Improvements
Enhancements to curve selection
Selection based on actual RB allocations, rather than channels [1]
3rd curve for case where IM3s are not overlapping spectral regrowth [2]
Identification of cases where all IM3s fall inside the LTE or NR channels (No A-MPR)

## Slide 4: Potential Improvements (cont.)
Investigate Potential Enhancements to power trading
May be possible to define rules to trade power and allow higher NR powers than what is currently allowed by the constant total back-off approach, especially at low LTE power
NR must take backoff based on given LTE power
  R-IM3 power on each side of channel pair is dominated by mixing at Tx on that same side
  R-IM3 power sensitivity to own Tx PA power changes is very different from sensitivity to external signal changes. [3]
UE could consider which side problematic IM3 is on (LTE or NR side) and trade power accordingly

## Slide 5: Potential Improvements (cont.)
Assumptions for measurements have large impact on A_MPR allowance
Existing assumptions for measurements result in very large, unrealistic, A-MPR allowances. Rel-15 allows up to 15 dB of backoff, which would effectively preclude deployment if really needed.
Real devices nearing deployment need far less A-MPR because of better antenna isolation and PA linearity.
Investigate Refining Assumptions for PA operating Modes
Need to consider what PA operating modes are realistic for intra-band EN-DC measurements, given the impact of backoff to coverage
Could PA biasing be assumed to exceed minimum ACLR spec (-31 dBc)?
Investigate Refining Assumptions on Antenna Isolation
10 dB isolation assumption was based on lower frequency. Could assumption for measurements be increased?

## Slide 6: Potential Improvements (cont.)
New Capability Signaling for Improved UE capabilities
Optional support for High Linearity PAs
Optional support for High Antenna Isolation
Could allow reduced A-MPR allowances for UEs that signal capability
Other Potential Improvements
Consideration of waveform difference, DFT vs. CP-OFDM
Other Potential improvements are not precluded.

## Slide 7: Agreed Way Forward
Companies agree to bring proposals for improving B41/n41 EN-DC A-MPR for Rel-16 considering the following mechanisms, and consider their applicability to other bands and to generic MPR:
Improving Curve selection by introducing a third curve, and considering the case where IM3s fall entirely inside channels
Enhancing Power Trading mechanisms, including UE considering side of IM3 of concern (LTE or NR)
In addition, companies are encouraged to study the following mechanisms, and consider their applicability:
Consideration of waveform (DFT vs. CP-OFDM) of transmission on side (LTE or NR) of IM3 of concern
Reconsidering appropriate PA operating points for 2PA intra-band EN-DC
Reconsidering appropriate antenna isolation for 2PA intra-band EN-DC
New Capabilities signaling that allow UE to signal support for high PA linearity, and high antenna isolation, with new specifications for A-MPR allowances based on those.
Other potential improvements are not precluded.

## Slide 8: References
[1] R4-1901854 Draft CR for 38.101-3: Clarification of NS_04 allocation bandwidth, Sprint
[2] R4-1901929 Additional A-MPR curve for B41/n41 EN-DC , Sprint
[3] R4-1901930 R-IM3 Sensitivity to LTE and NR Powers in B41/n41 EN-DC , Sprint