## Slide 1: Way forward on RRM enhancement for HST
Qualcomm Inc, ...
3GPP TSG-RAN WG4 Meeting #90-Bis Xi’an, China, 8 – 12 April, 2019
R4-1904804
Document for: Approval

## Slide 2: WF for Pcell cell reselection and identification requirement
Cell detection/identification requirement for DRX 1.28s
  Option 1(Huawei): 6 DRX cycle when DRX cycle is 1.28s.
  Option 2(Intel): keep original requirement (10 DRX cycle)
Cell detection/identification requirement for DRX 2.56s
  Option 1(Huawei): remove requirement for DRX
  Option 2(CMCC): keep requirement for DRX 2.56s

## Slide 3: WF for Scell measurement requirement
 | activated Scell meas | deactivated Scell no common DRX (in measCycleSCell) | deactivated Scell common DRX (take max between no common DRX and below DRX value)
Option 1(CMCC, Ericsson, NTT DOCOMO, QC) | same as Pcell | identify: 10 meas: 3 | same as Pcell with HST enhancement
Option 2 (Intel, Ericsson) | same as Pcell | Investigate the need to add sf40 and/or sf80 to measCycleScell or revisit multiplication factor to give equivalent performance of sf40/sf80 with one of the existing deactivated SCEll measurement cycles | Investigate the need to add sf40 and/or sf80 to measCycleScell or revisit multiplication factor to give equivalent performance of sf40/sf80 with one of the existing deactivated SCEll measurement cycles

## Slide 4: WF for UL Timing
Option 1(Ericsson): maximum adjustment step size (Tq) shall be increased to 7 Ts to support UE speeds up to 500 km/h for bandwidth equal to or larger than 5 MHz
Option 2(Intel, QC): maximum adjustment step size (Tq) shall be increased to 5 Ts to support UE speeds up to 500 km/h for bandwidth equal to or larger than 10 MHz
Option 3(Huawei): maximum adjustment step size (Tq) shall be increased to 5.5 Ts to support UE speeds up to 500 km/h for bandwidth equal to or larger than 10 MHz
Agreement: For HST, Tq number
  The current Tq has to be increased at least for the case when bandwidth is larger than 10MHz.
  The concrete number needs more discussion.
  For smaller bandwidth, FFS

## Slide 5: WF for RLM monitoring
Option 1(Intel): A new signaling will be introduced for UE to indicate network that it is going to be out-of-sync if PDCCH block error rate is above Qout,E1
Option 2(QC, Ericsson): Do not introduce new signaling

## Slide 6: WF for Capability and Configuration Signaling
HST CA capability and configuration signaling will be decided in next meeting
  Option 1: Apply existing highSpeedEnhancedMeasFlag to the Scell
  Option 2: Introduce new UE capability and flag for supporting enhanced RRM on SCC
Capability and configuration signaling for Rel.16 new requirements targeting higher speed will be decided in next meeting
Other changes/options are not precluded