## Slide 1: WF on handling of LTE anchor agnostic
NTT DOCOMO, INC.
R4-1904993
3GPP TSG RAN WG4 Meeting #90bis
Xian, China, 8th– 12th April, 2019

## Slide 2: Background
According to LS from RAN5[1], from perspective of conformance test, RAN5 evaluation indicate that LTE anchor agnostic may not be applied to following two test cases, and it may be required to test all EN-DC combinations (LTE 1 band + NR FR1 1 band) in these cases, although there are no exceptional requirement in TS 38.101-3.
  6.5B.3.3.1 General spurious emissions (Inter-band EN-DC within FR1)
    IM interference by dual uplink impact (R5-190975)
  7.3B.2.3 Reference sensitivity (Inter-band EN-DC within FR1)
    Impact of Interference from “LTE UL -> NR DL” and “NR UL -> LTE DL” (R5-190976)
    Not only exceptional cases (e.g. MSD, IM) but also non-exceptional cases impact
There is a concern about the amount of testing time when testing all EN-DC combination of LTE 1 band + NR 1 band.
Some companies do not believe that the above testing is needed since anchor agnostic verification is sufficient. Other companies do believe that the testing is needed.

## Slide 3: Way forward
RAN4 should study how to reduce the amount of testing time while verifying core requirements of general spurious emission in 2UL case, and REFSENS in 1UL/2DL case(either of LTE and NR is set to minimum output power) for inter-band EN-DC within FR1 until RAN4#91.
  For general spurious:
    Option1: Test one of each EN-DC combinations of 1NR band + 1 LTE low band, Mid band, and High band, per NR bands.
      Further study which EN-DC combinations should be chosen to verify the requirements.
      Only test frequencies where 2nd and 3rd IMD falling into.
    Option2: Test one 1 LTE band + 1 NR band EN-DC combinations per NR bands
      Further study which EN-DC combinations should be chosen to verify the requirements.
        One possible way is to choose randomly.
      Only test frequencies where 2nd and 3rd IMD falling into.
    Option3: Only test EN-DC combinations that 2nd and 3rd IMD falling into own uplink bands
    Other options are not precluded.
  For REFSENS:
    Option1: Basically test all EN-DC of 1LTE band + 1 NR band but study how to reduce test time.
      For example:
        Not test if LTE CA consisting of corresponding bands is already tested
          Ex) Not test 1A_n3A if already 1A_3A is tested.
        Not test “LTE Tx to LTE Rx” in LTE SA if “LTE Tx to LTE Rx” is tested in 1UL/2DL EN-DC.
        Not test “NR Tx to NR Rx” in EN-DC mode if UE support NR FR1 SA.
    Option2: same as option1
    Option3: same as option2 in general spurious emission.
      Test certain EN-DC 1LTE band + 1 NR band combinations if interference issue are identified
 | Low band | Mid band | High band
UL operating band | <1 GHz | =>1GHz and =<2.2GHz | >2.2GHz

## Slide 4: Reference
[1] R4-1900020, “LS on applicability of LTE anchor agnostic to specific RF test cases”, NTT DOCOMO, INC., RAN#90.