## Slide 1: WF on PC2 EN-DC (1 LTE TDD band + 1 NR TDD band)
CMCC, vivo, OPPO, CATT
3GPP TSG-RAN WG4 Meeting #90-bis R4-1905001
Xi’an, China, 8 – 12 April, 2019

## Slide 2: Background
In RAN#82 meeting, WID on Power Class 2 UE for EN-DC (1 LTE TDD band +1 NR TDD band) were approved [1]. The objective of the work item is to specify the RF requirements for Power Class 2 EN-DC (1 LTE band +1 NR band with 1Tx).
RAN4 need to specify UE Tx duty cycle requirements sufficient to prevent exceeding local regulatory limits such as SAR for inter-band PC2 EN-DC UE.
The following inter-band EN-DC were approved to support PC2 HPUE for 5G NR:
EN-DC configuration | Uplink EN-DC configuration
DC_39A-n41A | DC_39A-n41A
DC_39A-n79A | DC_39A-n79A
DC_41A-n79A | DC_41A-n79A

## Slide 3: Agreements for PC2 EN-DC Combination (LTE TDD PC3+NR TDD PC3)
As network based solution, at least the following is proposed.
  Introducing a new signaling which indicates that the NR maxUplinkDutyCycle capability corresponds to LTE UL/DL configuration and it is a per band combination capability
  The NR maxUplinkDutyCycle capability for PC2 inter-band EN-DC is optional.
    The UE behaviour is FFS if NR maxUplinkDutyCycle capability for PC2 inter-band EN-DC is absent
  It is assumed that the UE follows the UL grant regardless of duty-cycle indication (but can account for the indication)
  The values range of NR maxUplinkDutyCycle for PC2 inter-band EN-DC are from [20]% to 100% and the default value for NR uplink duty cycle can be specified according to different TDD configurations as following
UE based solution is FFS. Also solution to combine network and UE based solution will be FFS
LTE UL/DL Configuration (Uplink duty cycle) | 0 (60%) | 1 (40%) | 2 (20%) | 3 (30%) | 4 (20%) | 5 (10%) | 6 (50%)
Default value for NR maxUplinkDutyCycle (10% as granularity) | [40]% | [60]% | [80]% | [70]% | [80]% | [90]% | [50]%

## Slide 4: References
[1] RP-182877 New WID on Power Class 2 UE for EN-DC (1 LTE band +1 NR band). CMCC
[2] R4-1903024 SAR requirements for PC2 EN-DC (1 LTE TDD band + 1 NR TDD band). CMCC
[3] R4-1900468 Discussion on SAR requirement for EN-DC PC2 UE. CATT
[4] R4-1900257 Discussion on TDD inter-band NSA HPUE. OPPO
[5] R4-1903245 Further discussion on SAR requirement for EN-DC PC2 UE. CATT
[6] R4-1903054 Discussion on TDD inter-band NSA HPUE SAR. OPPO
[7] R4-1904660 Discussion on maximum duty cycle for TDD EN-DC HPUE. vivo