## Slide 1: WF on BS study for 7 -24 GHz
R4-1905242
Ericsson, Huawei

## Slide 2: General
The WF contains a very brief summary of discussions and suggested actions for each topic
The discussion summaries should not be understood as conclusions; they are purely intended as indications of views expressed at RAN4#90bis
The recommended actions are not intended to be restrictive; further contribution not suggested in the WF is welcomed.

## Slide 3: WF on BS Study for 7-24 GHz
The following topics were discussed at RAN4#90bis. For each topic, a summary of discussion and recommendation for contribution at RAN4#91 is presented.
BS classes
Discussion:
  In principle, the current set of BS classes can be supported, i.e. Wide Area, Medium Range, Local Area
  Possibly the more powerful BS classes may be restricted depending on spectrum scenario (need and ability to supress emissions, etc)
Action
  Discuss further potential output power and array size for each BS class

## Slide 4: BS types
Discussion:
  -C type seems unlikely to be needed for WA; may be needed for smaller BS classes
  -O type seems likely to be needed
  Whether –H type is needed should be considered further
    IF –H and –O are included, then the work to develop requirements is greater due to the need to develop and relate both conducted and OTA requirements
  Initial assessment of conducted testing is that it is feasible up to around 10-12 GHz
Action:
  Contribute further on feasibility and complexity and cost of conducted testing, and the drivers/need for –H requirements

## Slide 5: PA behaviour and considerations
Discussion:
  There may be a technology breakpoint somewhere around 10-12 GHz
  The feasibility and benefit of linearization should be considered, taking into account bandwidth, array of transmitters etc.
  Potential output power, efficiency and ACLR can be estimated
Action:
  Contribute on PA trends in terms of achievable power, efficiency, ACLR
  Discuss on the potential for linearization
  Contribute and discuss what to capture in the TR on PA behaviour

## Slide 6: Phase noise
Discussion:
  A contribution on general trends in phase noise was presented. It was commented that opinions on phase noise modelling differ
  VCO-noise only, or phase noise at a single frequency offset frequency should not be considered to directly represent phase noise impact to EVM performance
  In addition to scientific publications, commercially available components give an indication on achievable performance
  Study should not consider only oscillators with purely silicon-technology based resonators, but other implementations should be also considered
Action:
  Contribute on assumptions on phase noise trends and expected levels
  Contribute on whether PT-RS is expected to be needed to deal with phase noise (and assumed for signal quality assessments)
  Contribute on what is important to capture in the TR on phase noise

## Slide 7: RX requirements
Discussion:
  FR1 RX requirements have fixed sensitivity and interferer levels adapted by an estimated element/module gain.
  FR2 has declared reference sensitivity and interferers related to that. There is a need to consider which approach could be applicable.
  The out of band blocking requirement level has a discontinuity within this range; further consideration is needed on how to handle that.
  Estimates of noise figure at example frequencies was presented
Action:
  Contribute further on noise figure drivers and estimates
  Contribute further on concept for RX requirements
  Contribute further on how to handle OOB blocking discontinuity

## Slide 8: Co-location
Discussion:
  Initial analysis suggested TX IMD semes not needed; co-location emissions possibly
  Measurement of co-location requirements is not obvious
Action:
  Contribute on the need for co-location requirements (i.e. Expected isolation between BS within this range and also to existing FR1, FR2)
  Contribute on the testability of co-location

## Slide 9: RF filtering
Discussion:
  Some first estimates of RF filter performance were presented
  There is no need to quantify OOB emissions levels
  Consideration may be needed of level of integration, impact on output power, feasibility to sufficiently suppress emissions of high power BS
Action
  Contribute further on filter technology capabilities, including performance, loss, integration possibilities

## Slide 10: EMC requirements
Discussion:
  Initial analysis of the EMC Emission requirements was presented, observing that in case of OTA AAS BS architecture, the Radiated Emission requirements would be captured by the BS RF specification under the RF Radiated Spurious Emission requirement.
  Initial analysis of the EMC Immunity requirements was presented, observing that most requirements are transparent to the BS frequency range and/or BS architecture, except for the Radiated Immunity (RI) requirement. In case of RI, the testing frequency range is specified by IEC up to 6 GHz, only.
Action:
  According to 7-24GHz SI work-plan approved during RAN4#90, provide the EMC conclusions on EMC Emission and Immunity requirements during the RAN4#91 meeting in May.

## Slide 11: Other
It is sufficient to consider single-band operation only for the study item phase
Further discussion is needed on how to capture impact to BS requirements
  How technology considerations relate to BS requirements
  What can be concluded in the SI, what more work is needed in the WI
There is a need to clarify what is meant with FR1, FR2 and ”extension” of a frequency range, both within the BS context and more widely
TDD OFF power was not discussed. FR1 and FR2 have different approaches and for FR2, testability is a challenge.
Action:
Contribute on:
  What is understood in BS terms to be included/not included in ”extensions” of existing FR
  How TDD OFF power requirement may be designed and tested
  How to organize the information on BS requirements in the spec.