## Slide 1: Way forward on LTE HST UE demodulation simulation assumptions
Intel Corporation
3GPP TSG-RAN WG4 #91 Meeting Reno, U.S.A., 13 – 17 May, 2019
R4-1907746
Document for: Approval

## Slide 2: Background
In RAN4#90bis, a WF (R4-1904832) was approved.
An agreement was made to prioritize the following scenario:
Priority 1: TM3 under bi-directional channel with cap on Doppler shift
(Qualcomm, NTT DOCOMO, CMCC, Intel, MTK)
Note 1: This agreement does not exclude work on unidirectional scenario as Priority 2.
Note 2: This agreement does not exclude work on DMRS-based transmission mode.
In this WF, the specific simulation assumptions are provided based on Rel.14 HST-SFN channel model.

## Slide 3: Simulation assumptions for bi-directional HST-SFN channel (R.16)
Parameter | Unit | Test 1
Downlink power allocation ρA | dB | -3
Downlink power allocation ρB | dB | -3 (Note 1)
Downlink power allocation σ | dB | 0
Noc at antenna port | dBm/15kHz | -98
PDSCH transmission mode |  | 3
Bandwidth | MHz | 10 (50 RBs)
Duplex mode |  | FDD
Allocated PDCCH symbols |  | 2
MCS |  | [13] for subframes 1,2,3,4,6,7,8,9; N/A for subframes 0,5
Antenna configuration |  | 2x2
Channel condition |  | 4-path bi-directional HST-SFN (R.16)
Note 1: PB = 1 Note 2: The requirement defined is based on the normalized channel model, i.e. the power of each tap is normalized to the instantaneous total received power from four taps. |  | 
4-path bi-directional HST-SFN (R.16) | 
Parameter | Value
Ds | 1000m
Dmin | 50m
v | 500km/h
Max Doppler fd | 972Hz
For MIMO layer, tentatively refer to R.87 FDD in TS36.101.
The simulation parameters in the tables are for information only.
Interested companies are encouraged to use these parameters and provide PDSCH demodulation simulation results for alignment in RAN4#92 Meeting.
Interested companies can provide simulation results for 4Rx, whether to introduce 4Rx test is FFS.

## Slide 4
Parameter | Unit | Test 1
Downlink power allocation ρA | dB | -3
Downlink power allocation ρB | dB | -3 (Note 1)
Downlink power allocation σ | dB | 0
Noc at antenna port | dBm/15kHz | -98
PDSCH transmission mode |  | 3
Uplink-Downlink Configuration |  | 1
Special Subframe Configuration |  | 4
Bandwidth | MHz | 10 (50 RBs)
Duplex mode |  | TDD
Allocated PDCCH symbols |  | 2
MCS |  | [13] for subframes 1,4,6,9; N/A for subframes 0,5
Antenna configuration |  | 2x2
Channel condition |  | 4-path bi-directional HST-SFN (R.16)
Note 1: PB = 1 Note 2: The requirement defined is based on the normalized channel model, i.e. the power of each tap is normalized to the instantaneous total received power from four taps. |  | 
4-path bi-directional HST-SFN (R.16) | 
Parameter | Value
Ds | 1000m
Dmin | 50m
v | 500km/h
Max Doppler fd | 972Hz
For MIMO layer, tentatively refer to R.87 TDD in TS36.101.
The simulation parameters in the tables are for information only.
Interested companies are encouraged to use these parameters and provide PDSCH demodulation simulation results for alignment in RAN4#92 Meeting.
Interested companies can provide simulation results for 4Rx, whether to introduce 4Rx test is FFS.