## Slide 1: WF on basket WID adding legacy Channel BW to existing NR bands
Ericsson, Huawei, …
3GPP TSG-RAN WG4 Meeting #92bis R4-1912984
Chongqing, China, October 14-18 2019

## Slide 2: Background
New basket WI [1] was proposed at last RAN#85 to manage all requests related to adding channel bandwidth support to NR existing bands.
It was then agreed to further discuss and details the scope, way of working, … in following RAN4 meetings.
[2], [3], [4] and [5] elaborate on this new basket WI.

## Slide 3: Scope
Channel bandwidths in: {5 MHz, 10 MHz, 15 MHz, 20 MHz, 25 MHz, 30 MHz, 40 MHz, 50 MHz, 60 MHz, 70 MHz, 80 MHz, 90 MHz, 100 MHz}
Existing NR bands only.
  Including SDL and SUL BUT:
    No CA combination is updated, this shall be addressed via CA basket WI.

## Slide 4: Out of scope
New NR bands (including LTE re-farmed bands)
Channel bandwidths not in: {5 MHz, 10 MHz, 15 MHz, 20 MHz, 25 MHz, 30 MHz, 40 MHz, 50 MHz, 60 MHz, 70 MHz, 80 MHz, 90 MHz, 100 MHz}
New CA and/or EN/DC combinations.

## Slide 5: Way of working
New request (4 supporters) should be submitted with enough spectrum information to justify the request:
  On RAN4 reflector at least 2 weeks before RAN4 meeting.
  Technical challenge shall be flagged (e.g. Specific channel BW)
Basket WID is updated with the new requests and submitted to RAN4 for endorsement (spectrum information and technical challenge should be identified/discussed), and then to RAN for approval.
Work ongoing: At least check or define emissions requirements, MPR (relative BW) and A-MPR, Refsens and any other RF requirement that is needed for the new bandwidth for the specific band.
Interested companies will write all draft CRs to complete one request in same RAN4 meeting
If all draft CRs for one request are endorsed, basket WI Rapporteur will merge them with other endorsed draft CRs for other request(s) in big CRs to the corresponding TSs.
Those big CRs will be sent on RAN4 email reflector for approval (1 week).
If approved, they will be sent to RAN for approval.
Band | Channel bandwidth and SCS | Contact name, company | Contact email | Other supporting companies | Spectrum information | Technical Challenge | status

## Slide 6: Way of working

## Slide 7: Release independant - Support
Addition of channel BW is release independant:
  Support is FFS for the Release of introduction.
    To be clarified in RAN4#93.
    FFS if the request for additional channel BW is coming very late (2 meetings before the current Release deadline).
  Support is optional for earlier releases.
  Support is mandatory for the following releases.

## Slide 8: Reference
RP-192011, New basket WID adding new CBW support in existing NR bands, Ericsson
R4-1910866, Discussion on basket WI for adding new channel bandwidth(s) support to existing NR bands, Huawei
R4-1911519, Views on adding new Channel Bandwidths for NR bands, Apple
R4-1912486, Addition of new bandwidths: mandatory vs. optional, Qualcomm
R4-1912388, New basket WID – adding wider CBW to existing bands, Ericsson