## Slide 1: Way forward on NR mobility enhancement
Intel
3GPP TSG-RAN4 Meeting #93
Reno, USA, 18 – 22 November, 2019
R4-1913436
Document for: Approval

## Slide 2: Agreements on DAPS HO interruption in D1
Interruption for intra-frequency HO with BWsource ≥ BWtarget:
  Option 1:
  Side condition: power imbalance between the two cells should be within X dB. X is FFS
    Option 2:
    Side condition: power imbalance between the two cells should be within X dB. X is FFS
RAN4 assumes PRACH resource is contained in the configured BWP in target cell.
FFS on the interruption requirement when the relationship between CBW of target and source cell is different the relationship between BWP of target and source cell.
 | NR Slot length (ms) | Interruption length X (slotsnote 1)
0 | 1 | [1]
1 | 0.5 | [2]
2 | 0.25 Note 2 | [4]
Note 1: The same SCS of source cell and target cell is assumed. Note 2: Both source cell and target cell are on FR1. |  | 
 | NR Slot length (ms) | Interruption length X (slotsnote 1)
0 | 1 | [1]
1 | 0.5 | [1]
2 | 0.25 Note 2 | [2]
Note 1: The same SCS of source cell and target cell is assumed. Note 2: Both source cell and target cell are on FR1. |  | 

## Slide 3
Definition of delay (2):
Starting point: D2 starts at the time UE receives the indication of source cell release. D2 is the same as NR PSCell release delay.
Ending point: when the UE accomplish the release actions specified in TS 38.331
Interruption on the target cell during delay (2):
For BWsource = BWtarget
  Interruption length is same as that in delay (1).
  Side condition: power imbalance between the two cells should be within X dB. X is FFS
For BWsource > BWtarget
  2ms
  Side condition: power imbalance between the two cells should be within X dB. X is FFS
From handover command until the source cell is successfully released (during the whole handover procedure), UE is not allowed to cause any other interruption except for the ones defined in delay (1) and (2).
Note: in case simultaneous UL Tx is not supported, UE is allowed to cause more interruption to the source cell if UL transmissions of source and target cell overlap in time.
Agreements on DAPS HO

## Slide 4: Agreement on conditional handover
Handover delay is no more than:
DCHO = TRRC_1 + Tmeasure + TRRC_2 + Tinterrupt
Where:
TRRC_1 is defined the same as existing processing time for RRC reconfiguration message containing CHO configuration
Interruption during CHO:
Tinterrupt = TIU + Tprocessing+ T∆ ms
Where TIU , Tprocessing and T∆ are defined same as legacy handover.
TRRC_2: Second segment of RRC processing time, starts after UE realizes the condition is met and identity of target cell is determined. During TRRC_2 UE is allowed to finish associated operations earlier and leave the source cell.
Tmeasure is specified by:
  reusing event triggered reporting requirements. (i.e. referring to corresponding requirement in TS38.133 clause 9)

## Slide 5: Way forward
Companies are encouraged to provided analysis on:
Interruption in DAPS HO D1 to down select from option 1 and option 2 in slide 2.
Power imbalance between the source and target cells in DAPS intra-frequency HO side condition.
TRRC_2 in conditional handover
Conclusion on issues above will be made in RAN4#94.