## Slide 1: WF on NR IAB RRM
Qualcomm, AT&T, NOKIA, CMCC
3GPP TSG-RAN WG4 Meeting #93 Reno, Nevada, Nov 18th – 22nd, 2019
R4-1915798

## Slide 2: Background - I
RAN4 already agreed to the following during this and the previous meeting.
Requirements | Comments | Is requirement needed?
Cell reselection | Intra-frequency Inter-frequency | No
Handover |  | FFS
RRC Connection Mobility Control | RRC re-establishment Random access RRC release with redirection | Yes
SCell activation/deactivation delays |  | No
Interruptions related to SCells addition, release, activation, deactivation | Interruptions on serving cells due to any of the addition, release, activation, or deactivation procedures | No
PSCell addition/release delays |  | No
Active BWP switching | Interruptions at active BWP switching Active BWP switching delay | No
TCI switching | TCI switching delay | FFS

## Slide 3: Background - II
RAN4 already agreed to the following during this and the previous meeting.
Requirements | Comments | Is requirement needed?
RLM | Requirements for RLM, e.g., based on SSB, CSI-RS or both | FFS
Link recovery procedures | Requirements for SSB-based and CSI-RS based BFD and CBD | FFS
Measurements requirements (time duration, number of cells, etc.) |  | FFS
Measurement accuracy requirements |  | FFS
MT timing related requirements | MT transmit timing (Te and Tq) Timing Advance | Yes
 | MRTD MTTD | Yes if carrier aggregation band combinations are introduced
Switching time between MT and DU | --- | TBD in RAN4 RF session
DU timing related requirements | 3 us requirement | Yes
 |  | FFS
 | T_delta command | 

## Slide 4: Background - III
IAB network planning depends very much on defining some minimum RRM requirements for the IAB MTs. Without RRM requirements it is not possible for an operator to plan for an IAB network.
Ensuring inter-operability among different IAB nodes is very important to guarantee the performance of an IAB network. Inter-operability can be achieved by defining RRM requirements for IAB nodes.
FR2 is the main use case for Rel-16 IAB networks. Defining RLM, BFD and CBD related requirements is essential to guarantee performance in FR2 IAB network.
Reference: R4-1909929, Defining RRM requirements for IAB nodes.

## Slide 5: Way Forward - I
RAN4 agrees to define IAB RRM requirements based on the following table.
Requirements | Comments | Is requirement needed?
Cell reselection | Intra-frequency Inter-frequency | No (already agreed)
Handover |  | No
RRC Connection Mobility Control | RRC re-establishment Random access RRC release with redirection | Yes (already agreed)
SCell activation/deactivation delays |  | No (already agreed)
Interruptions related to SCells addition, release, activation, deactivation | Interruptions on serving cells due to any of the addition, release, activation, or deactivation procedures | No (already agreed)
PSCell addition/release delays |  | No (already agreed)
Active BWP switching | Interruptions at active BWP switching Active BWP switching delay | No (already agreed)
TCI switching | TCI switching delay | No

## Slide 6: Way Forward - II
RAN4 agrees to define IAB RRM requirements based on the following table.
Requirements | Comments | Is requirement needed?
RLM | Requirements for SSB based and CSI-RS based RLM evaluation period | Yes for no-DRX mode
Link recovery procedures | Requirements for SSB-based and CSI-RS based BFD and CBD evaluation period | Yes for no-DRX mode
Measurements requirements (time duration, number of cells, etc.) |  | No
Measurement accuracy requirements |  | No
MT timing related requirements | MT transmit timing (Te and Tq) Timing Advance | Yes (already agreed)
 | MRTD MTTD | Yes if carrier aggregation band combinations are introduced (already agreed)
Switching time between MT and DU | --- | TBD in RAN4 RF session (already agreed)
DU timing related requirements | 3 us requirement | Yes (already agreed)
 |  | No
 | T_delta command | 

## Slide 7: Way Forward - III
The specific duration of evaluation periods of SSB and CSI-RS based RLM, BFD and CBD for an IAB MT are FFS.