## Slide 1: WF on RRM measurement relaxation for Power Saving
CATT
3GPP TSG-RAN WG4 Meeting #93 R4-1915845
Reno, USA, 18 - 22 Nov 2019

## Slide 2: WF on RRM measurement relaxation
For information: Scenarios
  #1: Low mobility scenario
  #2: Not in cell-edge scenario
  #3: Low-mobility + Not in cell-edge scenario
RRM measurement relaxation methods for UE power saving in RRC_idle/inactive state
  Option 1: Allow RRM measurements with longer intervals
  Option 2: Reuse LTE MTC/NB-IoT RRM measurement relaxation for neighbour cell monitoring
    Note: modifications are not precluded

## Slide 3: WF on RRM measurement relaxation
Applicability of RRM relaxation methods when the relaxation criteria are fulfilled
 | Applicable RRM relaxation methods
Scenarios #1 | Option 1
Scenarios #2 | Option 1
Scenarios #3 | Option 2

## Slide 4: Agreements in on-line session

## Slide 5: WF on RRM measurement relaxation
RRM measurement relaxation for inter-frequency carrier with higher priority
  RAN4 to study how to relax the requirement for inter-frequency carrier with higher priority if NW configure relaxation command
  RRM measurement relaxation by reducing the number of frequency layer to be measured is FFS
  RAN4 to study EMR impact on power saving mode in next meeting
  RAN4 to study the RRM impact, e.g. timeline of DCI based BWP switch, due to cross-slot scheduling power saving technique