## Slide 1: 3GPP TSG-RAN WG4 Meeting #93 Reno, USA, November 18 -22, 2019
Ericsson, Nokia, Nokia Shanghai Bell, Qualcomm Incorporated, Huawei, HiSilicon
Way forward on Rel-16 MTC RRM enhancement
R4-1915889

## Slide 2: Wake-up signal
Based on the Rel-16 WUS contributions provided to RAN4#92bis meeting, following options are identified:
  Option 1: : Rel-15 WUS reception requirements apply for Rel-16 UE.
  Option 2: Required number of repetitions for WUS reception with 1 tx antenna when DRX cycle length is ≤ 1.28 s is increased from 32 to 64. Others can be kept unchanged.
It is agreed to use option 1 for release 16 WUS, i.e. release 15 reception requirements are reused.

## Slide 3: Preconfigured UL resource
When TA is obtained in RRC_IDLE mode, the values of M and N are derived as follows:
    Normal coverage
      min(480, NxDRX cycle)
    Enhanced coverage
      min(800, NxDRX cycle)
  Where N is the relaxation factor N given by Table 4.6.2.1A-1 and Table 4.6.2.3A-1 for normal and enhanced coverage respectively.
UE should make the first and second measurements available within this time range

## Slide 4: Summary of accuracy proposals for BL UEs
Es/Iot [dB] | Nokia | Ericsson | Huawei | Qualcomm | Averaged value
≥ -6 |  3.5 dB |  4 dB |  - dB |  5.5 dB |  [4.5] dB
≥ -12 dB |  5 dB |  4 dB |  7 dB |  5.5 dB |  [5.5] dB
-15 <= Es/Iot <= -12 dB |  7.5 dB |  5 dB |  8 dB |  6 dB | [6.5] dB
The accuracy values are are including RF margin

## Slide 5: Summary of accuracy proposals for non-BL UEs
The accuracy values are are including RF margin
Es/Iot [dB] | Nokia | Ericsson | Qualcomm | Intel | Averaged value
≥ -6 |  3 dB |  4 dB |  4 dB |  3.2 dB |  [3.5] dB
≥ -12 dB |  4.5 dB |  4 dB |  4.5 dB |  4.5 dB |  [4.5] dB
-15 <= Es/Iot <= -12 dB |  6.5 dB |  5 dB |  6 dB |  6.4 dB |  [6.0] dB

## Slide 6: Mobility enhancement: RSS based RSRP measurement for BL UEs
Improved measurement accuracy requirements for RSRP based on RSS is defined based:
  [3] samples in normal coverage
  [5] samples in enhanced coverage
Whether RRM requirements are defined for RSS based RRM measurements for neighbour cells in RRC_CONNECTED state is FFS due to impact on existing gaps and existing measurement requirements.

## Slide 7: MPDCCH performance improvement for RLM
  RLM core requirements, i.e., TS36.133 7.19, can be applicable for UE category M1 configured with improved MPDCCH.
  RAN4 discuss the SNR test points of RLM Qin/Qout with improved MPDCCH in RRM performance part.

## Slide 8: DL quality reporting
For 2-bit DL quality report mapping
  MPDCCH Aggregation level is assumed to be 24.
  Wait for RAN2 decision on whether 3 or 4 values can be reported
For the DL quality report accuracy
When RL is reported, i.e., MPDCCH AL=24

## Slide 9: DL quality reporting
For the DL quality report accuracy
  When RL is reported, i.e., MPDCCH AL=24,
    For FFS in Note 2:
      Option 1: -6 ≤ Ês/Iot (No upper limit)
      Option 2: -6 ≤ Ês/Iot ≤ [3] dB
  When AL is reported, i.e., MPDCCH RL=1,
    For FFS in the conditions,
      Option 1: Ês/Iot >= -6 dB
      Option 2: Ês/Iot >= [3] dB
NPDCCH Repetition | Pm-Dsg (%) | Conditions
R (Note 1) | ≤1 | -6 ≤ Ês/Iot (Note 2)
R/[4] | >1 | -6 ≤ Ês/Iot (Note 2)
R | ≤1 | -15 ≤ Ês/Iot ≤ -6 dB
R/[8] | >1 | -15 ≤ Ês/Iot ≤ -6 dB
Note 1: R is the reported MPDCCH repetition level that UE has reported. Note 2: FFS whether to set the upper limit, e.g. 3dB. |  | 
NPDCCH Repetition | Pm-Dsg (%) | Conditions
Lk (Note 1) | ≤1 | FFS
Lk-[2] | >1 | FFS
Note 1: is the reported AL level where is the index to the AL set . |  | 
NPDCCH Repetition | Pm-Dsg (%) | Conditions
Lk (Note 1) | ≤1 | FFS
Lk-[2] | >1 | FFS