## Slide 1: 3GPP TSG-RAN WG4 Meeting #93 Reno, US, 18- 22 Nov, 2019 Agenda item: 9.17.2.3.2
Samsung
Way forward on NR HST PRACH demodulation requirement
R4-1915871
Document for: Approval

## Slide 2: Background
The following WFs were approved:
  R4-1910128 WF on NR BS HST demodulation requirements , RAN4#92
  R4-1912729 WF on NR HST BS PRACH demodulation requirements, RAN4#92b

## Slide 3: PRACH Format
PRACH format
  For 500km/h velocity, use PRACH format A2/B4/C2
  For 500km/h velocity, no extra requirements for PRACH format 0
    Common understanding: PRACH format 0 with 2334Hz also shows UE with 500km/h at 1.9GHz can be supported

## Slide 4: Frequency offset
Frequency offset under AWGN for PRACH format 0 for 350km/h
  Restricted set Type A
    High-mobility scenario: 1340Hz
    Low- mobility scenario: 625Hz
  Restricted set Type B
    High-mobility scenario: 2334Hz
    Low-mobility scenario: 625Hz
Frequency offset under AWGN for PRACH formats with short sequence length targeting 500km/h
  Align with PUSCH maximum Doppler shift

## Slide 5: Test Preamble Parameters
Format 0
  Restricted set type A
    {Ncs, logical sequence index, V} ={15, 384,0}
      Common understanding: For restricted set type A, under high Doppler more than 1340Hz other preambles than the tested one may deviate in performance
  Restricted set type B
    {Ncs, logical sequence index, V} ={15, 30,30}
Short sequence format
  15 KHz
    {Ncs, logical sequence index, V} ={23, 0, 0}
  30 KHz
    {Ncs, logical sequence index, V} ={46, 0, 0}

## Slide 6: Test Preamble Parameters
Timing error tolerance for AWGN and TDLC 300-100
  Reuse the time error tolerance for corresponding NR PRACH normal performance requirements, i.e.
Format | Scs | AWGN | TDLC300-100
0 | 1.25 | 1.04us | 2.55us
A2,B4,C2 | 15 | 0.52us | 2.03us
 | 30 | 0.26us | 1.77us

## Slide 7: Simulation Results
Interested companies are encouraged to provide the ideal and impairment simulation results in the next meeting for NR HST PRACH requirement