## Slide 1: WF on switching time for IAB
Qualcomm
3GPP TSG-RAN WG4 Meeting #93 Reno, Nevada, Nov 18th – 22nd, 2019
R4-1916004

## Slide 2: Background - I
RAN plenary agreed to the following in the work item document of IAB for NR [1]
  Define RRM core requirements for both backhaul and access links of IAB node.
  Define latency requirements for switching between communication over parent backhaul link (i.e. MT) and child backhaul/access links (i.e. DU).
  Define timing requirements for IAB specific network synchronization. This may include (a) requirement for “case 1” timing (e.g. accuracy of DL transmission timing alignment between an IAB-node and its parent node), and (b) cell phase synchronization accuracy for multi-hop IAB network.

## Slide 3: Background - II
Requirements | Comments | Is requirement needed?
RLM | Requirements for RLM, e.g., based on SSB, CSI-RS or both | FFS
Link recovery procedures | Requirements for SSB-based and CSI-RS based BFD and CBD | FFS
Measurements requirements (time duration, number of cells, etc.) |  | FFS
Measurement accuracy requirements |  | FFS
MT timing related requirements | MT transmit timing (Te and Tq) Timing Advance | Yes
 | MRTD MTTD | FFS
Switching time between MT and DU | --- | TBD in RAN4 RF session
DU timing related requirements | 3 us requirement | Yes
 |  | FFS
 | T_delta command | 
RAN4 RRM session agreed to the following
[1] R4-1914985, MT-DU switching time in an IAB node, Qualcomm.

## Slide 4: Background - III
MT to DU | DL Tx | UL Rx
DL Rx |  | 
UL Tx |  | 
DU to MT | DL Rx | UL Tx
DL Tx |  | 
UL Rx |  | 
  RAN1 agreed to the following in the last meeting:
  A parent IAB node can be made aware of the number of symbols Ng the child IAB node would like the parent IAB node not to use at the edge (beginning or end) of a slot when there is a transition between child MT and child DU. Separately or additionally, the child IAB node can be made aware of the number of guard symbols that the parent IAB node will provide.
  Ng can be provided for each of the [8] possible transitions with potential overlap:
  If Ng is not provided it is assumed to be 0
  NOTE: this agreement does not introduce any performance requirement on IAB nodes.
By next meeting, RAN1 will decide the maximum gap symbols to be 3 or 7.
[1] R4-1914985, MT-DU switching time in an IAB node, Qualcomm.

## Slide 5: Background - IV
Case 1: IAB-MT DL RX to IAB-DU DL TX | Overlapping exists. 1 symbol will be impact which results in at least 6us gap left for switching
Case 2: IAB-MT DL RX to IAB-DU UL RX | No issue for switching with ‘X’ symbol
Case 3: IAB-MT UL TX to IAB-DU DL TX | TA offset of UL TX at least 7us for switching
Case 4: IAB-MT UL TX to IAB-DU UL RX | TA offset of UL TX at least 7us for switching
Case 5: IAB-DU DL TX to IAB-MT DL RX | MT reception delay due to propagation time may not sufficient for switching. Further study needed.
Case 6: IAB-DU DL TX to IAB-MT UL TX | Further study needed to check how many ‘X’ symbol needed
Case 7: IAB-DU UL RX to IAB-MT DL RX | Propagation delay may not guarantee switching.
Case 8: IAB-DU UL RX to IAB-MT UL TX | Overlapping exists. In addition, puncture 1 symbol seems not sufficient.
[2] presented following analysis of latency for switching between MT and DU in an IAB network based on some assumptions.
[2] R4-1913338, Switching time between IAB-MT and IAB-DU, Samsung.

## Slide 6: Necessity of Defining Requirements
According to RAN1 agreement, when child IAB MT informs its parent regarding the number of symbols that it needs in transition period, the parent can disregard that information.
  Child IAB will have to drop some symbols of its DU so that it can switch from MT to DU.
  If child IAB drops too many symbols, it will impact overall performance.
  If we don’t define any requirement, it’s not possible to guarantee performance
Testing latency for switching between RX to TX, RX to RX and TX to RX may be difficult.
Testing latency for switching between TX to TX may be relatively easier.

## Slide 7: Proposal
Decision to define latency requirement for switching between MT TX and DU TX will be finalized in the next meeting.
  Companies are requested to provide required latency values for switching in the next meeting.