## Slide 1: WF on UE RF requirements for band n259
Ericsson
R4-1916054
3GPP TSG-RAN WG4 #93
Reno, USA, 18 – 22 November, 2019

## Slide 2: UE single band spherical coverage Min EIRP at 50 %-tile CDF
 | UE single band spherical coverage Min EIRP at 50 %-tile CDF
Apple | 4.8 dBm
Sony, Ericsson | 6.1 dBm
MediaTek | 6 dBm
Huawei | 6.1 dBm
Average value | 5.8 dBm

## Slide 3: UE single-band min EIS at 50 %-tile CDF
 | UE single-band min EIS at 50 %-tile CDF
Apple | -71.4 dBm/50MHz
Sony, Ericsson | -72.1 dBm/50MHz
MediaTek | -72 dBm/50MHz
Huawei | -72.1 dBm/50MHz
Average value | -71.9 dBm/50MHz

## Slide 4: Way forward
Based on the averaging method, inputs [1]-[4], the following is proposed:
UE single band spherical coverage Min EIRP at 50 %-tile CDF : 5.8 dBm
UE single-band min EIS at 50 %-tile CDF : -71.9 dBm/50MHz

## Slide 5: Multiband framework for band n259
Option 1 (default): To define multiband relaxation factor for each ”supported bands with n259”, respectively
Option 2: Remove multiband relaxation for Rel-16
Option 3: To define an upper limit per band for Multiband relaxation
Way forward:
companies are encouraged to continue the discussions and provide inputs to the next meeting on preferred option.

## Slide 6: Non band specific requirements for band n259
Regarding the requirements where the objective band is not mentioned (e.g. occupied bandwidth, rx squrious), existing requirements are applied to n259 respectively.

## Slide 7: References
[1] R4-1913545, Derivation of spherical coverage EIRP and EIS for band n259, Apple, RAN4 #93
[2] R4-1915044, Spherical coverage and multi-band relaxation for n259, Sony, Ericsson, RAN4 #93
[3] R4-1913665, n259 PC3 single-band spherical coverage requirement, MediaTek, RAN4 #93
[4] R4-1915353, UE RF requirements for n259 , Huawei, Hisilicon, RAN4 #93