## Slide 1: WF on CSI-RS based L3 measurement capability and requirements
OPPO, [ … ]
3GPP TSG-RAN4 Meeting #94e-bis
Electronic Meeting, 20th – 30th April 2020
R4-2005357

## Slide 2: WF on assumption and applicability
Agreement
  Requirements shall be defined when CSI-RS is configured with an associated SSB.
    No requirements in Rel-16 for the case associatedSSB is not configured for CSI-RS
Measurement capabilities per MO or per layer
  Option 1: per frequency layer
    Option 1a (CATT, Nokia): a frequency layer is identical to an MO
    Option 1b (ZTE, Apple): One or multiple MOs can be one frequency layer.
  Option 2: per MO
    A frequency layer is identical to an MO
  Option 3: Measurement capabilities per MO or per layer are the same, since single MO is configured per frequency layer,
    CSI-RS resources in the same MO should have the same center frequency, SCS and CP type.

## Slide 3: WF on number of frequency layers to be monitored
Agreement:
  The total number of carrier UE shall be capable of monitoring at least 13 effective carrier frequency layers
CSI-RS based NR inter-frequency layers
  Option 1 (MediaTek, OPPO, Qualcomm, CATT, Apple, Huawei):
    UE shall be able to measure at least 7 NR frequency layers in total, including SSB frequency layers and CSI-RS frequency layers.
  Option 2 (CMCC):
    UE shall be able to measure at least [3] CSI-RS frequency layers.
    UE shall be able to measure at least 8 NR frequency layers in total, including SSB frequency layers and CSI-RS frequency layers.
  Option 3 (ZTE):
    UE shall be able to measure at least [7] CSI-RS frequency layers

## Slide 4: WF on number of cells to be monitored
Option 1 (MediaTek, OPPO, Qualcomm, Nokia): Shared capability for CSI-RS&SSB
  Number of monitored cells is determined by the UE capability based on SSB based measurements.
Option 2(Huawei, CATT, CMCC): Separated capability for CSI-RS
  Option 2a (Huawei):
    Re-use the SSB requirements for CSI-RS on number of cells UE shall monitor per layer.
  Option 2b (CMCC):
    For each intra-frequency layer, UE is capable of measuring [8] CSI-RS cell;
    For each inter-frequency layer, UE is capable of measuring [4] CSI-RS cell.
Option 3(ZTE): Capabilities for CSI-RS only and CSI-RS&SSB
  UE shall be capable of performing CSI-RS based measurements for at least [8] identified cells in FR1 for intra frequency measurement and at least [4] identified cells in FR1 for inter frequency measurement, at least [6] identified cells in FR2 for intra frequency measurement and at least [4] identified cells in FR2 for inter frequency measurement.
  UE shall be capable of performing SSB and CSI-RS based measurements for at least [12] identified cells in FR1 for intra frequency measurement and at least [6] identified cells in FR1 for inter frequency measurement.
  UE shall be capable of performing CSI-RS based measurements for at least [9] identified cells in FR2 for intra frequency measurement and at least [6] identified cells in FR2 for inter frequency measurement.

## Slide 5: WF on number of CSI-RS resource/beams to be monitored
Option 1(CATT, Huawei): UE shall monitor at least 32 CSI-RS resources per frequency layer
Option 2(ZTE): Define different UE capability for different scenarios, and number of CSI-RS resources shall be monitored by UE,
  [24] CSI-RS resources for intra frequency measurements in FR1
  [48] CSI-RS resources for intra frequency measurements in FR2,
  [16] CSI-RS resources for inter frequency measurements in FR1,
  [24] CSI-RS resources for inter frequency measurements in FR2.
Option 3 (MTK,OPPO, Apple): Requirements defined the same requirements as those for SSB
  If network configures more CSI-RS resources in an MO than the UE measurement capability, the UE behavior is undefined.
  For FR1, 14 and 7 CSI-RS resources for intra-f and inter-f, respectively.
  For FR2, 24 and 10 CSI-RS resources for intra- and inter-frequency, respectively and at least 1 CSI-RS resources per cell.
Option 4 (CMCC, Huawei)：
  For each intra-frequency layer, the number of CSI-RS resource is proposed to be [32].
  For each inter-frequency layer, the number of CSI-RS resource is proposed to be [24].
Do not preclude other options (Quaclomm)

## Slide 6: WF on UE capability to indicate maximum CSI-RS resources in a slot per MO
Option 1(Huawei, MTK, OPPO): Introduce UE capability to indicate the maximum number of CSI-RS resources per MO in a slot.
Option 2(ZTE): Not to define UE capability to indicate maximum CSI-RS resources in a slot per MO.
Option 3(Qualcomm, Apple, Huawei): The total number of CSI resources that UE can monitor per slot should come from the UE capability maxNumberCSI-RS-RRM-RS-SINR.
  FFS how to split up

## Slide 7: WF on UE buffering and processing capability
Option 1: Introduce UE capability on the minimum separation between two slots with CSI-RS resources.
Option 2: Not to introduce UE capability on the minimum separation between two slots with CSI-RS resources.

## Slide 8: WF on CSI-RS resources configurations
Agreement:
  Introduce restrictions about time-domain scheduling for CSI-RS resources
FFS the maximum number of CSI-RS resources periodicities configured per intra-frequency and inter-frequency MO
FFS how to introduce CMTC
  Option 1(Apple):Introduce CSI-RS Measurement Timing Configuration (CMTC).
    All CSI-RS resources for L3 meaurement should be configured within CMTC window
    CMTC window duration: considering CSI-RS periodicity is up to [40]ms, the CMTC window should be less than [5] ms.
    Up to [2] CMTC periodicities can be configured per CSI-RS intra-frequency layer
    Up to [1] CMTC periodicity can be configured per CSI-RS inter-frequency layer
FFS whether to introduce CMTC in Rel-16

## Slide 9: WF on measurement requirements for Case 1 if associatedSSB is not configured for CSI-RS
Option 1 (MTK, Apple, Intel, Huawei, Qualcomm, Nokia, OPPO, CATT, ZTE):
  No requirements in Rel-16.
Option 2 (DOCOMO, CMCC):
  the requirement needs at least consider the CSI-RS measurement time, if associatedSSB is not configured, assuming UE shall base the timing on its serving cell (indicated by refServCellIndex or PCell)

## Slide 10: WF on measurement requirements for Case 2 if associatedSSB is configured for CSI-RS
  Agreements:
  CSI-RS based cell identification can consider
    1) Cell search via SSB, 2) PBCH decoding and 3) CSI-RS measurement.
    If configured SSB fails to be detected, requirement should not be defined.
FFS: If UE already detects the SSB of the target cell and deriveSSB-IndexFromCell is indicated, PBCH decoding can be skipped.
FFS: the working assumption of single FFT window and whether to define a capability.
FFS the requirements for the cases
  If the MO includes the serving CSI-RS resource with associated SSB
  if the MO doesn’t include the serving CSI-RS resource and the CSI-RS resource associated SSB is configured
  FFS AGC adjustment time.
  FFS CSSF
  FFS scheduling restriction

## Slide 11: WF on Scaling factor for Rx beam sweeping
Agreement:
  If the CSI-RS is QCL-ed to the associated SSB, no Rx sweeping is needed only after SSB has been detected.
  If CSI-RS configured with associated SSB but not QCL-ed to the associated SSB, Rx sweeping is needed.
    FFS on the scaling factor N =8.
  For FR2, if the RX beam sweeping for QCL-ed associatedSSB is not finished, requirement should not be applied.

## Slide 12: WF on CSI-RS resources outside of DRX/MG duration
Agreement
  No UE performance requirement is defined for the CSI-RS resources that are not within DRX on-duration or measurement gap

## Slide 13: WF on requirements of Measurement Gap
More discussion based on the options as below in next meeting.
  Requirements with or w/o gaps
    Option 1 : For CSI-RS based measurement requirement, the following scenarios are prioritized to be defined in Rel-16:
      Intra-frequency measurement without gap
      Inter-frequency measurement with gap
  The principle for gap-needed or gapless
    Option 1: The UE will need GAPs for CSI-RS L3 measurements if
      The SCS of CSI-RS is different from active BWP [if UE is not capable of mixed numerology]
      The CSI-RS is not fully confined within the active BWP
      The CP of cells to be measured is different from that of active BWP (60 kHz SCS only)
    FFS : The tuning time for CSI-RS based measurements that are outside UE’s active BWP will be same as that for BWP switch.

## Slide 14: WF on Collision between L1 measurement of serving cell and CSI-RS L3 measurement of neighbour cell
FFS on collision between L1 measurement of serving cell and CSI-RS L3 measurement of neighbour cell
Option 1(LGE, MTK, OPPO, Apple):
  Do not define CSI-RS measurement requirements for the collision case.
Option 2(LGE, MTK, Qualcomm, OPPO, ZTE, Huawei):
  Network should configure L1 measurement resource to avoid collision with CSI-RS L3 measurement resource of neighbour cell.

## Slide 15: WF on Scheduling restriction
Whether to introduce the UE capability to indicate the simultaneous reception of CSI-RS of neighbour cell and SSB of serving cell
  Option 1(OPPO, CATT, MTK, Apple,Huawei, Qualcomm): New UE capability
  Option 2: Reusing SimultaneousRxDataSSB-DiffNumerology
  Option 3(MTK, ZTE): Do not consider the case mix-numerology between data/SSB of serving cell and CSI-RS of neighbour cell

## Slide 16: WF on Scheduling restriction
Option 1 (Huawei):
  If UE is not able to support mixed numerology of data and CSI-RS L3 mobility, the following scheduling restrictions apply due to intra-frequency CSI-RS based L3 measurement:
    if the associatedSSB is configured, UE is not expected to transmit or receive on 2 data OFDM symbols impacted by CSI-RS resource symbol to be measured.
    if the associatedSSB is not configured, UE is not expected to transmit or receive on the data OFDM symbol impacted by CSI-RS resource symbol to be measured, provided timing difference between the CSI-RS resource and the serving cell should be less than half CP corresponding to the SCS of the CSI-RS.
  When UE performs CSI-RS intra-frequency measurements in a TDD band, UE is not expected to transmit and receive on 2 data OFDM symbols impacted by CSI-RS resource symbol to be measured.
  Scheduling restriction shall be considered when UE performs RX beam sweeping.
Option 2 (MediaTek, DOCOMO):
  The scheduling restriction on the additional OFDM symbols before and after SSB is not needed.
Option 3 (LGE, Apple):
  Define scheduling restriction on one data symbol before and after CSI-RS symbol to be measured due to Rx beam sweeping.
  Do not define scheduling restriction if the timing difference between serving and neighbor cell including cell phase synchronization is guaranteed to be less than CP length
Donot preclude other options(Qualcomm)