## Slide 1: WF on NR-U RRM (Part 3) Agreements and topics discussed in email thread: [94e Bis][106] NR_unlic_RRM_Core_Part_3
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 Meeting #94-e-Bis R4-2005375
Electronic Meeting, April 20 – April 30, 2020
Agenda Items: 6.1.5.11 and 6.1.5.12

## Slide 2
Agreements from the 1st round
Agreements from the 2nd round
Agreements from the GoToWebinar Session

## Slide 3: Topic #1: SFTD measurements
Issue 1-2: UE behavior when reaching the maximum extension of the SFTD measurement
  UE behavior upon exceeding Tmeasure_SFTD_LBT_max: UE shall stop the search and stop performing the related measurement.

## Slide 4: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-1-1, Issue 2-1-2, Issue 2-1-3 and Issue 2-1-4:
  Define the following UE capabilities
    For RLM/BFD/CBD UE is required to monitor at least N1 candidate SSB positions from the set of SSBs that are QCLed with each other within the set of configured resources
    For intra and inter-frequency measurements UE is required to monitor at least N2 candidate SSB positions from the set of SSBs that are QCLed with each other within SMTC
      FFS for the case Q is not provided to the UE
      FFS how to handle IDLE mode capabilities
    Candidate N1 and N2 values are [1, 2, …]
    FFS whether N1 = N2
    FFS whether to have different capabilities for FBE and LBE modes
  Send LS to RAN1 to ask for feedback on candidate values N1 and N2 taking into account impact on the overall system performance
  Further discuss other cases

## Slide 5: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-2-2: Additional requirements on consecutively missing SSBs during the measurement period
  No additional requirement is specified on consecutively missing SSBs

## Slide 6: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-3-1: Lmax for the intra-frequency PSS/SSS detection period
Following values for intra-frequency:
Procedure | Rel-15 samples | Maximum number of DL LBT failures |  | 
 |  | Parameter name | Parameter value | Condition
PSS/SSS detection, no gaps | 5 | LPSS/SSS,max | 7 | Max(TDRX,TSMTC)≤40
 |  |  | 5 | 40<Max(TDRX,TSMTC)≤320
 |  |  | 3 | TDRX>320
PSS/SSS detection for deactivated SCell, no gaps | 5 | LPSS/SSS,deact,max | 7 | Max(TDRX, measCycleSCell)≤40
 |  |  | 5 | 40< Max(TDRX, measCycleSCell)≤320
 |  |  | 3 | TDRX>320
PSS/SSS detection, with gaps | 5 | LPSS/SSS,gaps,max | 7 | Max(TDRX,TSMTC, MGRP)≤40
 |  |  | 5 | 40<Max(TDRX,TSMTC, MGRP)≤320
 |  |  | 3 | TDRX>320

## Slide 7: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-3-2: Lmax for the inter-frequency PSS/SSS detection period
Following values for inter-frequency:
Procedure | Rel-15 samples | Maximum number of DL LBT failures |  | 
 |  | Parameter name | Parameter value | Condition
PSS/SSS detection, with gaps | 8 | LPSS/SSS,gaps,max | 12 | Max(TDRX,TSMTC, MGRP)≤40
 |  |  | 8 | 40<Max(TDRX,TSMTC, MGRP)≤320
 |  |  | 5 | TDRX>320

## Slide 8: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-3-3: Requirements when reaching the maximum extension of the detection period
  Upon exceeding LPSS/SSS,max, the UE is not required to meet the corresponding intra-frequency or inter-frequency PSS/SSS detection requirement.

## Slide 9: Topic #3: RSSI and CO measurements in NR-U
Issue 3-1-1: Normalization of the RSSI measurement report
  UE shall not normalize RSSI measurements for reporting purpose
Issue 3-1-2: RSSI measurement report mapping
RSSI measurement report mapping in NR-U is defined as:

## Slide 10: Topic #3: RSSI and CO measurements in NR-U
Issue 3-2-3: Need for new measurement gap patterns
  No new measurement gap pattern to be defined for RSSI Measurements in NR-U. No requirement for RMTC with duration larger than 5ms
Issue 3-3-5: Interruption
RAN4 to define interruption requirements on SCells that are deactivated when RMTC or measurement cycles are long. LTE LAA requirements in clauses 7.8.2.11 and 7.8.2.12 of TS 36.133 can be used as a starting point.

## Slide 11: Issues that need further discussion

## Slide 12
The intention of this part of the Way forward is to list the options discussed during RAN4 94e-bis. Companies are encouraged to provide input to the topics in this Section.
The issues are detailed in R4-2005390.

## Slide 13: Topic #1: SFTD measurements
Issue 1-1: Maximum scaling of inter-RAT SFTD measurements
Final candidate options:
  Option 1: k=4.
  Option 2: k =3.
Note from the moderator: No conclusion in RAN4#94e bis. Most companies compromised to k =4, but one company would agree to compromise on k =3. It is worth noting that the original proposals were k =10 and k=2. The proponents of k=10, already compromised to k=6 and now, k=4. The discussion should be continued in RAN4 #95e.

## Slide 14: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-4-1: UE behaviour in case of successively exceeding the maximum number of DL LBT failure during measurements
Candidate Options:
  Option 1 (Original): After N unsuccessful measurement attempts of an already identified cell due to exceeding the max number of unavailable SMTC occasions, UE may restart from the detection stage again. Value of N can be further discussed in RAN4.
  Option 2 : After N unsuccessful measurement attempts of an already identified cell due to exceeding the max number of unavailable SMTC occasions, UE shall stop the measurement attempts on this SSB, where N is TBD.
  Option 3: The requirements do not apply after N unsuccessful measurement attempts of an already identified cell due to exceeding the max number of unavailable SMTC occasion. N is TBD.

## Slide 15: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-5-1: Assumption of Q in PBCH reading
  Option 1: Q can be assumed to be always known to the UE
  Option 2: RAN4 to wait for ASN.1 freeze to decide on whether SSB-PositionQCL-Relationship-r16 can always be assumed known to UE

## Slide 16: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-6-1: Scheduling restriction during SS-RSRP and SS-SINR measurement
    Option 1:
    When the UE performs intra-frequency measurements in unlicensed spectrum, the following restrictions apply due to SS-RSRP or SS-SINR measurement
      The UE is not expected to transmit PUCCH/PUSCH/SRS on SSB symbols scheduled to be measured, and on 1 data symbol before each consecutive SSB symbols scheduled to be measured and 1 data symbol after each consecutive SSB symbols scheduled to be measured within SMTC window duration. If the high layer in TS 38.331 [2] signalling of smtc2 is configured, the SMTC periodicity follows smtc2; Otherwise SMTC periodicity follows smtc1.
  Note from the moderator: companies that could not support option 1 and raised concerns, please bring alternatives to this option on the next meeting, considering the comments captured in the summary.

## Slide 17: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-6-2: Scheduling restriction during SS-RSRQ
  Option 1:
    When the UE performs intra-frequency measurements in unlicensed spectrum, the following restrictions apply due to SS-RSRQ measurement
      The UE is not expected to transmit PUCCH/PUSCH/SRS on SSB symbols scheduled to be measured, RSSI measurement symbols, and on 1 data symbol before each consecutive SSB scheduled to be measured/RSSI symbols and 1 data symbol after each consecutive SSB scheduled to be measured/RSSI symbols within SMTC window duration. If the high layer signalling of smtc2 is configured(in TS 38.331 [2]), the SMTC periodicity follows smtc2; Otherwise the SMTC periodicity follows smtc1. When intra-band carrier aggregation in unlicensed spectrum is performed, the scheduling restrictions due to a given serving cell should also apply to all other serving cells in the same band on the symbols that fully or partially overlap with the aforementioned restricted symbols."
  Note from the moderator: companies that could not support option 1 and raised concerns, please bring alternatives to this option on the next meeting, considering the comments captured in the summary.

## Slide 18: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-7-1: UE behaviour in RRC_CONNECTED mode when the serving cell is unavailable for consecutive SSB bursts
Candidate options:
  Option 1: In RRC_CONNECTED mode, UE shall initiate measurements on neighbour cells indicated by the serving cell if it is unable to measure on the serving cell for at least X consecutive number of SSB bursts not available at the UE, where the value of X is TBD.
  Option 2: Don’t introduce new UE behaviors as the problem can be taken care of by existing mechanisms.

## Slide 19: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-8-1: Event Triggered reporting delay
  Modified Option 1: This measurement reporting delay excludes a delay, which is caused by no UL resources being available for UE to send the measurement report on, and all delays due to UL LBT failures until the successfull transmission of the report.”
  Option 2: For event-triggered measurement reporting, the UE measurement reporting delay is extended due to UL LBT failures until the time point of the successful reporting attempt, according to [TBD RAN2 specification]. No extension for UL channel access category 1
Option 1 seemed agreeable, however, one company asked for clarification which was not provided in the discussions. Can companies address the following in the next meeting: “…on how can we assume or implicitly require that the access is available if we want to ensure a proper operation in unlicensed spectrum? Basically, this translates into the question on how the requirement with option 1 would be tested – as reporting in a scenario without UL LBT failures?”

## Slide 20: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-8-2: Event Triggered periodic and periodic reporting delay
  Candidate Options:
    Option 1: For event-triggered periodic and periodic reporting delay, the same definition shall be adopted as in Rel-15.
    Option 2: For event-triggered and event-triggered periodic measurement reporting, the UE measurement reporting delay is extended due to UL LBT failure, until the time point of the successful reporting attempt, according to [TBD RAN2 specification]. No extension for UL channel access category 1
    Option 3: same as option 1 in issue 2-8-1
One company asked for clarification of Option 1 which was not provided in the discussions. Can companies address the following in the next meeting: “…on how can we assume or implicitly require that the access is available if we want to ensure a proper operation in unlicensed spectrum? Basically, this translates into the question on how the requirement with option 1 would be tested – as reporting in a scenario without UL LBT failures?”

## Slide 21: Topic #3: RSSI and CO measurements in NR-U
Issue 3-1-3: RSSI measurement reporting criteria
  Candidate options:
    Option 1:
      With Ecat=1, 1 report for RSSI and channel occupancy measurements is capable of minimum 1 RSSI measurement and 1 channel occupancy measurement over a channel [TS 37.213] per carrier frequency with CCA.
    Option 2:
      A RSSI/CO report consists of 1 RSSI measurement and 1 CO measurement. RSSI/CO report over multiple sub-bands requires multiple measurement objects.

## Slide 22: Topic #3: RSSI and CO measurements in NR-U
Issue 3-2-1: Intra-frequency and inter-frequency RSSI definition
Candidate options (same as last meeting):
Condition 1:
  Option 1a: RMTC configured SCS is the same as the active BWP in the serving cell.
  Option 1b: RMTC configured SCS is the same as the SCS of the serving cell SSB,
Condition 2:
  Option 2a: Measurement BW is contained within the active BWP of the serving cell
  Option 2b: The center frequency of the PRB set configured for RSSI measurement is aligned with the center frequency of an intra-frequency SSB.
Moderator: Companies are encouraged to address the concerns captured in the moderator summaries in their contributions for next meetings, and to provide their views on the need for measurement gaps for intra-frequency measurements (Issue 3-2-2).

## Slide 23: Topic #3: RSSI and CO measurements in NR-U
Issue 3-2-2: Need for measurement gaps for intra-frequency RSSI measurements
  This discussion is depends on 3-2-1. Please provide your views next meeting.
Issue 3-3-1: RSSI measurement bandwidth and assumed bandwidth for RSSI accuracy
  Option 1: RSSI measurement Bandwdith is the LBT bandwidth
  Option 2: The RSSI measurement bandwidth is less than the LBT bandwidth.

## Slide 24: Topic #3: RSSI and CO measurements in NR-U
Issue 3-3-2: RSSI measurement period
  Option 1:
    The RSSI and CO measurement periods depend on:
      max(reportInterval, rmtc-Period) in non-DRX when measurement gaps are not required,
      max(reportInterval, rmtc-Period, DRX) in DRX when measurement gaps are not required, or
      max(reportInterval, rmtc-Period, MGRP and gap sharing) in DRX when measurement gaps are required.
      The CSSF definition and how to account it in the RSSI requirements is to be further discussed
  Option 2:
    The RSSI and CO measurement period is scaled with the number of measurement objects / CSSFinter.

## Slide 25: Topic #3: RSSI and CO measurements in NR-U
Issue 3-3-4: Scheduling Restriction during intra-frequency RSSI/CO measurements
  Option 1:
    When the UE performs intra-frequency RSSI/CO measurements in unlicensed spectrum, the following restrictions apply due to RSSI/CO measurements
      The UE is not expected to transmit PUCCH/PUSCH/SRS on RSSI measurement symbols, and on 1 data symbol before each RSSI symbols and 1 data symbol after each RSSI symbols within RMTC window duration.
      When intra-band carrier aggregation in unlicensed spectrum is performed, the scheduling restrictions due to a given serving cell should also apply to all other serving cells in the same band on the symbols that fully or partially overlap with the aforementioned restricted symbols.
Moderator: there were concerns with this option in asynchronous scenarios. Please address these concerns in the next meeting.

## Slide 26: Topic #4: L1-RSRP
Issue 4-1-1: UE behavior when receiving the MAC CE deactivation command for semi-persistent CSI reporting, in case of UL LBT failure for sending the ACK
Candidate options:
  Option 1: If UE cannot transmit HARQ-ACK on MAC-CE deactivation due to UL CCA failure, UE continues to be in its previous state, i.e., it should measure and report L1-RSRP until it successfully transmits HARQ-ACK
  Option 2: For semi-persistent CSI reporting with PUCCH, if UE cannot transmit HARQ-ACK on the MAC CE deactivation due to the UL LBT failures, UE continues the L1-RSRP measurements but delay the L1-RSRP reporting. If UE does not receive deactivation command during the delay period, UE restarts to transmit L1-RSRP reporting. FFS how to extend the delay.
  Option 3: It is preferred to delay the L1-RSRP reporting when the HARQ feedback cannot be transmitted after receiving the MAC CE deactivation command. A time limit shall be defined when the L1-RSRP reporting is delayed. When exceeding the time limits, UE shall abandon the stored measurement results, where the time limit is FFS. The UE shall also abandon the measurement results when the HARQ feedback is retransmitted for the deactivation command

## Slide 27: Topic #4: L1-RSRP
Issue 4-1-2: Semi-persistent L1-RSRP reporting delay
Issue 4-1-3: Semi-persistent CSI reporting delay
Candidate options:
  Option 1: Extend the delay, how to extend the delay is FFS
  Option 2: Semi-persistent L1-RSRP reporting delay in NR-U reuses the Rel-15 reporting delay

## Slide 28: Topic #4: L1-RSRP
Issue 4-2-1: CSI-RS based L1-RSRP
  Option 1:
    Set the CSI-RS based L1-RSRP evaluation period for NR-U as follows:
Moderator: one company commented that, since CSI-RS is not designed for detection purpose, it is unclear how to determine CSI-RS is available or not. Please, address this issue in the next meeting.