## Slide 1: Way forward on NR URLLC performance requirements with Ultra-Low BLER
R4-2005526
Moderator (Ericsson)

## Slide 2: Agreements from 1st round
No slot aggregation for the ultra-low BLER requirement
CP-OFDM waveform only
UE DM-RS configuration is 1+1. Reconfirm or revise this decision in case the decision for DM-RS configuration for the slot aggregation requirement differs. BS DM-RS configuration is 1+1. Reconfirm or revise this decision in case the decision for DM-RS configuration for the slot aggregation requirement differs. These agreements apply for FR1 only.
Further investigate and confirm UE MCS. MCS13 is baseline but a different MCS could be agreed if better.
Regarding number of UE requirements: It is not of importance to agree a number; rather agree the number of different scenarios and the number of requirements will fall out. Note that currently it appears to be 4 for PDSCH plus potentially CQI, but this depends on final set of scenarios.
Regarding number of BS requirements: It is not of importance to agree a number; rather agree the number of different scenarios and the number of requirements will fall out. Note that currently 2 SCS and 2 mapping type are agreed; this number could change depending on agreements (There can be applicability rules to reduce testing of course).

## Slide 3: Agreements from 2nd round
PUSCH bandwidth and number of RB
  Same as agreed for the slot aggregation (high BLER) requirement
Value for X
  X value as [1] dB for BS requirements
  X value as [0.5] dB for UE requirements

## Slide 4: Open issues
How to capture X in the specification
  Option 1: Do not capture in specifications; include directly into core spec requirement by assuming part of IM
  Option 2: Capture as part of TT in the conformance specification
  Option 3: Do not capture in specifications, X is not part of IM.
BS TDD pattern
  Option 1: 3D1S1U (S=10:2:2) for 15 KHz, 7D1S2U (S=6:4:4) for 30 KHz
  Option 2: DSUU
Number of UE tests
  Option 1: 1
  Option 2: 2
Number of BS tests
  Option 1: 1 using applicability rule
  Option 2: 4

## Slide 5: Open issues
Create CQI requirements for ultra-low BLER
  First focused on evaluation the feasibility from test aspect and applicability rules before we decide whether introducing test cases or not.
FR2 requirements for ultra-low BLER
  Keep it open meanwhile prioritize discussion on introducing FR1 requirements in Q2; and interested companies are encouraged to bring more information and analysis for the deployment/usage scenarios in FR2 with ultra-low BLER and/or higher BLER for high reliability and low latency