## Slide 1: WF on PC2 EN-DC FDD+TDD HPUE China Unicom, CHTTL, vivo, Huawei, Xiaomi
3GPP TSG-RAN WG4 Meeting #94-e-bis R4-2005188
Electronic Meeting, Apr.20th – Apr.30th 2020

## Slide 2: Backgrounds
The scope of the WI is as following
Target on finishing this WI is in RAN#88.
The objective of this WI is to specify the standard needed for Power Class 2 (PC2) high power UE for EN-DC for 1 LTE FDD band and 1 NR TDD band (23dBm LTE + 23dBm NR and 23dBmLTE + 26dBm NR). The scope of this WI is the example band combination DC_3A_n78n. Specifically, it includes the following aspects:
Design the UE capability report signalling and facilitate SAR compliance based on the outcomes of the studies in TR 37.815
Standardize RF requirements
Evaluate any additional impact to the requirements due to the high power on UL.
Note: RAN4 needs to discuss whether existing RAN2 signalling can be reused to solve the issues in this WI. If there is RAN2 signalling impact then RAN4 will send LS to RAN2 to inform the solution. No RAN2 TUs are requested for this WI.

## Slide 3: Agreements from last meeting
Two fixed LTE reference configurations of the PC2 FDD-TDD EN-DC, DutyLTE1=70% , DutyLTE2=40% were agreed
Average of two proposed options i.e. [IMD2: 31.9 dB] ; [IMD4: 18.5dB] for DC_3A_n78 combination were agreed
The following capability set was agreed, corresponding to DutyLTE1 and DutyLTE2.
  maxNRDuty1 ∈ {30%, 40%, 50%, 60%, 70%, 80%, 90%, 100% , Full_duty_supported}
  maxNRDuty2 ∈ {30%, 40%, 50%, 60%, 70%, 80%, 90%, 100% }
  Full_duty_supported: no restriction on uplink scheduling for both LTE and NR bands for applicability of PC2 inter-band EN-DC (FDD+TDD) requirements, i.e. SAR compliance will be fulfilled by UE based mechanisms e.g. P-MPR etc. If UE indicate maxNRDuty1= Full_duty_supported, maxNRDuty2 signaling will be overridden i.e. UE will follow Full_duty_supported capability.

## Slide 4: Way Forward – Subtopic 1-3
Issues on “blind” scheme (scheme of reducing LTE FDD power)
  Option 1: Not to introduce “blind” scheme. (vivo, OPPO, Xiaomi, CU, Qualcomm, Samsung, Huawei, CHTTL, LGE)
  Option 2: Introduce a new item in UE signalling to indicate if “Reduce_FDD_power” is supported. (vivo, CHTTL)
  Option 3: When capability parameters are absent. (T-mobile)
  Option 4: Introduce the “blind” scheme as the baseline (a minimum total EN-DC power; also applies when duty-cycle capabilities are absent and in “fallback” from the duty-cycle scheme). （Ericsson, T-mobile, Vodafone)
  It is recommended to discuss the following two questions in order to facilitate the discussion in subtopic 1-3:
  - Whether the scheme of “Reduce_FDD_power” is beneficial on top of the scheme based on reporting capability?
  - The impact on supporting the "blind scheme" when the UL EN-DC scheduling exceeds the UE capability on the UE side?

## Slide 5: Way Forward – Subtopic 1-1
Choosing “default value” or “blind scheme” when capability parameters are absent
  Option1: Using default value of maxNRDuty for two cases of LTE and NR power combination (vivo, OPPO, Xiaomi, CU, Samsung, CHTTL, Huawei)
    Option 1-a: consider a conditional statement for 100% UL percentage with an upper limit of the UL power setting on the LTE side for each fixed LTE reference configuration.
  Option2: Following “blind” scheme by reduced power (PLTE) and use of the common UL-DL patterns on the TDD CG (Ericsson, T-mobile, Vodafone)
  Companies are suggested to focus on the decision between option 1 and option 2 in the first round, Option 1-a is suggested to be discussed afterwards.

## Slide 6: Way Forward – Subtopic 1-2
Choosing “PC fallback” or “blind scheme” when the UL EN-DC scheduling exceeds the UE capability
  Option1: UE should fallback to PC3 (vivo, OPPO, Xiaomi, CU, Qualcomm, Samsung, Huawei)
  Option2: “Blind” scheme should be followed (Ericsson, T-mobile, Vodafone)