## Slide 1: Way forward on PDSCH CA normal demodulation requirements
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #94-e-Bis
E-meeting, 20 April – 30 April, 2020
Agenda Item: 6.18.1.1
R4-2005546

## Slide 2: FRC for FR2 requirements
      Rank and MCS for FR2
  Rank 2 and MCS 10

## Slide 3: Requirements for TDD-FDD CA and TDD-TDD CA with different SCSs
      Pcell configuration for performance requirements
  Option 1: Reuse single carrier performance for CA, and no matter which cell is Pcell for the requirements.
  Option 2:
    For CA with different SCSs, define requirements for both 15kHz Pcell and 30kHz Pcell.
    For FDD + TDD CA with 15 kHz SCS, define requirements for both FDD 15 kHz Pcell and TDD 15 kHz Pcell
  Option 3: Decide after conclusion on “Pcell configuration for the test” will be reached
      Pcell configuration for the test
  Option 1: The test coverage can be considered fulfilled if UE passes one of scenario with one of the CC as PCell as per the real testing request
  Option 2: If Pcell in both carriers are supported, configure TDD cell as Pcell in TDD-FDD CA, configure 15 kHz SCS cell as Pcell in TDD 15+30kHz SCS CA. (scenarios with larger number of HARQ processes)
  Option 3: If Pcell in both carriers are supported, configure FDD cell as Pcell in TDD-FDD CA, configure 30 kHz SCS cell as Pcell in TDD 15+30kHz SCS CA. (scenarios with less number of HARQ processes)
  Option 4: If PCell in both carriers are supported, configure FDD 15kHz cell as PCell in FDD 15kHz + TDD 15kHz CA, configure 30kHz SCS cell as PCell in both FDD 15kHz + TDD 30kHz CA and TDD 15kHz + TDD 30kHz CA
  Option 5: If Pcell in both carriers are supported, both FDD and TDD cell should be tested as Pcell for TDD-FDD CA and configure 30 kHz SCS cell as Pcell in TDD 15+30kHz SCS CA
  Note: Companies are encouraged to check if there are UE capability signalling which allows to check whether UE supports TDD PCell or FDD PCell and whether UE supports15 kHz PCell or 30 kHz PCell

## Slide 4: Requirements for TDD-FDD CA and TDD-TDD CA with different SCSs
      HARQ process number
Performance requirements:
  Reuse single carrier FDD and TDD requirements for FDD-TDD CA and TDD CA with different SCSs
HARQ process number |  | CCs with the same duplex mode & SCS with Pcell | CCs with different duplex mode / SCS with Pcell
FDD 15 kHz + TDD 30 kHz CA | FDD PCell | 4 | 8
 | TDD PCell | 8 | 8
FDD 15 kHz + TDD 15 kHz CA | FDD PCell | 4 | 4
 | TDD PCell | 8 | 8
TDD 15 kHz + TDD 30 kHz CA | 15kHz PCell | 8 | 12 (Note 1)
 | 30kHz PCell | 8 | Option 1: 6 Option 2: 8
Note 1: FFS scheduling details: Option 1: different RTTs (10 or 20 slots) are used for different HARQ processes, and initial transmission and retransmission are scheduled on the same type of TDD slot. Option 2: initial transmission and retransmission can be scheduled on different types of TDD slot |  |  | 

## Slide 5: Test applicability rule
      Numerology in each CA duplex mode
  Test #1: FDD 15 kHz + FDD 15 kHz
  Test #2: FDD 15 kHz + TDD 30 kHz, in case UE supports different SCS on different carriers for FDD-TDD CA, otherwise FDD 15 kHz + TDD 15 kHz
  Test #3: TDD 30 kHz + TDD 30 kHz, in case UE supports it, otherwise TDD 15 kHz + TDD 30 kHz

## Slide 6: Test applicability rule
      Categorizing of CA capabilities
  Option 1: Define different capabilities for intra-band contiguous CA, intra-band non-contiguous CA and inter-band CA with different numbers of bands.
  Option 2: Define different capabilities for intra-band contiguous CA, intra-band non-contiguous CA and inter-band CA.
  Companies to bring proposals on the demod spec structure for CA, with the motivation to minimize future maintenance.
      Test of different CA capabilities
  Option 1: Test intra-band contiguous CA, intra-band non-contiguous CA and inter-band CA with the largest number of bands.
  Option 2: Test all the supported CA capabilities, including intra-band contiguous CA, intra-band non-contiguous CA and inter-band CA with different numbers of bands.

## Slide 7: Test applicability rule
      Selection of CA configuration(s) and CBW combination
  Further discuss by taking into account:
    The supportedSubCarrierSpacingDL, maxNumberMIMO-LayersPDSCH and supportedModulationOrderDL are reported for each CC and scalingFactor are reported per band for FR1 and FR2.
    The testable SNR for FR2.