## Slide 1: Way forward on LTE UE and BS performance requirements for additional enhancements for NB-IOT
Huawei,Hisilicon
R4-2005605
3GPP TSG-RAN WG4 Meeting #94-e-Bis
Electronic Meeting, April 20th – 30th 2020

## Slide 2
UE
    FFS define performance requirements for NPDSCH with 2 HARQ processes (i.e., for Cat-NB2) and interleaved multi-TB scheduling
    Interested companies are encouraged to provide simulation results as per the simulation assumptions in slide#3, considering the test time and achievable SNR test point.
    If performance improvements are observed as per the evaluations between the interleaved and continuous transmission, corresponding NPDSCH performance requirements definition can be considered
      FFS the detailed parameters and test applicability if RAN4 will define the test case.
      BS
    FFS define performance requirements for NPUSCH format 1 with 2 HARQ processes and interleaved multi-TB scheduling
    Interested companies are encouraged to provide simulation results as per the simulation assumptions in slide#4 , considering the test time and achievable SNR test point.
    No need to introduce BS demodulation requirements for coexistence of NB-IoT and NR with symbol-level reservation
Performance requirements

## Slide 3
Simulation assumptions for NPDSCH with multi-TB transmission (Informative)
Parameter | Value
System bandwidth | 200 kHz
Operation mode | Stand alone
Antenna configuration | 1T1R
Channel model | ETU 1Hz
Frequency error | 0 Hz
Timing error | 0μs
Performance target | SNR@70% of maximum throughput
NSF | 10
Repetition number | 32
Transmission mode | Interleaved, Continuous
HARQ process | 2
Carrier Type | Non-anchor
TB size | 1032
Duplex mode | HD-FDD

## Slide 4
Simulation assumptions for NPUSCH format 1 with multi-TB transmission (Informative)
Parameter | Value
Number of tones | 12
SCS | 15kHz
Antenna configuration | 1T2R
Channel model | ETU 1Hz
Frequency error | 0Hz
Timing error | 0μs
Performance target | SNR@ 70% of maximum throughput
NRU | 10
Repetition number | 32
HARQ process | 2
Transmission mode | Interleaved, continuous
TB size | 872

## Slide 5: Reference
R4-2003704 Discussion on NPDSCH performance requirements for additional enhancements for NB-IOT, Huawei, HiSilicon
R4-2003705 Discussion on NPUSCH performance requirements for additional enhancements for NB-IOT, Huawei, HiSilicon
R4-2004021 Open issues on UE/BS demodulation requirements for Rel-16 NB-IoT, Ericsson
R4-2004074 UE and BS demodulation requirements for NB_IOTenh3, Nokia, Nokia Shanghai Bell
R4-2005580 Email discussion summary for [94e Bis][212] NB_IOTenh3_Demod, Moderator (Huawei)