## Slide 1: WF on simulation assumptions for beam squint study
SONY
3GPP TSG-RAN WG4 Meeting # 94-e-Bis R4-2005675
Electronic Meeting, 20 – 30 Apr., 2020

## Slide 2: Background
Beam squint happens when DL BM reference signals and UL/DL control and/or data channels of interest are not within the same CC, see figure on right
Beam squint causes a received signal to have a frequency selective characteristic
  It is a radiative-domain impairment
  It causes gain droop, like impairment caused by active circuitry in the conducted domain
Problem statement: Given CC1 and CC2 separated by ∆f and assuming the UE uses the codebook entry optimized for CC1, what is the degradation of CC2 spherical coverage?
The WF includes the refined simulation assumptions for further align the quantified results of radiative degradation due to the beam squint when common beam management is adopted for CC1 and CC2.
Difference in antenna gain, ‘x’ dB
gNB
UE
Conducted power in transmitted CCs
Ref signal for BM
Blue CC squints away from target direction due to separation in frequency from reference signal
Power received OTA
‘x’ dB

## Slide 3: Simulation assumptions
Parameter* | Value | Notes
Antenna array size | implementation choice | Companies are recommended to align the antenna array size according to TR-38.817
Element spacing | implementation specific | 
Antenna Element pattern | See TR38.803/Patch/Dipole | Antenna element choice is up to implementation
Phase shifter impairments | See TR38.817-01 | Reuse gain variation and phase variation models from the Rel-15 beam correspondence study, frequency drift of phase shifter also be taken into account
Transmission line impairments | Modeled TL length and loss per element | Transmission line lengths per antenna element, mismatch, and loss
To derive and align the performance degradation due to the beam squint in next meeting, the following simulation assumptions for antennas are encouraged to be used:
*Note: parameters which have been taken into account for spherical coverage and multi band relaxation shall not be double counted.

## Slide 4: Simulation on the degradation of EIRP spherical coverage due to beam squint
EIRP spherical coverage: EIRP in CA is measured as the total power received over all CCs.
Two CCs are assumed in the simulation (CC1 and CC2):
  The codebook is optimized for CC1 while estimating the spherical coverage based on the total power of CC1 and CC2 (EIRP_total (theta, phi) = EIRP_CC1(theta, phi)+EIRP_CC2(theta, phi)) spherical coverage 1
  The codebook is optimized for CC1 and CC2, respectively, while estimating the spherical coverage based on the total power of CC1 and CC2 (EIRP_total (theta, phi) = EIRP_CC1(theta, phi)+EIRP_CC2(theta, phi))  spherical coverage 2
  The degradation of the spherical coverage based on the total power on CC1 and CC2 shall be quantified
    degradation = spherical coverage 2-spherical coverage 1
The degradation needs to be presented as a function of frequency separation between CC2 and CC1.
  The frequency separation between two CCs: 0 MHz to 5200 MHz (both CCs are below 30 GHz), 0MHz to 6400MHz (both CCs are above 37 GHz)

## Slide 5: Simulation on the degradation of EIS spherical coverage due to beam squint
EIS spherical coverage: Sensitivity in CA is measured per CC
Two CCs are assumed in the simulation (CC1 and CC2):
  The codebook is optimized for CC1 while estimating the spherical coverage for CC2  spherical coverage 1
  The codebook is optimized for CC2 while estimating the spherical coverage for CC2  spherical coverage 2
  The degradation of the spherical coverage for CC2 shall be quantified
    degradation = spherical coverage 2-spherical coverage 1
The degradation needs to be presented as a function of frequency separation between CC2 and CC1.
  The frequency separation between two CCs: 0 MHz to 5200 MHz (both CCs are below 30 GHz), 0MHz to 6400MHz (both CCs are above 37 GHz)

## Slide 6: WF
The companies are encouraged to provide results on the EIRP and EIS degradation based on the simulation assumptions in the next meeting.
The impact on other RF requirements, e.g., transmit power control tolerance and TPC loop convergence, are also recommended to be studied.

## Slide 7: Reference
R4-2004872 Beam squint analysis for FR2 UEs Qualcomm Incorporated
R4-2004755 on beam squint cased degradation Huawei, HiSilicon
R4-2003349 Preliminary analysis on beam squint due to larger frequency separation Sony, Ericsson
R4-2004714 Views on radiative degradation mechanisms for larger frequency separation Apple Inc.
R4-2005105 Email discussion summary for [94e Bis][19] NR_RF_FR2_req_enh_Part_3 Moderator (Qualcomm Incorporated)