## Slide 1
3GPP TSG RAN WG4 Meeting #95-e R4-2008269
Electronic Meeting, 25 May – 5 June, 2020
Agenda item: 14.2.4
Source: vivo
Title: Consideration on NR SISO OTA WI

## Slide 2
Outlines
Background
Discussion of LTE history
Consideration on NR FR1 SISO OTA

## Slide 3
Background
2019.11, Reno USA, RAN5#85
R5-198965 New SID on NR FR1 and EN-DC FR1 UE TRP and TRS, RAN5#85, Rohde & Schwarz, Orange
“The technical objective of this study item is to define the necessary testing conditions to ensure NR FR1 UE TRP and TRS are tested properly when following the methodology already defined in TS 37.544. More specifically, the SI covers the definition of measurement frequencies and test procedure for the following areas pertaining to Handheld UE, LEE (Laptop Embedded Equipment) and LME (Laptop Mounted Equipment)”
Conclusion: Due to sustained objection from Apple RAN5 didn't endorse the SI proposal. It is up to the proponents to present it at the RAN plenary.
2019.12, Spain, RAN#86
RP-192905 New SID on NR FR1 and EN-DC FR1 UE TRP and TRS Orange Spain, Rhode & Schwarz, CMCC
RP-192431 Views on the NR FR1 TRP/TRS requirement specification Apple Inc.
“Proposal: It is proposed to recast the SI proposed in [1] into a work item led by RAN4 with RAN5 given secondary responsibility with the objective to define UE NR FR1 and EN-DC TRP and TRS minimum requirements and conformance test specification”
RAN chair: suggests to discuss this until March 20 to converge so that the work could be done in 3GPP

## Slide 4
Discussion of LTE history
It is “painful”
About 6 years : 2012.12 RAN#58~ 2018.3 RAN#79
3 Rapporteur companies:
  Nokia 2012.12~2016.6
  Telecom Italia and Vodafone, 2016.6 ~2018.3
20 revisions of WID: most only change completion date
Numerous effort from participating companies: research, testing, contributions, meeting time and life time!
No consensus, WI was stopped.
TSG meeting # | TSG Tdoc number of status report | TSG Tdoc of WI/SI description sheet as approved by TSG (if any) | overall level of completion as decided by TSG for the SI / Core part / Testing part | completion date as decided by TSG for the SI / Core part / Testing part
58 | WI/SI started | RP-122030 | 0% | June 2014
59 | RP-130067 | RP-130217 | 5% | June 2014
60 | RP-130496 | RP-130703 | 10% | June 2014
61 | RP-130974 | RP-130703 | 10% | June 2014
62 | RP-131509 | RP-130703 | 15% | June 2014
63 | RP-140257 | RP-130703 | 20% | June 2014
64 | RP-140785 | RP-130703 | 25% | Sept 2014
65 | RP-141158 | RP-130703 | 30% | Dec 2014
66 | RP-141973 | RP-141966 | 35% | Dec 2015
67 | RP-150104 | RP-141966 | 40% | Dec 2015
68 | RP-150615 | RP-141966 | 40% | Dec 2015
69 | RP-151227 | RP-141966 | 50% | Dec 2015
70 | RP-151913 | RP-151917 | 50% | Mar 2016
71 | RP-160231 | RP-151917 | 50% | Jun 2016
72 | RP-161329 | RP-161323 | 50% | Dec 2016
73 | RP-161529 | RP-161323 | 60% | Dec 2016
74 | RP-162060 | RP-162061 | 65% | Mar 2017
75 | RP-170221 | RP-170223 | 75% | June 2017
76 | RP-171007 | RP-171010 | 85% | Sept 2017
77 | RP-171585 | RP-172035 | 85% | March 2018
Revisions of LTE SISO OTA WID

## Slide 5
Discussion of LTE history
Still, It is valuable.
Sophisticated frameworks have been developed.
  CDF approach: obtain candidate values from specific percentiles of CDF curves, then refine them by factors like number of supported bands
  joint band passing rate (JBPR): measurement over a selected set of bands and evaluating the ratio of the number of passed UEs over the total number of UEs
Numerals testing data submitted from operators, vendors and testing organizations: > 1000 TRP&TRS test points
Example flow chart of JBPR
(from R4-1702766 Samsung)

## Slide 6
Consideration on 3GPP NR FR1 SISO OTA
3 options to proceed
Option1: only test methodology in RAN5 (RP-192905)
Option2: define minimum requirements in RAN4, then RAN5 (normal procedure, RP-192431)
Option3: nothing
Proposal: adopt option2
  There are clear demands from proponents of option1, option3 is precluded
  3GPP study and consensus on NR FR1 SISO OTA performance requirements is highly meaningful for 5G industry
Supporting IM name
Orange
Vodafone
Telecom Italia
Rohde & Schwarz
CMCC
NTT DOCOMO
China Unicom
China Telecom
KDDI
AT&T
Supporting companies of RP-192905

## Slide 7
Consideration of 3GPP NR FR1 SISO OTA
This time can be better
Experience: long discussion on LTE, actually LTE was not far away from success
Technically: NR FR2 tests are all OTA. MIMO OTA is much more complex from technology point of view
Interest: many operators, vendors jointed the discussion in both RAN5#85 and RAN#86 meeting
Summary of LTE TRS proposal (from R4-1710392 intel)
B41/BHH: proposal is ~10dBm, same as CCSA requirements which have been used for years
From CCSA YD/T 1484.6

## Slide 8
Consideration of 3GPP NR FR1 SISO OTA
Regional organizations already made significant progress, CCSA, CTIA, etc.
with expertise resource of 3GPP and reasonable spirit of compromise, 3GPP consensus will provide general guidance for the whole 5G industry!
Operating band | Channel bandwidth | NR Sensitivity (dBm) |  |  | 
 |  | SA mode |  | EN-DC mode | 
 |  | Average | Max | Average | Max
N41 | 100MHz | [-81~-80] | [-80~-79] | [-81~-79] | [-80~-78]
N78 | 100MHz | [-81~-80] | [-80~-79] | [-81~-79] | [-80~-78]
Table: Range of CCSA candidate values of Handheld NR UE TRS minimum performance requirement in free space

## Slide 9
Draft WI proposal
Please see draft motivation and WID in R4-2004054/R4-2004055

## Slide 10
THANK
YOU