## Slide 1: WF on BC based on SSB
Huawei, HiSilicon, [ ]…
R4-2008481
3GPP TSG-RAN WG4 #95-e
May 25th – June 5th, 2020
Electronic meeting

## Slide 2
WF1: Beam correspondence requirement based on SSB-only
Whether and how much performance relaxation, ∆p, relative to the condition which assumes both SSB and CSI-RS are present, is necessary
  Alt 1: ∆p = 0 dB (LGE, Qualcomm, NTT DOCOMO, Samsung, Nokia, Sony, OPPO, Ericsson, [Intel])
    Will have impact on SSB searching efficiency
  Alt 2: 0 < ∆p ≤ 3 dB (Futurewei, Huawei, Apple)
Note for discussion：A common understanding has emerged that it is up to UE implementation how to refine the UE beam based on SSB, with one company providing an example algorithm of hierarchical beam refinement. Other companies have argued that this implementation choice is not required by the specification.
Based on this common understanding, and appreciating the detailed description of a possible UE implementation provided to Issue 1-1-5 in [1] by one company, it is FFS whether an LS to RAN1 and also a check with RAN4 RRM session is needed to determine the feasibility of the assumption on “up to UE implementation how to refine the UE beam based on SSB, with one company providing an example algorithm of hierarchical beam refinement” and whether it is capable of meeting RRM requirements on L1-SINR and L1-RSRP reporting.
Further note for consideration: the network must be able to rely on SSB-only beam correspondence. If ∆p = 0 dB cannot be agreed: an Msg.1 EIRP requirement must be met separately. This should be established before any discussion on test case applicability.
Notes: Qualcomm: 1. We have shared experimental results (R4-2007283) that delta(P)=0 is indeed feasible for Rel-16 FR2 UEs. (no delta(P) is necessary). Furthermore, in order to address a concern about UE RRM performance impact due to SSB-based Rx beam refinement, an example has been also provided in 1-1-1-5. Note that feasibility assessment doesn’t mean that it should be viable for all UE implementations, but it confirms that the requirement can be established without relaxation for UEs that can support this feature. 2. Removed comment not relevant to BC, and added supporting companies.
Ericsson: added text in blue.
Apple: Added a recommendation to determine whether the proposed UE implementation in comments to Issue 1-1-5 should be checked in an LS to RAN1 and also be checked with RAN4 RRM session to determine the feasibility of the assumption on “up to UE implementation how to refine the UE beam based on SSB, with one company providing an example algorithm of hierarchical beam refinement” and whether it is capable of meeting RRM requirements on L1-SINR reporting. Also recommend removing the note on further consideration, since discussion on initial access BC is out of scope of this requirement.

## Slide 3
WF2: Applicability rule for peak direction
Applicability rule for peak direction:
  Alt 1: Applicable for both ∆p = 0 dB and ∆p > 0
  restrict the side condition applicability only to the Rel-16 beam correspondence enhancement, and all of the remaining FR2 RF requirements in Rel-16 shall continue to be defined based on the Rel-15 side conditions (i.e. both SSB and CSI-RS signals are present during beam peak search and spherical coverage measurements).
  Alt 2: Applicable for both ∆p = 0 dB and ∆p > 0
    If a UE meets beam correspondence requirements either based on SSB or based on CSI-RS, it is considered to have met the beam correspondence requirements based on SSB and CSI-RS.
    If a UE meets beam correspondence requirements based on SSB, it is considered to have met the beam correspondence requirements based on CSI-RS.
    The single beam peak direction for other UL tests shall be determined by the single Rel-16 BC which is to be tested according to applicability rule
  Alt 3: Applicable for both ∆p = 0 dB
  If UE support eBC in Rel-16 and passes the requirements, then the BC requirement in Rel-15 will be skipped
  Alt 4: Applicable for both ∆p = 0 dB and ∆p > 0
  Tx requirements other than BC only need to be tested once, regardless whether Rel-16 BC is same to Rel-15 BC or not. For UEs supporting Rel-16 BC, all other Tx requirements is tested with beam peak or TRP derived by Rel-16 BC and skip Rel-15 tests if beam correspondence requirements are same for Rel-16 and Rel-15, otherwise, only test with beam peak or TRP derived by Rel-15 BC.
  Alt 5: No separate consideration necessary. Beam peak direction will automatically be determined from test skipping (or hierarchy) rules. If the UE supports multiple variants of BC, it is assumed the UE can meet all its requirements with any of the associated side conditions.
  Note for discussion: Alt3 and Alt4 are in the same principle, Alt4 provide how to handle with ∆p > 0
Notes: Qualcomm: Added Alt 5 based on our view on 1-1-3 in 1st round. We humbly suggest you to switch the slide order between WF2 and WF3.

## Slide 4: WF 3: Test case applicability
Further refinement of the agreement “Rel-15 BC test is declared automatically passed if a UE passes Rel-16 BC test using the same SSB configuration and SNR as in Rel-15” in WF R4-2005735
  Alt 1
  If RAN4 agrees to introduce beam correspondence based on SSB with relaxation, Rel-15 tests cannot be skipped since the performance is different between Rel-15 and Rel-16. Potential test case reduction techniques can be further discussed
  If no relaxation is defined, Rel-16 BC can only be declared by UE with bit 1 in Rel-15, otherwise, Rel-16 BC and Rel-15 BC are independent capability can be declared by both bit 0 and bit 1 UE.
  Alt 2
  If a UE meets beam correspondence requirements either based on SSB or based on CSI-RS, it is considered to have met the beam correspondence requirements based on SSB and CSI-RS.
  If a UE meets beam correspondence requirements based on SSB, it is considered to have met the beam correspondence requirements based on CSI-RS.
  Alt 3
  If a UE meets a Rel-16 beam correspondence requirement without relaxation, then it automatically meets Rel-15 BC requirement
  For a UE capable of Rel-16 BC, all UL tests requiring MOP condition are conducted based on the Rel-16 RS-set it declares support for. If the UE supports both types of RS-sets for Rel-16 BC, one UL representative test (e.g. min peak EIRP testing) using the second RS set is additionally conducted. Choice of beam peak is determined from first set RS. It is up to RAN5 which RS is ‘first’ and which is ‘second’. If the UE supports multiple variants of BC, it is assumed the UE can meet all its requirements with any of the associated side conditions.
Notes: Qualcomm: Added Alt 3. Alt 1 and 2 are not mutually exclusive. And as we shared our view in 1st round, to address test skipping/applicability rules taking into account Rel-15, Rel-16 SSB-based, and Rel-16 CSI-RS based BC requirements, we add Alt 3 based on Alt 1-1-3-5 as a global test applicability rule.
Ericsson: added text in blue (underlined)
Apple: If we do achieve compromise based on ∆p>0, then it also makes sense to discuss potential test case reduction techniques. This is also useful since the BC based on SSB requirement shall not impact other core RF requirements, and the beam peak search / spherical coverage test still needs to be performed according to the Rel-15 SSB+CSI-RS side conditions

## Slide 5
WF 4: SSB periodicity
SSB periodicity
Alt 1: RAN4 revisits the SSB periodicity =20ms for SSB based BC. Suggest SSB periodicity = 5ms to reduce the test time in RRC connected mode
Keep SSB periodicity =20ms for SSB based BC, which reflects the real network configuration. One of the purposes of conformance testing.
Notes: Ericsson: changes in blue.

## Slide 6
Reference
[1] R4-2008952, “email discussion summary on NR FR2 UE RF part 2”, Apple