## Slide 1: WF on NR Mobility Enhancements
Intel Corporation
3GPP TSG-RAN WG4 Meeting #95-e R4-2008585
Electronic Meeting, May 25th – June 5th 2020

## Slide 2: Background
Agreements in this way forward are based on email discussion in R4-2009020 Email discussion summary for [95e][208] NR_Mob_enh_RRM
Agreements in the last RAN4#94-e-bis meeting can be found in:
  R4-2005392 Email discussion summary for [94e Bis][108] NR_Mob_enh_RRM
  R4-2005305 WF on NR Mobility enhancement RRM requirements

## Slide 3: DAPS handover: Agreement in 1st round
Issue 1-4 Definition of asynchronous DAPS HO for intra-frequency or intra-band scenarios shall be based on:
Agreement: If side condition for sync is not met, async DAPS HO is assumed. (agreement in RNA4#94-e-bis)
Issue 1-5 Additional note for sync condition:
Agreement: If the receive time difference exceeds the cyclic prefix length of that SCS, demodulation performance degradation is expected for the first symbol of the slot. (agreement in RNA4#94-e-bis)
Issue 1-6 Response to RAN1 LS (R1-2003058):
Agreement: RAN4 doesn’t need to reply RAN1 LS
Issue 1-7 LS to RAN2 on misalignment between RAN2 and RAN4 on the following capabilities:
Agreement: Since RAN2 is already aware of this, it is not necessary to send this LS.

## Slide 4: DAPS handover: way forward for 2nd round
Issue 1-1: interruption requirements for async intra-frequency DAPS HO.
Agreement: one more slot of interruption is allowed compared to sync scenario
Issue 1-2: interruption requirements for async intra-band inter-frequency DAPS HO.
Agreement: one more slot of interruption is allowed compared to sync scenario

## Slide 5: DAPS handover: way forward for 2nd round
Issue 1-3: definition of synchronous DAPS HO for intra-frequency or intra-band scenarios shall be based on: 6 us MRTD and 7.6 us MTTD between source and target cells.
  Note 1: If the receive time difference exceeds the cyclic prefix length of that SCS, demodulation performance degradation is expected for the first symbol of the slot.
  Note 2: A UE is not expected to transmit in the uplink earlier than after the end of the last received downlink symbol in the same or different cell where is given by Table below.
  Note 3: A UE is not expected to receive in the downlink earlier than after the end of the last transmitted uplink symbol in the same or different cell where is given by Table below.
Transition time | FR1
 | 25600
 | 25600
Transition time | FR1
 | 25600
 | 25600

## Slide 6: Test case list for DAPS HO and CHO
Applicability rule: the UE only supporting sync DAPS HO is not required to test async cases.
Test case number | Test purpose | Description | Responsible company
1 | Intra-frequency sync DAPS handover test in SA for FR1 | See table in section 4.5 in R4-2009020 | Qualcomm
2 | Intra-frequency async DAPS handover test in SA for FR1 | See table in section 4.5 in R4-2009020 | Qualcomm
3 | Intra-band Inter-frequency sync DAPS handover test in SA for FR1 | See table in section 4.5 in R4-2009020 | Intel
4 | Intra-band Inter-frequency async DAPS handover test in SA for FR1 | See table in section 4.5 in R4-2009020 | Intel
5 | Inter-band Inter-frequency sync DAPS handover test in SA for FR1 | See table in section 4.5 in R4-2009020 | Huawei
6 | Inter-band Inter-frequency async DAPS handover test in SA for FR1 | See table in section 4.5 in R4-2009020 | Huawei
7 | Conditional intrafrequency handover test in SA for FR1 | See table in section 4.5 in R4-2009020 | Ericsson
8 | Conditional interfrequency handover test in SA for FR1 | See table in section 4.5 in R4-2009020 | Ericsson
9 | Inter-frequency sync DAPS handover test in SA for FR1-FR2 | See table in section 4.5 in R4-2009020 | Huawei
10 | Inter-frequency async DAPS handover test in SA for FR1-FR2 | See table in section 4.5 in R4-2009020 | Huawei
11 | Conditional intrafrequency handover test in SA for FR2 | See table in section 4.5 in R4-2009020 | Ericsson
12 | Conditional interfrequency handover test in SA for FR2 | See table in section 4.5 in R4-2009020 | Ericsson