## Slide 1: Way forward on MRTD for FR2 inter-band CA
3GPP TSG-RAN WG4 Meeting #94-e-Bis
Electronic Meeting, 25 May – 5 June, 2020
R4-2008626
Apple,…

## Slide 2: Background
In RAN4#94e-bis, agreed WF can be summarized as
  Continue discussing the definition and applicable band combinations of common and independent beam management in RF session
    Investigate if there are other solutions than strict timing requirement for tackling the impacts due to UE beam management implementation
  Decision on MRTD for common beam management will be pending on the assumptions of common beam management defined in RF session
  MRTD for independent beam management will be decided by RAN4#95e based on majority view.
    Subject to the decision on MRTD for independent beam management, the FR2 MRTD defined in Table 7.6.4-2: Maximum receive timing difference requirement for inter-band NR carrier aggregation in TS38.133 at least can be applied for independent beam management. It is FFS for common beam management.
In RAN4#95e, the 1st round discussion is summarized in R4-2008510

## Slide 3: WF on FR2 inter-band CA
On MRTD for CBM (strive to down select between option 1 and 2 by the end of RAN4#95e)
  Option 1:
    At least 260ns MRTD is feasible for CBM from UE perspective
    Further study feasibility to support up to 3us MRTD under assumption of co-located deployment in terms of impact on performance (e.g. possible scheduling restrictions)
      E.g. potential performance degradation and other WG impact due to MRTD larger than a threshold (e.g. 260ns) should be studied
      It is FFS the study should be done within Rel-16 timeframe or in Rel-17
  Option 2:
    Do not define CBM RRM requirements in Rel-16 if no consensus can be made by [RAN4#95e or RAN4#96e]

## Slide 4: WF on FR2 inter-band CA
On MRTD for IBM
    Keep existing requirement, i.e. 8us, unchanged
    Revision of Table 7.6.4-2: Maximum receive timing difference requirement for inter-band NR carrier aggregation in TS38.133 for both R15 and R16 (depending on the conclusion of MRTD for CBM, strive to down select between option 1 and 2 by the end of RAN4#95e)
      Option 1: clarify 8us MRTD only applies to IBM. (CR from Apple)
        That means new MRTD should be specified for CBM
      Option 2: clarify new MRTD, if introduced, only applies to CBM
        That means existing 8us MRTD may also apply to CBM (CR from Ericsson)
        MRTD = 8 µs, but an MRTD = 3 µs is applicable for UE which is only capable of common beam management for a band combination where common beam management is possible. The UE may, assume collocated site, in this case (CR R4-2007096).
        Proponent of this option still needs to clarify the applicability of MRTD=8us, e.g. to IBM only or both IBM and CBM

## Slide 5: WF on FR2 inter-band CA
On MTTD for CBM
    Option 1: no requirement specified
    Option 2: 3.5us
    Option 3: depends on MRTD
On MTTD for IBM
    Option 1: 8.5us
    Option 2: depends on MRTD