## Slide 1: Way forward on PDSCH CA normal demodulation requirements
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #95-e
E-meeting, 25 May – 5 June, 2020
Agenda Item: 6.18.1.1
R4-2008838

## Slide 2: Requirements for TDD-FDD CA and TDD-TDD CA with different SCSs
      Pcell configuration for performance requirements
  Define requirements for both 15kHz Pcell and 30kHz Pcell (for CA with different SCSs) and both FDD 15 kHz Pcell and TDD 15 kHz Pcell (for FDD + TDD CA with 15 kHz SCS)
      Pcell configuration for the test
  The test coverage can be considered fulfilled if UE passes any one of scenario with one of the CC as PCell for FDD 15 kHz + TDD 15 kHz
  If Pcell in both carriers are supported for FDD 15 kHz + TDD 30 kHz, configure TDD cell as Pcell
  If Pcell in both carriers are supported for TDD 15 kHz + TDD 30 kHz, configure
    Option 1: 15 kHz SCS cell as Pcell
    Option 2: 30 kHz SCS cell as Pcell

## Slide 3: Requirements for TDD-FDD CA and TDD-TDD CA with different SCSs
      HARQ process number
  Companies are encouraged to check the performance difference of scheduling options for TDD 15 kHz + TDD 30 kHz CA with 12 HARQ processes
          if no simulation results show there is performance impact by scheduling the initial transmission and retransmission in different types of slots, then no need to differentiate the two options in TS 38.101-4.
 |  | CCs with the same duplex mode & SCS with Pcell | CCs with different duplex mode / SCS with Pcell
FDD 15 kHz + TDD 30 kHz CA | FDD PCell | 4 | 8
 | TDD PCell | 8 | 8
FDD 15 kHz + TDD 15 kHz CA | FDD PCell | 4 | 4
 | TDD PCell | 8 | 8
TDD 15 kHz + TDD 30 kHz CA | 15kHz PCell | 8 | 12 (Note 1)
 | 30kHz PCell | 8 | Option 1: 6 Option 2: 8
Note 1: FFS scheduling details: Option 1: different RTTs (10 or 20 slots) are used for different HARQ processes, and initial transmission and retransmission are scheduled on the same type of TDD slot. Option 2: initial transmission and retransmission can be scheduled on different types of TDD slot |  |  | 

## Slide 4: Requirements for TDD-FDD CA and TDD-TDD CA with different SCSs
      K1 values
  Option 1: K1 values are provided based on Pcell’s SCS in scenarios with mixed SCSs.
  Option 2: K1 values are based on each cell’s own SCS
  Other options are not precluded
  Companies are encouraged to check RAN1 procedure for considered scenarios.
 |  | CCs with the same duplex mode & SCS with Pcell | CCs with different duplex mode / SCS with Pcell
FDD 15 kHz + TDD 30 kHz CA | FDD PCell | 2 | {2}
 | TDD PCell | {8,7,6,5,5,4,3,2} | {7,6,4,11,9,7,6,4}
FDD 15 kHz + TDD 15 kHz CA | FDD PCell | {2} | {2}
 | TDD PCell | {4,3,2,6,5} | {4,3,2,6}
TDD 15 kHz + TDD 30 kHz CA | 15kHz PCell | {4,3,2,6} | {4,4,3,3,2,2,6,6}
 | 30kHz PCell | {8,7,6,5,5,4,3,2} | {7,5,4,11}

## Slide 5: Test applicability rule
      Categorizing of CA capabilities
  Option 1: Define different capabilities for intra-band contiguous CA, intra-band non-contiguous CA and inter-band CA with different numbers of bands.
  Option 2: Define different capabilities for intra-band contiguous CA, intra-band non-contiguous CA and inter-band CA.
  Companies to bring proposals on the demod spec structure for CA, with the motivation to minimize future maintenance.
      Test of different CA capabilities
  Option 1: Test intra-band contiguous CA, intra-band non-contiguous CA and inter-band CA with the largest number of bands.
  Option 2: Test all the supported CA capabilities, including intra-band contiguous CA, intra-band non-contiguous CA and inter-band CA with different numbers of bands.

## Slide 6: Test applicability rule
      Selection of CA configuration(s) and CBW combination
  Further discuss by taking into account:
    The supportedSubCarrierSpacingDL, maxNumberMIMO-LayersPDSCH and supportedModulationOrderDL are reported for each CC and scalingFactor are reported per band for FR1 and FR2.
    The testable SNR for FR2.

## Slide 7: Plan for CRs
      Endorse the draft CR for NR FR1 requirements with 4Rx in this meeting
  Encourage companies to provide comments for this draft CR in section 2.3.2.
      Endorse all others CRs on requirements and FRCs in RAN4 #96e (Aug) meeting
  For CMCC and QC’s CRs, align the structure with Huawei’s draft CR
      Agree all the CRs for CA normal PDSCH together (including CRs requirements, FRCs and test applicability rules) in RAN4 #97e (Oct-Nov) meeting