## Slide 1: WF on UL MIMO MPR/A-MPR for 29 dBm
T-Mobile USA
R4-2008902
3GPP TSG-RAN WG4 Meeting #95-e
Electronic Meeting, May 25th – Jun 5th 2020
Agenda: 8.14.2

## Slide 2
In RAN4 #94Bis-e, a way forward [1] was approved encouraging measurements for n41 with 2x26 dBm Tx chains to inform MPR requirements.
  Antenna isolation of 10 dB
  Two 26 dBm Tx chains (NR)
  Equal Power, equal backoff, on both transmit chains
  Various channel and allocation BWs, with focus on “worst case” allocations
Other WIs and discussion threads have also been discussing UL MIMO and MPR requirements, for various power classes and Tx chain capabilities
Background

## Slide 3: Background on EVM and IBE
Unlike OOBE and Spurious Emissions, EVM and IBE are not generally regulated. (No FCC tests)
UL MIMO brings potential new impacts to EVM and IBE only as a result of RIMD from 2Tx.
  Difficult to measure directly in lab environments
  OTA Conformance testing for EVM and IBE are not forseen.
Any impairments to EVM or IBE would impact only the channel used by the cell, controlled by the operator. Any UL BLER increase would be managed by link adaption.

## Slide 4
Companies encouraged to bring measurements for n41 2Tx to inform MPR and NS_04 A-MPR specs
  10dB assumed antenna isolation
  Focus on OOBE, spurious emissions, and ACLR
  15 kHz SCS as 1st priority, other SCS secondary
  Measurements for amplitude-correlated 1-layer, and amplitude-uncorrelated 2-layer transmission
  Measurements for DFT-S and CP-OFDMA
  Focus on identifying limiting factors for different allocation regions (e.g. edge, outer, inner). Redefinitions of regions may be considered.
EVM and IBE should be specified to be measured per connector, because of 2Tx test challenges, and lack of regulatory impact.
Companies are encouraged to consider feasible performance improvements beyond current 1Tx specifications.
Way Forward:

## Slide 5: Waveforms and Transmission Modes
Waveform | Correlated 1-layer | Noncorrelated 2-layer
DFT-S-OFDMA | Transparent TxD (Scenario-1 [2]) | N/A
CP-OFDMA | Transparent TxD (Scenario-1 [2]) Scenario-3 [2] | 2-layer MIMO
Priority for measurements:
Amplitude-correlated 1-layer (critical for Cell Edge)
Amplitude-noncorrelated 2-layer (expected Worst case for MPR)

## Slide 6
[1] | R4-2005190 | Way Forward on MPR for PC1.5 UL MIMO and Tx div | 
[2] | R4-2005652 | WF on Uplink Full Power Transmission | 
[3] | R4-2008404 | WF on EVM Requirement for UL MIMO Transmission | 
References