## Slide 1: WF on impact of NR positioning measurements on RRM
Ericsson
3GPP TSG-RAN WG4 Meeting # 95-e
Electronic Meeting, May 25-June 05, 2020
Agenda: 6.8
R4-2009266

## Slide 2: Rel-15 MG patterns for positioning measurements
All Rel-15 MG patterns are applicable for positioning measurements.
FFS: Whether performing PRS measurement in successive MG occasions subject to signaled UE capability {N,T}? N = duration of DL PRS symbols in ms processed every T ms.

## Slide 3: New MG Patterns
Introduce 2 new MG patterns with MGL ≥ 10 ms and MGRP ≥ 80 ms.
FFS whether the new MG patterns are applicable for RRM measurement or not.
FFS: details of new MG patterns.
Candidate MGL and MGRP for new MG patterns:
  MGL = {10, 18, 20, 34, 40 and 50} ms
  MGRP = {80, 160, 320 and 640} ms
  Combination of MGL and MGRP is FFS
  Other options for MGL and MGRP are not precluded
New MG patterns shall be UE capability.
In case RRM requirements for new MG are not finalized in RAN4#96-e then no new MG will be introduced in Rel-16.

## Slide 4: Gap sharing between RRM and positioning measurements
Re-use the handling of LTE PRS in Rel-15 CSSF for gap sharing between NR PRS and RRM.

## Slide 5: Active BWP switch during gaps used for PRS measurements
FFS: whether to define UE behavior if active BWP switching overlaps/collides with gaps used for PRS measurements.
Candidate options if the UE behavior is defined:
  Option 1:
    Active BWP switching is prioritized over PRS measurement in a gap where active BWP switching is triggered.
      FFS: whether UE is required to meet PRS measurement requirements if option 1 is adopted.
  Option 2:
    PRS measurement is performed in a gap even if active BWP switching is triggered in that gap i.e. PRS measurement is prioritized in gaps.

## Slide 6: Impact of concurrent RRM/PRS processing/measurement
FFS: whether concurrent RRM/PRS processing has any impact on RRM/PRS measurement.

## Slide 7: Conditions for accurate path loss measurement
UE’s path loss measurement is considered accurate/reliable provided that the side conditions for the measurement used by the UE for the path loss estimation are met.
FFS whether to include following criteria for deriving measurement accuracy in the LS response:
  measurement error is within 5-th percentile and 95-th percentile of the CDF.

## Slide 8: SRS transmission during DRX inactive
FFS: whether it is feasible for UE to transmit SRS for positioning during the DRX inactive period from UE power consumption/complexity and BS implementation perspectives.