## Slide 1: [draft] WF on WRC-19 outcome and impact on RAN4 specifications
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 Meeting #95-e R4-2008410
Online Meeting, 25 May - 5 June 2020

## Slide 2: Background (1/3)
Common understanding of which regulatory requirements TS38.101-2 should address (for information only):
  Note: Necessity of -8dBm/200MHz is FFS.
  Note: Some must be met simultaneously like 1/2/4 and 1/3/4 for Europe.
Region3/ | Requirement 1 | Requirement 2 | Requirement 3 | Requirement 4 | Requirement 5 | Requirement 6
Global, US, Japan | Protected range: spurious Band applicability: all Limit: -13 dBm/MHz | Protected range: 23.6 - 24.0 GHz Band applicability: n258, n257 Limit: +1 dBm/200 MHz | Protected range: 23.6 - 24.0 GHz Band applicability: n258, n257 Limit: -5 dBm/200 MHz | N/A | Protected range: 36.0 to 37.0 GHz Band applicability: n260, n259 Limit: +7 dBm/1000 MHz | Protected range: 36.0 to 37.0 GHz Band applicability: n260, n259 Limit: -13 dBm/1 MHz
Europe |  |  |  | Protected range: 7.25 GHz ≤ f ≤ 2nd harmonic Band applicability: all bands Limit: -10 dBm/100 MHz |  | 

## Slide 3: Background (2/3)
To introduce the regulatory requirements in TS 38.101-2, the following issues have been discussed.
  Connectivity issues when adding new NS values to existing bands [1][2][3]
  Handling of regulation to change from a loose limit to stringent one with transition period [3]
    Invoked larger A-MPR from the changeover date
    Allows UEs violating regulation to work if the NS value for stringent one is optional support
  NS value mapping and A-MPR issues [3]

## Slide 4: Background (3/3)
Agreements from WF [3] in RAN4#94-e-bis (This is an extract, the details are described in [3])
  The followings are package agreements.
    How to resolve the issues identified in the background slides
    NS mapping and associated A-MPR
      After the process on how to resolve the newly introduced NS issues and NS mapping is agreed, each band will be handled independently without waiting for the completion of the other bands.
  A feature for a UE to report newly supported NS value(s) for a legacy band to a network is introduced. Four Alts are listed.
    Alt 1-1: Explicit signaling for a UE to report newly supported NS value(s) for a legacy band to the network (introduce a new signaling feature)
    Alt 1-2: Explicit signaling for a UE to report newly supported NS value(s) for a legacy band to the network (reuse modifiedMPR bits)
    Alt 1-3: Explicit signaling for a UE to report newly supported NS value(s) for a legacy band to the network, such that supporting of NS values is optional
    Alt 2: Delay introduction of new NS until beginning of Rel-X, such that it is mandatory for a UE designed against Rel-X to support all NS values defined in the Rel-X version of the specification and which correspond to the bands which the UE supports.
  For NS mapping and A-MPR,
    Adopt one of the two (Option 1 or 2 in [3]) based on necessity of -8dBm/200MHz.
    +1dBm/200MHz for n257 & 7dBm/1GHz for n259 are introduced into NS_200, respectively, at least if no A-MPR is needed.
    The same mapping for single CC is applied to that for CA.
    A note is added to NS values for changed emissions limits (example shown: -5dBm/200MHz after 1st Sep 2027 in [3])

## Slide 5: Option 1: -8dBm/200MHz stays
 | n257 | n258 | n259 | n260
NS_200 | 1dBm/200MHz into general | No change | 7dBm/1GHz into general | No change
NS_201 | -8dBm/200MHz + -10dBm/100MHz | -8dBm/200MHz + -10dBm/100MHz |  | 
NS_202 | -10dBm/100MHz + 1dBm/200MHz | -10dBm/100MHz + 1dBm/200MHz |  | 
NS_203 |  | 1dBm/200MHz |  | 
NS_204 | -5dBm/200MHz | -5dBm/200MHz |  | 
NS_205 |  |  |  | 7dBm/1GHz + -13dBm/MHz
NS_206 | -5dBm/200MHz + -10dBm/100MHz | -5dBm/200MHz + -10dBm/100MHz |  | 
Note: n261 is omitted since the band has no connection with lower/upper EESS protection.
Notes: Qualcomm: (removed -10/100 from NS_201). Supporting -10/100 requirement will require higher AMPR for NS_201 relative to v16.3. Devices that support exist NS_201 already exist. At this time we do not support repurposing an existing NS unless we are running out of NS flags for a band.
We ask if companies can check if NS_206 is required as a standalone NS. We think NS_202 has enough AMPR to support -5 dBm/ 200 MHz due to compliance with -10/100. So NS_206 is not required for EU, post 2023, based on existing view of emissions requirements

## Slide 6: Option 2: -8dBm/200MHz isn’t necessary
 | n257 | n258 | n259 | n260
NS_200 | 1dBm/200MHz into general | No change | 7dBm/1GHz into general | No change
NS_201 | FFS | FFS |  | 
NS_202 | -10dBm/100MHz + 1dBm/200MHz | -10dBm/100MHz + 1dBm/200MHz |  | 
NS_203 |  | 1dBm/200MHz |  | 
NS_204 | -5dBm/200MHz | -5dBm/200MHz |  | 
NS_205 |  |  |  | 7dBm/1GHz + -13dBm/MHz
Note: n261 is omitted since the band has no connection with lower/upper EESS protection.

## Slide 7: WF 1
Take Option 2 and Alt 1-2(Need to discuss) from [3] as package agreements
  -8dBm/200MHz requirements is not needed and will be removed
  NS_202 includes harmonic requirements (Requirement 4) and +1 dBm/200 MHz (Requirement 2)
  Take A-MPR values proposed in [4]
    Author’s note: There is no objection in 1st round, but one company need further check in 2nd round
    +1dBm/200MHz for n257 & 7dBm/1GHz for n259 are introduced into NS_200, respectively, according to the previous agreements.
  Newly introduced NS is mandatory for UE brought into use at least after the changeover date (Need to discuss)
    Whether mandatory or not for UE brought into use before the changeover date is FFS
    FFS if mandatory status of NS is tied to release version
NOTE: This WF is applicable to WRC-19 requirements.
Notes: Qualcomm: Add note about tying NS mandatory status to release version to accommodate testing and verification considerations.

## Slide 8: WF 2
For handling of NS_201
    Whether modified MPR for NS_201 is needed or not is FFS (Need to discuss)
    Whether or not NS_201 is obsolete is FFS (Need to discuss)
    The descriptive Text in CR [5] should be same with that in CR [6] (It depends on which alts we choose)
Notes: Qualcomm: In general, we do not think repurposing NS_201 for a new requirement is a good idea, due to possible existence of fielded UEs. We are ok to leave it ‘orphaned’ but would prefer making obsolete to reduce UE testing. We can revisit this avenue if we define more than 8 NS values in each band and it is critical to repurpose disused NS.

## Slide 9: References
[1] R4-2000220, “Necessity of signaling supported NS values”, NTT DOCOMO, INC.
[2] R4-2003241, “More on necessity of signaling supported NS values”, NTT DOCOMO, INC., KDDI Corporation, SoftBank Corp.,
[3] R4-2005738, “WF on WRC-19 outcome and impact on RAN4 specifications”, NTT DOCOMO, INC.
[4] R4-2006788, “dCR to 38.101-2: Introduction of NS flags and A-MPR from WRC19 Resolutions”, Qualcomm Incorporated
[5] R4-2008163, “CR for modified MPR on NS_201”, Huawei, HiSilicon
[6] R4-2007038, “Introduction of the Annex modifiedMPR-Behaviour into the NR SA specification”, Ericsson