## Slide 1: WF on remaining Rx RF requirements for NR V2X
3GPP TSG-RAN WG4 Meeting #95-e
Electronic Meeting, 25 May – 5 June, 2020
Agenda item: 6.4.3.2
Document for: Approval
R4-2008448
CATT,…

## Slide 2: Background
In RAN4#95-e meeting, the remaining issues on Rx RF requirements for NR V2X, including REFSENS, the maximum input level and ACS were discussed in the 1st round [1].
The diversity gain, noise figure in band n38, REFSENS target SNR level, ΔRIB,c for V2X_20_n38 and the maximum input level still need further discussion in the 2nd round.

## Slide 3: Diversity gain
  Diversity gain
  Option 1: Use a value of 2.5 dB for diversity gain for NR V2X REFSENS calculations.
  Option 2: Keep the previous agreements to define 3dB diversity gain.
  Recommendations for 2nd round:
  Clarify whether the implementation loss of diversity gain is considered in the IM. If so, no need to consider implementation loss in diversity gain.

## Slide 4: Noise figure in band n38
  Noise figure in band n38
  Option 1: Use a value of 2.5 dB for diversity gain for NR V2X REFSENS calculations.
  Option 2: Keep the previous agreements to define 3dB diversity gain.
  Recommendations for 2nd round:
  Discuss whether the additional 4dB increase in NF (9dB to 13dB) for n38 is required to compensate for the cable losses.

## Slide 5: REFSENS target SNR level
  Reference measurement channel and simulation assumptions for REFSENS target SNR level
  Option 1: Use the reference measurement channel and simulation assumptions to derive REFSENSE target SNR level based on R4-2006821 from Qualcomm.
  Option 2: Keep the previous agreements to define target SNR level as -1dB for REFSENS.
  Option 3: Capture the REFSENS levels by using target SNR level -1dB in this meeting. Interested companies could also bring simulation results in the future meetings based on the aligned simulation assumptions. If the target SNR level based on simulation results is not -1dB, the reference measure channel can be correspondingly revised to satisfy -1dB target SNR level.
  Recommendations for 2nd round:
  Companies to check whether Option 3 can be agreed.

## Slide 6: ΔRIB,c for V2X_20_n38
  ΔRIB,c for V2X_20_n38
  Option 1: Use the HTF to reduce the 3rd harmonic impact into n38. ΔRIB,c is 0.2dB as use shared pain approach.
  Option 2: Keep the ΔRIB,c is TBD in TR.
  Option 3: A note should be placed either saying “No requirements apply for the case that there is at least one individual RE within the uplink transmission bandwidth of the relative higher band and when the frequency range of relative higher band’s uplink channel bandwidth or uplink 1st adjacent channel bandwidth is fully or partially overlapped with the 3 times of the frequency range of the relative lower band’s downlink channel bandwidth. The reference sensitivity is only verified when this is not the case” or a MSD number should be put into the spec to account for sensitivity degradation when 3rd harmonic of B20 falls into the operating band of n38. A trap filter cannot reduce the 3rd harmonic sufficiently to give only 0.2 dB of REFSENS degradation if a 3rd order harmonic from B20 falls inside band n38.
  Recommendations for 2nd round:
  The interference of the specific band combination, e.g. intermodulation in V2X_20_n38, should be further discussed in the 2nd round. It is preferred to derive a value of ΔRIB,c in this meeting.

## Slide 7: Maximum input level
  Maximum input level at n47
  Option 1: Follow the maximum input levels for NR Uu for 64QAM and 256QAM.
  Option 2: -25dBm for 64QAM and -27dBm for 256QAM applicable to all CBWs.
  Recommendations for 2nd round
  Check whether Option 1 (the majority view) can be agreed.
  If not, discuss whether the relaxation on the maximum input level for larger CBWs is needed.

## Slide 8: Reference
[1] R4-2008302, Email discussion summary for [95e][112] 5G_V2X_NRSL_UE_RF_RX, Moderator (CATT), RAN4#95e
[2] R4-2006259, Discussion on remaining issues on Rx RF requirements for NR V2X, CATT, RAN4#95e
[3] R4-2006261, TP on remaining issues on Rx RF requirements for NR V2X, CATT, RAN4#95e
[4] R4-2006262, CR for TS38.101-1, Introduce Rx RF requirements for NR V2X single carrier, CATT, RAN4#95e
[5] R4-2006821, REFSENS issues in V2X, Qualcomm Incorporated, RAN4#95e
[6] R4-2008223, On remaining NR V2X Rx requirements, Huawei, HiSilicon, RAN4#95e
[7] R4-2006746, TP on remaining issues for NR V2X UE, LG Electronics France, RAN4#95e